## Slide 1
Course on Wastewater Treatment Developments
Biological Wastewater Treatment in the Context of Water Quality Management
Helmut Kroiss

## Slide 2: Introduction (1) Human influence on natural water cycle, driven by solar energy
BWWT
We have global and ubiquitous influence

## Slide 3: Introduction (2)
Biological wastewater treatment (BWWT) is a core technology for water quality management worldwide due to important aspects:
Natural microbiomes are applied to protect aquatic ecosystems from organic pollution and eutrophication without adding new pollutants
BWWT is an adaptive and effective technology to avoid the degradation of the variety of species in our surface waters
It is a key technology for recycling treated wastewater for different purposes
BWWT can be made energy self-sufficient using the energy content of the pollution
The microbial processes in a BWWT are complex but have to be understood by all professionals involved as e.g. designers, operators etc. : the training program on BWWTP will markedly contribute to make it happen

## Slide 4: Introduction (3)
Operators and engineers control the environmental conditions in different units of a WWTP to make optimal use of the genetic information stored in the microbial communities developed over millions of years in order to achieve our goals. The process scheme of a WWTP as well as the wastewater composition strongly influence on competition between the microbial communities.
BWWT plants contain technology from at least: civil, mechanical, electrical, electronical and chemical engineering.
They have to meet the legal requirements at any time 24/7/365 (except disasters) which is a special challenge.
Microbes are growing and dying. This results in sludge production even it can be low. Inorganic particles in the influent are removed also producing sludge which needs treatment and disposal.

## Slide 5
Microbial activity starts at the source of wastewater and also continues after BWWT in the effluent as well as in the sludge.
Temperature, the flow regime in the sewer system depending on slope of the pipes, as well as dilution of the pollution from housholds and industry by drinking water or sewer infiltration influence biological treatment processes.
There is a very actual discussion on centralised versus decentralised solutions without sewer systems. They provide not the same services!
Wastewater treatment and recovery of valuable compounds might remain a centralised task mainly due to cost-efficiency considerations.
Introduction (4)

## Slide 6: Introduction (5)
Actual challenges for treatment plant design and operation:
Highly efficient removal of C, N and P compounds from the wastewater by biological treatment.
Removal of micropollutants partly by biological partly by chemical-physical post-treatment processes.
Energy neutrality with the final goal to achieve climate neutrality of WWT.
Recovery of valuable WW compounds (P, N, K, organic C) and heat.
Recycling of treated wastewater for different purposes.
Improved monitoring and data quality management for public information.
Maximise cost efficency of WWT within water quality management.

## Slide 7: Introduction (5)
Complexity of WWT is dramatically increasing which has to result in improved and extended training of experts in WWT, even beyond BWWT.
The flow of information between the experts and the producers of knowledge and experience (universities, professional associations, equipment suppliers) will play an increasing positive role on a local, regional and global scale.
There is no global technological solution. The role of specific local and regional conditions for technology selection will become increasingly dominant.
The loss of knowledge and experience by generational succession might be decreased by the progress in electronic information and communication. The success will depend on the willingness of the coming generations to learn from the past and to develop a better future by innovation.

## Slide 8: Message no.1
Biological wastewater treatment is a core technology for sustainable water management which has a local (settlement), regional (catchment) and political (state) dimension.
1970 no biological treatment
1985 biological treatment in progress

## Slide 9: The effect of BWWT in Austria (high water availability)

## Slide 10: Message no.2
It is not us treating the wastewater, but microorganisms for which we provide favourable environmental conditions to meet our goals.
  Beyond engineering based on scientific cause-effect relationships we have to understand microorganisms in their complex living ecosystem.

## Slide 11: Five laws of applied microbiology in biotechnology
The microorganism is always right, your friend and a sensitive partner.
There are no stupid micro-organisms.
Microorganisms can and will do everything.
Microorganisms are smarter, wiser, more energetic than chemists, engineers and others.
If you take care of your microbial friends they will take care of your future.
D. Perlman, 1980

## Slide 12: Microorganisms do the job
O2
O2
O2
O2
Filamentous
bacteria
Pollution
(dissolved, suspended)
Water
Protozoa
Sludge floc
Free-floating bacteria (flocs)
Attached biomass (biofilm)

## Slide 13
We have to understand microorganisms in their complex living ecosystem

## Slide 14: Message no.3
The complex local situation (at catchment scale and beyond) plays a dominant role for the selection of the best solution of wastewater treatment technology.
  Climate, hydrology, geology, slope, land use, food supply;
  Policy; economic, institutional, and educational development; legislation and enforcement;
  Biological wastewater treatment has to be embedded into regional waster management.

## Slide 15
Local situation:
Vienna (moderate continental climate)
Singapore (tropical marine climate)
Riad (desert, DW from sea, land locked)
Village in Uganda (tropical climate)
Village in Finland (cold climate)
Village at Scottish Atlantic coast
Appropriate solution:
Combined sewers with one central WWTP
Separate sewers with WWTPs and industrial reuse
WWTPs with dominant agricultural reuse)
Lagoons, constructed wetland
Inhouse wastewater treatment
Mechanical treatment with sea outfall
Appropriate solutions for: WW collection, treatment, reuse, sludge disposal, recovery of nutrients etc.

## Slide 16: Message no.4
Only correct and representative data result in successful design, modelling, operation and reporting
  Wastewater flow and pollution.
  Environmental conditions (T, pH, DO, etc.).
  Energy data (aeration, biogas, pumping, etc.).
  In the near future also climate gas emissions.
  As nothing is constant sampling and statistics play a very important role

## Slide 17
A case study from practice:
  A regional WWTP for about 20,000 inhabitants analysed the made a daily flow proportional influent sampling.
  Analytics have been checked and were classified correct .
  It turned out that sampling did not result in a representative sample due to inefficient complete mixing of the large flow proportional sample(~15 l/d) before taking a sample of >100 ml for chemical analysis.
  The pollution load calculation resulted in a 25 to 30% overestimation of the actual load.
How to verify the quality of the data: TP and COD mass balance!

## Slide 18
Total phosphorus TP mass balance (t/d), very simple and reliable for data quality assessment. Additional monitoring requirements pay back!
TPinfluent = TP effluent + TP sludge
COD (energy) balance is more complicated but must also fit!
Influent
Effluent
Sludge

## Slide 19: Message no.5
Never start wastewater treatment without having a reliable waste treatment and disposal solution for screenings, grit and sludge. Disposal is regulated by waste legislation.
  Waste legislation and water legislation have different historic and institutional background.
  Disposal means that responsibility for the solids is not any more with the wastewater treatment plant management.

## Slide 20: You cannot stop production of this odorous and ugly material (sludge).
Disposal has to be reliable and safe, based on a waste disposal permit before WWTP can start.

## Slide 21
This is no solution for
disposal of solids
and sludge!
Threads :
Odour
Hygiene
Climate gas emissions
Groundwater pollution
Slides at landfill
Costs for clean-up
Criminal law
?

## Slide 22: Message no.6
Human aspects are relevant.
  Without well-trained, skilled and dedicated staff a cost effective wastewater treatment cannot be achieved.
  Top down governance and supervising has to be in equilibrium with bottom up initiatives to improve operation.
  Recognition of successful management is at least as relevant as decent salaries for the ‘‘wastewater people“.
  Communication of knowlede, experience and technology need a framework within and beyond the different levels of responsibility.

## Slide 23: Human aspects
truth  lie
right  wrong
correct  false
personal reality
consent on values
proved cause-effect relations
Policy
Sciences
Technology

## Slide 24: Message no.7
Wastewater treatment is a never-ending challenge for the future.
  Future development of the local wastewater situation needs a long perspective (lifetime of the plant‘s hardware) and finally a political decision on design data.
  Risk minimisation by flexible design and operational modes for future requirements is and will remain a challenge.
  There is no way back into any historic situation where humans lived in “harmony with nature”: BWWT will help to find a compromise
  Proper wastewater transport and treatment are basic requirements for human and natural health.