## Slide 1
Course on Wastewater Treatment Developments
Planning and Implementing Flexible and Adaptable Urban Water Management Infrastructure
Glen T. Daigger

## Slide 2: Water and Resource Recovery Facility (WRRF) of the Future Must:
Produce Product Water Which:
  Matches Water Quality Standards of Receiving Water Bodies
  Meets “Fit for Purpose” Water Reuse Standards
    Non-Potable
    Indirect Potable
    Direct Potable
Process Increased Peak Wet Weather Flows
Recover a Wide Varity of Products:
  Energy
  Nutrients
  Organics
  Inorganics
Adapt to Evolving Roles in the Overall System:
  Water and Resource Recovery
  Resource Recovery with “Upstream” Water Recovery

## Slide 3: Understanding the Innovation Process

## Slide 4: Adoption of Innovations is a Social Process: Motives and Incentives for Adoption Change as Different Groups Implement
Nature of ‘Conversations’ Must Change Over Time
  Discuss Features with Innovators
  Discuss Benefits with Others
Disruptive Innovations Often Enter at the ‘Low End’
Rogers, E. M., Diffusion of Innovations, Free Press, NY, 2003.

## Slide 5: The S-Curve of Adoption is Demonstrated to Apply to Water Technologies
Parker, Wat. Envir. Res, 2011.

## Slide 6: New Technologies and Innovations First Find “Replacement” Niche
Stage | Mechanism | Cost | Market Share | Learning Rate
Invention | Random Breakthroughs and Basic Research | High | 0% | -
Innovation | Applied Research, Development, and Demonstration (RD&D) | High | 0% | -
Niche Market | Niche Applications; Replace Existing Use; Learning by Doing, Suppliers and Users Close Relationship | High but Declining | 0-5% | 20-40%
Pervasive Diffusion | Standardization, Mass Production, Economies of Scale, Network Effects | Rapidly Declining | 5-50% | 10-30%
Saturation | Commodity, Intense Competition | Low and Declining | Up to 100 % | 0-5%
Senescence | Few Improvements Possible | Low and Declining | Declining | 0-5%
Grübler, et al., Energy Policy, 27, 1999, 247-280.

## Slide 7: Once Introduced, New Technologies Follow Learning Curve
Grübler, et al., Energy Policy, 27, 1999, 247-280.

## Slide 8: Technologies Compete While They Evolve
Grübler, et al., Energy Policy, 27, 1999, 247-280.

## Slide 9: “Building Block” is Traditional Approach to Adapt to Varying Needs Over Time

## Slide 10: Example WRRF Layout Illustrating the Building Block Approach
Phase 1
Phase 2
Phase 3
Phase 4
Admin
O&M
Tertiary
Treatment
Primary
Treatment
Bioreactors
Primary
Treatment
Clarifiers
Biological
Treatment
Upgrade
Biological
Treatment
Upgrade
Head
works
Solids
Processing
Solids Processing
Service Entrances
Public Entrances

## Slide 11: Layout Facility for Anticipated Capacity Expansions
Phase 1
Phase 2
Phase 3
Phase 4
Admin
O&M
Tertiary
Treatment
Primary
Treatment
Bioreactors
Primary
Treatment
Clarifiers
Biological
Treatment
Upgrade
Biological
Treatment
Upgrade
Head
works
Solids
Processing
Solids Processing
Service Entrances
Public Entrances

## Slide 12: Layout Facility for Treatment Upgrade
Phase 1
Phase 2
Phase 3
Phase 4
Admin
O&M
Tertiary
Treatment
Primary
Treatment
Bioreactors
Primary
Treatment
Clarifiers
Biological
Treatment
Upgrade
Biological
Treatment
Upgrade
Head
works
Solids
Processing
Solids Processing
Service Entrances
Public Entrances

## Slide 13: Solids Processing Can be Expanded and Upgraded When Sufficient Space Allocated
Phase 1
Phase 2
Phase 3
Phase 4
Admin
O&M
Tertiary
Treatment
Primary
Treatment
Bioreactors
Primary
Treatment
Clarifiers
Biological
Treatment
Upgrade
Biological
Treatment
Upgrade
Head
works
Solids
Processing
Solids Processing
Service Entrances
Public Entrances

## Slide 14: Space Allocation for Tertiary Treatment Mitigates Solids and Headworks Off-Site Impacts
Phase 1
Phase 2
Phase 3
Phase 4
Admin
O&M
Tertiary
Treatment
Primary
Treatment
Bioreactors
Primary
Treatment
Clarifiers
Biological
Treatment
Upgrade
Biological
Treatment
Upgrade
Head
works
Solids
Processing
Solids Processing
Service Entrances
Public Entrances

## Slide 15: Separate Entrances Separate Operational and Public Functions
Phase 1
Phase 2
Phase 3
Phase 4
Admin
O&M
Tertiary
Treatment
Primary
Treatment
Bioreactors
Primary
Treatment
Clarifiers
Biological
Treatment
Upgrade
Biological
Treatment
Upgrade
Head
works
Solids
Processing
Solids Processing
Service Entrances
Public Entrances

## Slide 16: Adapting Practices to Current Needs

## Slide 17: Useful Life of Facility Components Indicates Replacement Priorities
Item | Useful Life (Years) | Comments
Structures | 50-100 | Lifetime of Concrete Structures (Including Rehab)
Mechanical Equipment | 15-40 | Rotating Equipment
Electrical Equipment | 10-20 | Determined by Obsolescence
Treatment Technology | 10-20 | Determined by Effluent Standards and Evolution of Technology
I&C Technology | 5-15 | Determined by Obsolescence
Daigger, Wat. Sci. & Tech., 2011

## Slide 18: Rapid Technological Change Means a New Paradigm – Design for Retrofit

## Slide 19: “Legacy Systems” Can be Successfully Dealt With
Centralized Systems Serve Existing Development
Distributed Elements Aggressively Incorporated Into New Developments and Redevelopment
  Allows System to be Converted Over Time
Existing Water Distribution and Wastewater Collection System Provides Necessary Capacity as Urban Density Increases
  Avoids Need for System Expansion
  May be “Downsized” Over Time and “Re-Purposed”
Centralized Plant Transitions From “Wastewater” to “Organic Matter” Processing Facility

## Slide 20: Managing (Not Taking) Risks is Key to Successful Innovation
Item | Description | Probability | Impact | Mitigation | Cost
1. | xxxxx | xx % | xxxxx | xxxxx | $xx
2. | xxxxx | xx % | xxxxx | xxxxx | $xx
3. | xxxxx | xx % | xxxxx | xxxxx: | $xx
Risk/Opportunity Analysis.
Fatal Flaws? Risks That Cannot be Mitigated.
Compare Option Mid-Points.
Implementation Plan Mitigates Risks, Seizes Opportunities.
Probability
50 %tile
PW ($)
Developed
Developing

## Slide 21: Water Service Provision Must Meet Multiple Criteria
Environmental | Social | Economic
Meets Environmental Standards: Water Air Soil | Service Coverage and Reliability: Water Sanitation/Wastewater Flooding | Sustainable Service Provision: Organizational Stability Reliable Water Management Asset Renewal Sustainable Funding
Resource Consumption | Level of Service: Non-Discrimination and Equity Transparency Affordability Participation | Contribution to Economic Development: Readily Expandable
Ecosystem Restoration | Enhance Public Health and Wellbeing | 
Minimize Toxics | Broader Public and Social Benefits | 

## Slide 22: Concepts of Uncertainty, Learning, and Flexibility Can be Incorporated into Planning
Uncertainty | Learning | Approach | Outcome
Low | Little to None Needed | Project Future and Develop Plan | Static Plan with Fixed Implementation “Triggers”
Medium to High | Little to None Needed | Scenario Planning | “No Regrets” Steps, Followed by Alternate Paths
Medium to High | Significant Opportunity | Real Options Analysis | “No Regrets” Steps, Followed by Adaptive Options

## Slide 23: Resulting in a Learning-Based and Adaptive Planning and Implementation Process
Malekpour, de Haan & Brown, 2016
Explore a portfolio of future possibilities
Deep uncertainties
Resolvable uncertainties
An optimal plan
A robust plan
Forecasting
Predict future conditions
Exploring
Valuation criteria: Limited
Valuation criteria: Multiple
Planning approach: Incremental, reactive
Planning approach: Visionary, proactive