## Slide 1
Course on Wastewater Treatment Developments
Biological Wastewater Treatment as a Technological System
Mino Takashi

## Slide 2: My research career
Biochemical/micro-ecological mechanism of “Enhanced Biological Phosphate Removal (EBPR)”
Modeling of Activated Sludge Process: “IWA Activated Sludge Models (ASM) No.1, 2 and 3”
Founding Coordinator of “Graduate Program in Sustainability Science (GPSS)” at The University of Tokyo

## Slide 3: Acinetobacter story (1)
Biological phosphate removal process (anaerobic-oxic process)
tank tank Settler
Influent Effluent
Return sludge
Introduction of an anaerobic zone at the front end of activated sludge aeration tanks promotes enhanced phosphate removal.
Phosphate Accumulating Organisms (PAOs) responsible for EBPR.
Anaerobic Oxic (aeration)
Excess (waste)
sludge

## Slide 4: Acinetobacter story (2)
Who win and why?
Acinetobacter:
  Based on the culture-based method, Acinetobacter was found to occupy a major portion (60-90%) of bacterial populations in the activated sludge process with high P removal efficiency.
Acumulibacter/more diverse microbial community:
  It was shown based on molecular methods that Acinetobacter was no more the primary species responsible for EBPR, but Accumulibacter and other diverse species contributed to EBPR.
Microscopic images
FISH images
( EUB probe) ( PAOmix probe)
(yellow: Poly-P staining)
(Photos by Fukushima T., Mino Laboratory)

## Slide 5: Acinetobacter story (3)
Acinetobacter was no.1 among the bacterial community that developed on the agar plates, but never the major population in the entire bacterial community.
By analyzing DNA sequences, you can identify more comprehensive bacterial populations, but still some technical biases must exist.

## Slide 6: A lesson learned from the Acinetobacter story
You should not look at only what you are interested in, but you should try to understand which parts/components/aspects of the entire system you are observing by the method you are applying.
(Unknown source, commonly available on the web.)

## Slide 7: Biological wastewater treatment
A part of primary urban infrastructure
Many physical, economic & social constraints exist in design & operation
Located at the downstream of urban system
Essential for comfortable life, but less visible, annoying & producing little valuable matters
An “open” ecosystem
Exposed to severe environmental selective pressures that facilitate serious biological competitions
A technology system controlled by engineer
Limited controllable parameters vs uncontrollable influent characteristics

## Slide 8: What frames/views can you apply to BWT?
Historical view.
BWT seen as material flows.
Are you looking at the removal of only organic matters, nitrogen and phosphorus in BWT?
What do wastewaters carry other than physical matters?
BWT and society.
What else?

## Slide 9: 1. Historical view

## Slide 10
2. BWT seen as material flows

## Slide 11
Reflection of Human Life
  Materials excreted from human body and used in our life can be transported in domestic wastewaters and are converged to WWTP.
Chemicals, toxins, harmful materials
  Heavy metals
  Antibiotics, endocrine Disrupters
  Micro-plastics
  Radioactivity
Pathogenic microorganisms and Viruses
  Gastroenteritis-causing viruses (norovirus, adenovirus, rotavirus, etc.)
  COVID-19 virus
Any useful materials?
  Wastewaters could contain many possibly useful minerals and micro-substances.
3. Are you looking at the removal of only COD, N and P in BWT?

## Slide 12
Energy
Heat
Information
What else?
4. What do wastewaters carry other than physical
matters?

## Slide 13
5. BWWT and society
Urban Functions
  Wastewater => Reuse as water resource
  Space in urban area => Recreation park
  Integrated into other urban infrastructures
Emergency evacuation from fires/earthquakes, etc.
  Space in urban area => Evacuation space/food storage
  BWT facilities => Emergency toilet
  Wastewater => Emergency fire protection water
Modern technologies
  Modeling + AI => Virtual WWTP
  Nanotech + Material Science => New Membranes
  Biotech + Engineering => New Reactors

## Slide 14: Final messages
Do not stay in the traditional field of wastewater treatment technologies, but look out for possible various interfaces with other social functions.
Intentional changes of frames through which you watch wastewater treatment facilities may bring you new insights that might give you fantastic ideas for future innovation.
Be flexible in thinking, and brave enough for changes.
Mino Takashi
Professor Emeritus, The University of Tokyo