## Slide 1
Course on Wastewater Treatment Development
Wastewater Treatment Innovation
A University Perspective
Mark C.M. van Loosdrecht

## Slide 2
Technologies coming from
our group at TU Delft
Scale-up to full-scale:
BCFS
Sharon
Anammox/Canon
Nereda
Alkaline gas treatment
PHA production
Kaumera
Vivianite P-recovery
Several processes development stopped

## Slide 3: Definition of innovation
Invention: An idea made manifest
Innovation: Idea applied successfully in practice
Schumpeter 1934
e.g. external versus submerged membranes
Dorr-Oliver 1967, Yamamoto et al. 1989
There should be a strong benefit to an invention in order to become an innovation.
Notes: Innovation is not a new word but still often misused in the wrong context. I prefer the original definition by Schumpeter, stating that an invention is an idea made manifest while innovation is an idea successful applied in practise. For example the invention of membranes became for the water technology an innovation when prof. Yamamoto decided to put the membranes inside the aeration tank. Or in other words there should be a strong benefit to an invention in order to become an innovation.

## Slide 4: Drivers for innovation
Scientific question/curiosity Why ...?
Technological challenge How can I …?
Market demand Can you …?
The combination of the above leads to innovation
Siberia/Mongolia
Canada
Notes: How can we achieve innovation? In my view a combination of three factors are essential: A scientific question based on curiosity, A technological challenge and finally a market demand. As example the curiosity on life in mongolian soda lakes contributed to the development by Paques and Shell of a biological gas desulphurisation plant applied at the gas fields in Canada.

## Slide 5: Innovation
Curiosity
Knowledge
Problem
Potential for innovation

## Slide 6
Role of biopolymers in microbial Ecology (BCFS, Nereda, PHA production)
“N-Gap” in wastewater treatment plant (Anammox)
Morphology formation in biofilms (Nereda, Kaumera)
Alkaline microbiology (H2S conversion)
Iron behavior in treatment (Vivianite)
Curiosity-driven innovation

## Slide 7: Innovation in water treatment
Focus points:
Compactness
Nutrient removal optimisation
Energy minimisation
Cost reduction
System integration
Not or less:
Energy generation
Nutrient recovery
Decentralisation

## Slide 8: Linear innovation model

## Slide 9: Cyclic innovation model (CIM)
A.J. Berkhout

## Slide 10: System error (I)
Gap between scientific knowledge and business needs
e.g. energy and resource recovery, decentralized systems, FO, MFC, etc.

## Slide 11
Many projects, but:
No real advantage
No breakthrough
Need: System advantage & good problem definition
Example: Pharmafilter
Example: Decentralized treatment – no market

## Slide 12: System error (II)
Gap between technological capabilities and social needs
e.g. membrane bioreactor for large WWTPs.

## Slide 13
Example: MBR technology
push without a market pull
Market development and prediction (2011 report):
Higher cost, more energy/chemicals
Only slightly better effluent compared to media filtration
2017: Latest news on MBR on WaterForum Online: 30 oktober 2008

## Slide 14
http://www.thembrsite.com/interactive-map-history-of-the-largest-municipal-mbr-installations/
New MBR plants

## Slide 15
Example: Anammox®
Notes: As example in the anammox development TU Delft STOWA, Paques and a Water board closely cooperated in a successful reactor development

## Slide 16: Development Anammox
60 to 80’s – regular reports of “unexpected nitrogen loss” usually interpreted as nitrogen removal by nitrifyers or aerobic deammonification
80’s: Pilot at Gist-brocades in Delft with “unexpected nitrogen loss”
Arnold Mulder/Gijs Kuenen: What is happening?
90-ies: Recognition of Anammox bacteria made Anammox processes possible to design and reliable operate
CURIOSITY!
INNOVATION!
Notes: If we look back at the development of the anammox technology we see that likely in the 60-80-ies regularly pilot or lab reactors existed with anammox without being recognized; it was just denoted as Nitrifier denitrification or aerobic deammonification. It was the scientific curiosity of prof Kuenen and Arnold Mulder who investigated the unexpected nitrogen loss which led to the discovery of anammox. Once the anammox microbiology was clearly recognized a process development could start which led to the innovative anammox process as we know it today.

## Slide 17: Granules and Anammox® reactor in China
Volume: 6,700 m3
Load: 1.7 kgN/m3.d
Startup time: 1 month (95% conversion)

## Slide 18: Mainstream: Need for Plug Flow
In Biofilm/Granular systems a certain degree of plug flow needed to outcompete NOB
ANAMMOX®
ANAMMOX®
Side stream
Main stream

## Slide 19
Example: Nereda®
Notes: As a second example in the recently developed Aerobic granular sludge technology TU Delft STOWA, DHV and several Waterboards closely cooperated

## Slide 20: Aerobic Granular Sludge
Original innovation:
Circox Reactor - compactness
Scientific questions:
Why does a certain biofilm morphology arise?
Why do bacteria form smooth granules?
→ Slow growth rate
Technological challenge:
How can we design a system selecting for slow growing bacteria?
Market questions:
Can you do this at very low investment costs?
Can full nutrient removal be implemented?

## Slide 21: Nereda® WWTP Epe First full-scale aerobic granular sludge plant
Granular sludge-based
30 % less capital costs, 25% energy saving, 70% less space
Notes: For application in the main stream we developed with DHV recently the Nereda Technology, where you see here the first full scale reactor. This concept based on traditional microbiology save 30 % in investment costs, 25 % in energy and needs 70 % less space.

## Slide 22: New process based on granular sludge - Nereda®
Better understanding of morphogenesis of microbial systems resulted in compact wastewater treatment process.
75% reduction in area
20-35% reduction in energy
20% reduction in costs
Introduced: 2012, now 100+ plants in operation
https://nereda.royalhaskoningdhv.com/
Notes: Innovation is not a new word but still often misused in the wrong context. I prefer the original definition by Schumpeter, stating that an invention is an idea made manifest while innovation is an idea successful applied in practise. For example the invention of membranes became for the water technology an innovation when prof. Yamamoto decided to put the membranes inside the aeration tank. Or in other words there should be a strong benefit to an invention in order to become an innovation.

## Slide 23: Largest Nereda®: Ringsend WWTP
Full plant upgrade
2,400,000 P.E.
159 MGD

## Slide 24: Aerobic Granular Sludge - Nereda® - Development
Mid ’90’s Research by Delft University of Technology (TUD)
2000 close co-operation TUD/DHV
2002 Stable granulation, extensive N- en P-removal in TUD lab
2002 Feasibility study showed great potential
2003 – 2005 Large pilot-research at Ede WWTP
2005 Start-up industrial launching customer
2006 Industrial units start Municipal National Nereda Research
2006 / 2008 Design/construction municipal demo units
2012 first Dutch full scale municipal plant
1998 Stable granulation in lab

## Slide 25: Success factors
Simple technology
Waterboard system
Patented system
National research program
10 years commitment
Realize only at end we formed a PPP
Enthusiasm and energy of one leader
Helle van der Roest

## Slide 26
“Loosing child factor”
Focus on publications/citations
Keep a system as long as possible ‘promising’
Potential fail factors

## Slide 27: Waterboard system as success factor
Have only one task
Many waterboards
Benchmarking
Common research by STOWA

## Slide 28
Scale
down
Optimisation
Dependence on pH,
Temperature, etc.
Simulation
Kinetics;
Insight in Process
Laboratory
Pilot
Testing/
Optimisation
Scale up
Application
Scale up
up
Designing
Costs & Processing
Production
Scale
From lab-scale to full-scale

## Slide 29
Nereda® process development
PhD’s @TUDelft
Cristian Picioreanu
Biofilm morphology
1996-1999
Antonio Martins
Activated sludge
morphology
1999-2003
Janneke Buen
Principle granulation
1996-2000
Mario Pronk
Process Engineering
2002-(2010-2016)- ……
Mari Winkler
Microbiology AGS
2008-2012
Merle de Kreuk
Scale-up AGS
2000-(2005)-2009

## Slide 30: Patents
Method for acquiring grain-shaped growth of a microorganism in a reactor
Patent number: 6566119
Type: Grant
Filed: October 14, 1999
Date of Patent: May 20, 2003
Assignee: Technische Universiteit Delft
Inventors: Joseph Johannes Heijnen, Marinus Cornelis Maria Van Loosdrecht
Method for the treatment of waste water with sludge granules
Publication number: 20060032815
Type: Application
Filed: September 16, 2003
Publication date: February 16, 2006
Applicants: Technische Universiteit Delft, Stichting voor de Technische
Inventors: Marinus Cornelis Maria Van Loosdrecht, Merle de Kreuk

## Slide 31
Transferred to RHDHV for use in wastewater treatment in 2012
Royalties since 2014 term finishes in 2026
Without patent:
No commitment of direction DHV for 10 year program
+ New patents on ALE and products from ALE
More complicated……
Patents

## Slide 32: As long as you do not recognise a resource it is not available
New invention?

## Slide 33: But what makes the granular sludge
A biopolymer with strong gelling properties
Potential to produce a biopolymer at a scale at least 100 times larger that current production volumes from wastewater
Can be used to produce novel materials with novel functionalities
Notes: Innovation is not a new word but still often misused in the wrong context. I prefer the original definition by Schumpeter, stating that an invention is an idea made manifest while innovation is an idea successful applied in practise. For example the invention of membranes became for the water technology an innovation when prof. Yamamoto decided to put the membranes inside the aeration tank. Or in other words there should be a strong benefit to an invention in order to become an innovation.

## Slide 34: Novel materials
How it looks in nature!
NACRE
What we get!
State of the art engineering polymers
Heat-resistant, fire-proof
High tensile strength
Structural coloration
Notes: Innovation is not a new word but still often misused in the wrong context. I prefer the original definition by Schumpeter, stating that an invention is an idea made manifest while innovation is an idea successful applied in practise. For example the invention of membranes became for the water technology an innovation when prof. Yamamoto decided to put the membranes inside the aeration tank. Or in other words there should be a strong benefit to an invention in order to become an innovation.

## Slide 35
Wastewater
Kaumera recovery
Kaumera-based materials
Market
TU Delft: Environmental Biotechnology, Biotechnology and Society, Advanced Soft Matter, Circular product design
Public authorities
Companies
Value chain development

## Slide 36
Kaumera production
Zutphen 500 ton/year

## Slide 37
Additional sludge reduction with 20 to 35%
Hydrolysis of sludge - Methanation
Positive earning model Kaumera recovery
  Cost price extraction is 0.5 to 0.8 € per kg
  Market price for alginate is 1.0 to 3.5 € per kg
Resource recovery from wastewater
Contribution towards circular economy
Why recover Kaumera®?
Notes: The reason why we and our PPP partners invest in the ALE recovery development are that:
ALE extraction not only contributes towards a circular economy with high0-end resource recovery from waste that is very much the future target for most European governments. Also it shows very interesting economics.
It reduces the sludge disposal costs as after ALE extraction dewaering of the sludge can be achieved with no or minimal amount of polymer, while overall volume of sludge to dispose of is reduced by 20 to up to 35%. As sludge disposal is quite expensive in Europe, these saving alone are already interesting to consider ALE recovery. But the high value of ALE against the extraction costs are certainly an even improtant driover.
Based on the current offerings we conservatively calculate with gate fee of 1 to 3.5 EUR per kg ALE, while the costs to extract it is in the range of 0.5 to 0.8 EUR.

## Slide 38: Conclusions
Important for innovation
Partnering - leadership
Curiosity-driven research
Good problem definition

## Slide 39: Conclusions
Important for innovation
Partnering - Leadership
Curiosity driven research
Good problem definition