## Slide 1
Course on Aerobic Granular Sludge
Process Operation
and Control
Eveline I. P. Volcke
Notes: Hello everybody, my name is Eveline Volcke and I am a professor at Ghent University.
Let’s talk about the process operation and control
of aerobic granular sludge reactors.
(NEXT SLIDE)
https://studybwwt.online/

## Slide 2
outline
Aerobic granular sludge (reactors)
Sections 11.3, 11.4 and extra’s
Notes: We will start with an introduction on aerobic granular sludge and aerobic granular sludge reactors,
(NEXT SLIDE)

## Slide 3
outline
Aerobic granular sludge (reactors)
Granule growth by avoiding diffusion limitation
Sections 11.3, 11.4 and extra’s
Notes: we will see that avoiding diffusion limitation is the prerequisite for growing granules.
(NEXT SLIDE)

## Slide 4
outline
Aerobic granular sludge (reactors)
Granule growth by avoiding diffusion limitation
Batch-wise reactor operation
Sections 11.3, 11.4 and extra’s
Notes: We will study the batch-wise reactor operation and
the corresponding concentration profiles,
in the lab as well as in for full-scale plants
(NEXT SLIDE)

## Slide 5
outline
Aerobic granular sludge (reactors)
Granule growth by avoiding diffusion limitation
Batch-wise reactor operation
Sequencing batch process control
Sections 11.3, 11.4 and extra’s
Notes: Then we will discuss some specific process control aspects associated with the batch-wise operation,
(NEXT SLIDE)

## Slide 6
outline
Aerobic granular sludge (reactors)
Granule growth by avoiding diffusion limitation
Batch-wise reactor operation
Sequencing batch process control
Additional granule selection pressures
Sections 11.3, 11.4 and extra’s
Notes: and we will end with some additional selection pressures which can be applied to obtain granular sludge
(NEXT SLIDE)

## Slide 7: aerobic granular sludge aerobic granular sludge reactors
Notes: Let’s start by having a look on what is aerobic granular sludge
and what are aerobic granular sludge reactors
(NEXT SLIDE)

## Slide 8: aerobic granular sludge - definition
‘Aggregates of microbial origin, which do not coagulate
under reduced hydrodynamic shear
and which settle significantly faster than activated sludge flocs’
Notes: Aerobic granular sludge is defined as
aggregates of microbial origin, which do not coagulate
under reduced hydrodynamic shear
and which settle significantly faster than activated sludge flocs’
(NEXT SLIDE)

## Slide 9: aerobic granular sludge - definition
‘Aggregates of microbial origin, which do not coagulate
under reduced hydrodynamic shear
and which settle significantly faster than activated sludge flocs’
Diameter > 0.2 mm
Notes: Typically, aerobic granules are larger than .2 mm
However, the fact that the granules do not coagulate
is more important than the size criterion.
(NEXT SLIDE)

## Slide 10: aerobic granular sludge - definition
‘Aggregates of microbial origin, which do not coagulate
under reduced hydrodynamic shear
and which settle significantly faster than activated sludge flocs’
Diameter > 0.2 mm
SVI5 SVI30
Notes: The sludge volume index or SVI is
the volume occupied by 1 gram of sludge after settling for a certain time.
For aerobic granules, the volume taken up after 5 minutes of settling is already about the same as the volume taken up after 30 minutes of settling.
So the SVI_5 is the same as the SVI_30.
This is a scientific way of expressing that the granules settle very fast.
(NEXT SLIDE)

## Slide 11: aerobic granular sludge - definition
‘Aggregates of microbial origin, which do not coagulate
under reduced hydrodynamic shear
and which settle significantly faster than activated sludge flocs’
Diameter > 0.2 mm
SVI5 SVI30
No compression of settled sludge
Notes: Another important feature of aerobic granular sludge is that there is no compression of the settled sludge,
unlike for activated sludge.
(NEXT SLIDE)

## Slide 12: aerobic granular sludge reactor
Notes: O.K., so we know what is aerobic granular sludge.
Let’s see what is an aerobic granular sludge reactor
and how it relates to a conventional wastewater treatment plant.
(NEXT SLIDE)

## Slide 13
Removal of C, N, P,
in different reactor compartments
Conventional WWTP
Anaerobic
Anoxic
Aerobic
Settling
Notes: In a conventional WWTP, the removal of carbon, nitrogen and phosphorus components takes place in different reactor compartments.
These compartments take up a lot of space.
Besides, wastewater needs to be pumped around between these compartments,
which brings along pumping costs.
(NEXT SLIDE)

## Slide 14
Removal of C, N, P,
in different reactor compartments
Bacteria grow in flocs
 slow separation from purified effluent
Conventional WWTP
Anaerobic
Anoxic
Aerobic
Settling
Biological Wastewater Treatment
Online Course Series
Notes: Another problem in conventional wastewater treatment is that the bacteria which purify the water, grow in flocs.
The density of these flocs is only slightly higher than the one of wastewater,
which makes that their separation proceeds very slowly and requires large settling tanks.
(NEXT SLIDE)

## Slide 15
Removal of C, N, P,
in different reactor compartments
Bacteria grow in flocs
 slow separation from purified effluent
Conventional WWTP
Anaerobic
Anoxic
Aerobic
Settling
Notes: This picture shows water with sludge flocs after 5 minutes of settling time.
(NEXT SLIDE)

## Slide 16
Removal of C, N, P,
in different reactor compartments
Bacteria grow in flocs
 slow separation from purified effluent
Conventional WWTP
Anaerobic
Anoxic
Aerobic
Settling
aerobic granular sludge
Bacteria grow in granules
Notes: In the case of aerobic granular sludge, the bacteria grow in granules
(NEXT SLIDE)

## Slide 17
Removal of C, N, P,
in different reactor compartments
Bacteria grow in flocs
Removal of C, N, P,
in different zones of a single granule
 slow separation from purified effluent
Conventional WWTP
Anaerobic
Anoxic
Aerobic
Settling
aerobic granular sludge
Bacteria grow in granules
Notes: The removal of carbon, nitrogen and phosphorus components
takes place in different zones of a single granule
so there is no need to pump around the wastewater between different compartments.
(NEXT SLIDE)

## Slide 18
Removal of C, N, P,
in different reactor compartments
Bacteria grow in flocs
Removal of C, N, P,
in different zones of a single granule
 slow separation from purified effluent
Conventional WWTP
Anaerobic
Anoxic
Aerobic
Settling
aerobic granular sludge
Bacteria grow in granules
Notes: The granules are closely packed in the reactor,
which results in a most compact installation
(NEXT SLIDE)

## Slide 19
Removal of C, N, P,
in different reactor compartments
Bacteria grow in flocs
Removal of C, N, P,
in different zones of a single granule
Bacteria grow in granules
 slow separation from purified effluent
Conventional WWTP
Anaerobic
Anoxic
Aerobic
Settling
aerobic granular sludge
 fast separation from purified effluent
Notes: The granules settle very welll
which makes that they can easily be separated from the purified effluent.
This is done in the reactor itself
so there is no need for settling tanks
which makes the installation even more compact.
(NEXT SLIDE)

## Slide 20
Removal of C, N, P,
in different zones of a single granule
Bacteria grow in granules
 fast separation from purified effluent
aerobic granular sludge reactors
 Compact installations
75% less space
 Up to 50% less energy use
 30% less investment costs
Biological Wastewater Treatment
Online Course Series
Notes: Overall, aerobic granular sludge reactors take up 75% less space than activated sludge plants.
The consume up to 50% less energy
and require 30% less investment costs.
(NEXT SLIDE)

## Slide 21: granule growth by avoiding diffusion limitation
Notes: But how to grow granules?
(NEXT SLIDE)

## Slide 22: How to grow granules?
Make sure that diffusion is not limiting!
Notes: Well, as was already made clear to you in the lecture of Mark van Loosdrecht,
the most important prerequisite is to make sure that diffusion is not limiting.
(NEXT SLIDE)

## Slide 23: Effect of diffusion
Bulking sludge
Flocculated sludge
Granular sludge
Notes: Indeed, if we look at how bacteria organize themselves…
(NEXT SLIDE)

## Slide 24: Effect of diffusion
Bulking sludge
DIFFUSION LIMITED
Low substrate concentration or high growth rate
Substrate limitation
Notes: … we see that in case of diffusion limitation, bulking sludge is obtained.
This is the case when the substrate concentration is low
or the biomass growth rate is high.
The substrate is limiting,
and the bacteria reach out in all directions to get food,
resulting in filamentous structures.
(NEXT SLIDE)

## Slide 25: Effect of diffusion
NON-DIFFUSION LIMITED
High substrate concentration or low growth rate
Growth limitation
Granular sludge
Notes: At the other side of the spectrum, there is granular sludge.
which is obtained when there is not diffusion limitation.
This is when the substrate concentration is high
or the biomass growth rate is low.
The substrate is not limiting,
but bacterial growth as such is the limiting factor.
This results in the growth of bacteria in the form of dense granules.
(NEXT SLIDE)

## Slide 26: Effect of diffusion
Bulking sludge
Flocculated sludge
Granular sludge
DIFFUSION LIMITED
Low substrate concentration or high growth rate
Substrate limitation
NON-DIFFUSION LIMITED
High substrate concentration or low growth rate
Growth limitation
Notes: And in between bulking sludge and granular sludge,
there is flocculated sludge
as is present in typical activated sludge wastewater treatment plants.
(NEXT SLIDE)

## Slide 27: How to grow granules?
Make sure that diffusion is not limiting!
 high substrate concentration
AND/OR low growth rate
Notes: O.K., so now we know that diffusion should not be limiting,
which means that the substrate concentration should be relatively high
or the growth rate should be relatively low
(NEXT SLIDE)

## Slide 28: How to grow granules?
Make sure that diffusion is not limiting!
Relatively easy for slow-growing micro-organisms
e.g. anaerobic granular sludge (UASB reactors)
 high substrate concentration
AND/OR low growth rate
Notes: This is relatively easy for slow-growing micro-organisms.
which is the case for micro-organisms involved in anaerobic digestion.
In that case one can grow even granules for high concentrations of soluble substrate
as is done in a UASB reactor
(NEXT SLIDE)

## Slide 29: How to grow granules?
Make sure that diffusion is not limiting!
Relatively easy for slow-growing micro-organisms
e.g. anaerobic granular sludge (UASB reactors)
But how to do so for fast-growing micro-organisms?
e.g. heterotrophic bacteria – organic carbon removal
 high substrate concentration
AND/OR low growth rate
Notes: So how can we possibly grow granules of heterotrophic bacteria, which convert organic carbon?
(NEXT SLIDE)

## Slide 30: How to grow granules?
Make sure that diffusion is not limiting!
Relatively easy for slow-growing micro-organisms
e.g. anaerobic granular sludge (UASB reactors)
But how to do so for fast-growing micro-organisms?
e.g. heterotrophic bacteria – organic carbon removal
 minimize substrate limitation
i.e., minimize limitation of organic carbon and oxygen
 high substrate concentration
AND/OR low growth rate
Notes: The trick is to minimize substrate limitation
which in this case means to minimize the limitation of organic carbon.
Also oxygen should not be limiting.
(NEXT SLIDE)

## Slide 31: Minimizing substrate LIMITATION
Notes: So now we know what to do,
we need to minimize substrate limitation for heterotrophic bacteria.
But how is this done in an aerobic granular sludge reactor?
(NEXT SLIDE)

## Slide 32: Minimizing substrate LIMITATION
Introducing anaerobic feeding phase
(‘feast’ phase)
No aerobic (fast) growth
BOD uptake by PAO/GAO
Production storage polymers
Notes: Well, the trick is to have an anaerobic feeding phase.
Given that the feeding phase is anaerobic,
there will not be any aerobic growth of heterotrophic bacteria,
which we know takes place fast
The biodegradable organic carbon or BOD will be taken up by PAO and GAO
phosphorus accumulating organisms and glycogen-accumulating organisms –
which will use it to produce storage polymers.
(NEXT SLIDE)

## Slide 33: Minimizing substrate LIMITATION
Introducing anaerobic feeding phase (‘feast’ phase)
No aerobic (fast) growth
BOD uptake by PAO/GAO
Production storage polymers
Aerobic (‘famine’) phase
No carbon left for other bacteria
Growth on intracellular storage polymers
Slow growth
Notes: Next comes an aerobic phase.
This is a famine phase, given that there is no carbon left for other bacteria than the PAO and GAO.
So the PAO and GAO grow on intracellular sotrage polymers, which is a slow growth,
which is not diffusion-limited.

## Slide 34: How to grow granules?
Make sure that diffusion is not limiting!
 Separation of substrate uptake and biomass growth
Notes: So in summary
aerobic granules are grown by making sure that diffusion is not limiting.
This is done by separating substrate uptake and biomass growth
by having a separate, anaerobic feeding phase
(NEXT SLIDE)

## Slide 35: How to grow granules?
Make sure that diffusion is not limiting!
Bacteria growing on internal storage polymers are slow growers
Anaerobic feeding phase selects slow-growing organisms
 dense, stable and smooth granules!
 Separation of substrate uptake and biomass growth
Notes: The bacteria growing on internal storage polymers are slow growers
and the anaerobic feeding phase selects for these slow-growing organisms
which results in the formation of dense, stable and smooth granules.
(NEXT SLIDE)

## Slide 36: batch-wise reactor operation
Notes: Let’s now zoom into the batch-wise reactor operation.
(NEXT SLIDE)

## Slide 37: Batch-wise operation
Operated in sequencing batch mode
Notes: Aerobic granular sludge reactors are operated in sequencing batch mode
(NEXT SLIDE)

## Slide 38: Batch-wise operation – laB
Notes: In the lab, it looks like this
(NEXT SLIDE)

## Slide 39: Batch-wise operation – laB
Influent
Anaerobic feeding – 1 hour
Notes: we start with an 1hour feed through the settled granular sludge bed.
Like this the biomass sees a high substrate concentration.
(NEXT SLIDE)

## Slide 40: Batch-wise operation – laB
Influent
Substrate uptake (organic carbon)
PHA storage
Aerobic growth
Phosphate release
Anaerobic feeding – 1 hour
Notes: The organic carbon substrate is converted into PHA.
Since there is no aeration,
There will be no aerobic growth.
At the same time PAOs are releasing phosphate.
(NEXT SLIDE)

## Slide 41: concentration profiles – laB
PO43-
Anaerobic feeding
Notes: And here are the corresponding concentration profiles
(NEXT SLIDE)

## Slide 42: concentration profiles – laB
PO43-
NH4+
Anaerobic feeding
Ammonium accumulation
Notes: Ammonium accumulates as it is fed and not converted.
(NEXT SLIDE)

## Slide 43: concentration profiles – laB
PO43-
NH4+
Anaerobic feeding
Ammonium accumulation
Quick organic carbon consumption
Phosphate release
Notes: Organic carbon is rapidly consumed and converted into storage compounds.
At the same time, phosphate is released.
(NEXT SLIDE)

## Slide 44: concentration profiles – laB
PO43-
NH4+
NO3-
Anaerobic feeding
Ammonium accumulation
Quick organic carbon consumption
Phosphate release
Nitrate consumption
Notes: And some nitrate which is left over from the previous cycle, is converted.
(NEXT SLIDE)

## Slide 45: Batch-wise operation – laB
Air
Aeration/reaction – 2 hours
Notes: Once the reactor has been filled with influent
the 2 hour aeration phase starts.
Now oxygen is available for the aerobic microorganisms to grow.
(NEXT SLIDE)

## Slide 46: Batch-wise operation – laB
Air
Aeration/reaction – 2 hours
Growth on storage polymers (PHA)
Notes: Given that there is little to no substrate left in the liquid
only those bacteria that have stored the substrate as storage polymers can grow.
(NEXT SLIDE)

## Slide 47: Batch-wise operation – laB
Air
Aeration/reaction – 2 hours
Growth on storage polymers (PHA)
Nitrification (outside)
Notes: Ammonium will be nitrified to nitrite and nitrate, by nitrifiers which are present at the outside of the granule.
(NEXT SLIDE)

## Slide 48: Batch-wise operation – laB
air
Aeration/reaction – 2 hours
Growth on storage polymers (PHA)
Nitrification (outside)
Denitrification (inside)
Notes: Subsequently nitrite and nitrate are available for denitrification.
Denitrification takes place using storage polymers as organic carbon source,
- remember that the organic carbon from the influent has been completely converted.
Denitrification is performed by bacteria which are located at the inside of the granule, typically PAO/
(NEXT SLIDE)

## Slide 49: Batch-wise operation – laB
Air
Growth on storage polymers (PHA)
Nitrification (outside)
Denitrification (inside)
Uptake of phosphate
Aeration/reaction – 2 hours
Notes: The influent phosphate and the phosphate which has been released in the anaerobic phase
will now be taken up and stored as polyphosphate.
(NEXT SLIDE)

## Slide 50: concentration profiles – laB
Aeration/Reaction
Notes: And here are the corresponding concentration profiles
(NEXT SLIDE)

## Slide 51: concentration profiles – laB
NH4+
NO3-
Aeration/Reaction
Ammonium conversion
Nitrate formation
Notes: ammonium is nitrified to nitrate
(NEXT SLIDE)

## Slide 52: concentration profiles – laB
PO43-
Ammonium conversion
NH4+
Phosphate uptake
Nitrate formation
NO3-
Aeration/Reaction
Notes: and phosphate is taken up
(NEXT SLIDE)

## Slide 53: Batch-wise operation – laB
Settling (2-10 min) / Effluent discharge
Notes: After the aeration phase comes a settling phase
followed by effluent discharge.
(NEXT SLIDE)

## Slide 54: Batch-wise operation – laB
Removal of slow settling biomass (flocs and small low-density granules)
Fast settling biomass retained (granules)
Settling (2-10 min) / Effluent discharge
Notes: Flocs and small particles that do not settle fast enough will be washed out.
Fast settling biomass, like granules, will be retained in the system.
(NEXT SLIDE)

## Slide 55: concentration profiles – laB
PO43-
NH4+
NO3-
Notes: And here you have the concentration profiles all together
(NEXT SLIDE)

## Slide 56: iNSIDE THE GRANULE
Outer layer: nitrifiers
Inside: (denitrifying) PAO
Notes: Inside the granule, it looks like this:
there are the nitrifiers in the outer layers
and the denitrifying phosphorus accumulating bacteria at the inside.

## Slide 57: Batch-wise operation – full-scale
Notes: Let’s now move on to full-scale
(NEXT SLIDE)

## Slide 58: Batch-wise operation – full-scale
Operated in sequencing batch mode
fill and draw
Notes: Full-scale aerobic granular sludge reactors are also operated in sequencing batch mode,
with a fill and draw phase…
(NEXT SLIDE)

## Slide 59: Batch-wise operation – full-scale
Operated in sequencing batch mode
fill and draw
aeration
Notes: an aeration phase…
(NEXT SLIDE)

## Slide 60: Batch-wise operation – full-scale
Operated in sequencing batch mode
fill and draw
aeration
short settling phase
Notes: and a short settling phase.
(NEXT SLIDE)

## Slide 61: Batch-wise operation – full-scale
Operated in sequencing batch mode
fill and draw in one phase
Notes: But the main difference with the lab-scale operation which I just presented
is that the influent feeding and the effluent withdrawal take place simultaneously.
(NEXT SLIDE)

## Slide 62: Batch-wise operation – full-scale
+ time saving
+ energy saving
+ relatively low discharge flow
Operated in sequencing batch mode
fill and draw in one phase
Notes: Simultaneous influent feeding and effluent discharge has several advantages:
It saves time and energy,
and makes that the discharge flow can be kept relatively low.
(NEXT SLIDE)

## Slide 63: concentration profiles – full-scale
Notes: And here you have the concentration profiles during a typical day of operation in a full-scale granular sludge installation.
(NEXT SLIDE)

## Slide 64: batch operation facilitates monitoring
 6 hours
Notes: Let’s isolate one cycle, which takes about 6 hours
(NEXT SLIDE)

## Slide 65: batch operation facilitates monitoring
 6 hours
Notes: and now stretch the profile a bit so we can see it better.
(NEXT SLIDE)

## Slide 66: batch operation facilitates monitoring
 6 hours
Qinfluent
 6 hours
O2
Notes: The orange line indicates when influent is fed
the blue line shows the oxygen concentration profile in the reactor.
(NEXT SLIDE)

## Slide 67: batch operation facilitates monitoring
 6 hours
Qinfluent
 6 hours
O2
NO3-
Notes: We see how nitrate is consumed during anaerobic feeding
and produced during the aerobic reaction phase

## Slide 68: batch operation facilitates monitoring
 6 hours
Qinfluent
 6 hours
O2
NO3-
NH4+
Notes: This is because, during the aerobic phase, nitrification takes place.
So ammonium is converted to nitrate.
(NEXT SLIDE)

## Slide 69: batch operation facilitates monitoring
 6 hours
Qinfluent
 6 hours
O2
NO3-
NH4+
PO43-
Notes: Phosphate is released during anerobic feeding
and taken up during the aeration phase
(NEXT SLIDE)

## Slide 70: batch operation facilitates monitoring
Notes: Overall, the dynamic concentration profiles obtained during batch-wise operation contain a lot of information.
The slope of the concentration profiles is related
to the biological conversion rates and to
the volume exchange ratio, that is the fraction of the reactor volume which is replaced with fresh wastewater during each cycle.
All of this information is very useful for process monitoring and control.
(NEXT SLIDE)

## Slide 71: batch operation  good effluent quality
Notes: This batch-wise operation also results in a good effluent quality.
(NEXT SLIDE)

## Slide 72: batch operation  good effluent quality
Continuous stirred tank reactor
Notes: In a continuous stirred tank reactor,
the concentrations in the reactor are equal to the effluent concentrations, which are typically required to be relatively low.
(NEXT SLIDE)

## Slide 73: batch operation  good effluent quality
Relatively low concentrations
in the reactor
 substrate-limited
Continuous stirred tank reactor
Notes: Operating the reactor at such low concentrations may lead to substrate limitation, and thus to low bioconversion rates.
(NEXT SLIDE)

## Slide 74: batch operation  good effluent quality
Batch reactor
Continuous stirred tank reactor
Relatively low concentrations
in the reactor
 substrate-limited
Notes: During batch operation,
the substrate concentrations in the reactor decrease over time,
from the influent concentration at time zero – which is typically high
to the required effluent concentration at the end of operation.
(NEXT SLIDE)

## Slide 75: batch operation  good effluent quality
Relatively high concentrations
in the reactor
 no substrate limitation
Batch reactor
Continuous stirred tank reactor
Relatively low concentrations
in the reactor
 substrate-limited
 higher overall bioconversion rates
Still lower effluent concentrations
Notes: As a result, the substrate concentration in the reactor is high most of the time
and will not be limiting the bioconversion rate.
As a result, the effluent concentrations can become very low
without lowering the overall conversion rates.
(NEXT SLIDE)

## Slide 76: sequencing batch process control
Notes: The batch-wise operation involves specific process control aspects
(NEXT SLIDE)

## Slide 77: Process control objectives
Why?
Notes: First of all: why do we need process control?
(NEXT SLIDE)

## Slide 78: Process control objectives
Why?
Meet effluent criteria for COD, N and P
Avoid suspended solids in effluent
Optimize SRT
Manage variations in influent flow rate and composition
Notes: Well, we need to meet the effluent criteria
for organic carbon (expressed in COD), nitrogen and phosphorus
We want to avoid suspended solids in the effluent
We want to optimize the sludge retention time or SRT
and we need to manage all of this dealind with variation in the influent flow rate and compositon
(NEXT SLIDE)

## Slide 79: Process control Handles
How?
Notes: A next question is : how can we control the process – what are the control handles that we have to influence the process ?
(NEXT SLIDE)

## Slide 80: Process control Handles
How?
Biological conversion rates are monitored over time
Notes: As already indicated, the batch-wise, dynamic reactor operation makes it possible to monitor the biological conversion rates over time.
(NEXT SLIDE)

## Slide 81: Process control Handles
How?
Biological conversion rates are monitored over time
Set-points are adjusted
Cycle and phase length control
Batch scheduling – see lecture Edward van Dijk
Notes: Furthermore, set points can be adjusted,
cycle and phase length can be controlled
and can even be adapted according to the influent conditions.
The last option is called batch scheduling – you will learn more about that in the lecture of Edward van Dijk.
(NEXT SLIDE)

## Slide 82: BASIC Process control
Fill and draw (feeding) phase
Aeration/Reaction
Notes: In this lecture, we will have a look at more basic control aspects of the sequencing batch reactor,
during the fill and draw phase
and during the aeration/reaction phase.
(NEXT SLIDE)

## Slide 83: Fill and draw
Operation
Anaerobic conditions
Fed from the bottom through settled bed
Organic carbon taken up and stored
No aerobic growth
Notes: The fill and draw phase is characterized by anaerobic conditions,
the influent is fed from the bottom through the settled sludge bed,
organic carbon is taken up and stored,
and there is no aerobic growth
(NEXT SLIDE)

## Slide 84: Fill and draw
Control
Cycle length: typically 1h
ensure enough rbCOD uptake
dependent on COD/P and BOD/COD;
Notes: The length of the fill and draw phase is typically one hour.
It needs to be long enough to ensure the uptake of readily degradable organic carbon
this will depend on the influent COD/phosphorus ratio and BOD/COD ratio.
(NEXT SLIDE)

## Slide 85: Fill and draw
Control
Cycle length: typically 1h
ensure enough rbCOD uptake
dependent on COD/P and BOD/COD;
Maximum volume exchange ratio (VER) = 65%
- to prevent influent being mixed with effluent during plug-flow feeding
- to prevent sludge washout
Notes: There is also a limitation regarding the volume exchange ratio or VER,
This is the ratio between the volume of the fresh influent which is fed in a cycle
over the reactor volume.
The volume exchange ratio always needs to be lower than 65%
to make sure that the influent wastewater is not mixed with the clean effluent
and to prevent sludge washout.
(NEXT SLIDE)

## Slide 86: Fill and draw
Control
Cycle length: typically 1h
ensure enough rbCOD uptake
dependent on COD/P and BOD/COD;
Maximum volume exchange ratio (VER) = 65%
- to prevent influent being mixed with effluent during plug-flow feeding
- to prevent sludge washout
Maximum upflow velocity vupflow = = 5 m/h
- to prevent sludge washout
Notes: Finally, there is also a requirement for the upflow velocity in the reactor,
The upflow velocity is calculated as the influent flow rate divided by the reactor cross section area.
It must remain lower than 5 m per hour
to prevent sludge washout
(NEXT SLIDE)

## Slide 87: aeration/reaction phase
Operation
Aerated
Notes: Next comes the aeration phase
(NEXT SLIDE)

## Slide 88: Reaction phase
Operation
Aerated
(almost) no rbCOD in liquid
Slow growth on intracellular storage polymers
Simultaneous removal or organic carbon, N, P
Notes: In this phase, there is almost no readily biodegradable organic carbon left in the liquid.
There is slow growth on intracellular storage polymers
and simultaneus removal of
organic carbon, nitrogen and phosphorus,
as we have discussed earlier
(NEXT SLIDE)

## Slide 89: Reaction phase
Control
Length aeration phase:
to allow nitrification + phosphate uptake
Notes: The length of the aeration phase is controlled
In order to allow nitrification and phosphorus removal
In some cases it is chosen to apply chemical phosphorus removal
Besides biological phosphorus removal.
(NEXT SLIDE)

## Slide 90: Reaction phase
Control
Length aeration phase:
to allow nitrification + phosphate uptake
Oxygen set-point
determines simultaneous nitrification-denitrification
Notes: The oxygen set point
Will determine the oxygen penetration depth in the granules and thus
The extent of simultaneous simultaneous nitrification -denitrification
(NEXT SLIDE)

## Slide 91: Reaction phase
Control
Length aeration phase:
to allow nitrification + phosphate uptake
Oxygen set-point
determines simultaneous nitrification-denitrification
Optional: additional phase with on/off aeration
if extra denitrification is required
Notes: In some cases, also an additional phase with on/off aeration is applied.
This is done when extra denitrification is required.
(NEXT SLIDE)

## Slide 92: additional granule selection pressures

## Slide 93: How to grow granules?
Make sure that diffusion is not limiting!
 Separation of substrate uptake and biomass growth
Notes: We already know that the prime prerequisite for growing granules is to make sure that diffusion is not limiting.
This condition is fulfilled by having an anaerobic feeding phase for substrate uptake
and an aerobic reaction phase for biomass growth.
This is the most important condition, but not the only one
(NEXT SLIDE)

## Slide 94: How to grow granules?
Make sure that diffusion is not limiting!
 Separation of substrate uptake and biomass growth
Selective wasting
Notes: Another important selection pressure
is selective wasting
(NEXT SLIDE)

## Slide 95: selective wasting
Reactor always contains some flocculent material (1-2 g/L)
  inert particulate organic carbon
  biomass grown on remaining organic carbon after anaerobic feeding
  eroded material from granules
   Poor-settling fraction
Notes: Selective wasting is based on the observation that the reactor always contains some flocculent material
This flocculent material consists of
(i) inert particulate organic carbon,
(ii) biomass grown on organic carbon
which was left over after anaerobic feeding
and of (iii) eroded material from granules
(NEXT SLIDE)

## Slide 96: selective wasting
Top of sludge bed is removed after a short settling period
 SRT floc fraction = 0.5-5 days
 SRT granules = 30 days
Reactor always contains some flocculent material (1-2 g/L)
  inert particulate organic carbon
  biomass grown on remaining organic carbon after anaerobic feeding
  eroded material from granules
   Poor-settling fraction
Notes: In selective wasting, the top of the sluge bed is removed after a short settling period
As a result, the flocculent biomass fraction in the reactor
will be retained in the reactor for less than 5 days
while the granules will have an SRT of about 30 days.
(NEXT SLIDE)

## Slide 97: selective wasting
i.e., settling-based selection
Top of sludge bed is removed after a short settling period
 SRT floc fraction = 0.5-5 days
 SRT granules = 30 days
Reactor always contains some flocculent material (1-2 g/L)
  inert particulate organic carbon
  biomass grown on remaining organic carbon after anaerobic feeding
  eroded material from granules
   Poor-settling fraction
Notes: So selective wasting selects for granules based on their good settling properties.
(NEXT SLIDE)

## Slide 98: How to grow granules?
Make sure that diffusion is not limiting!
 Separation of substrate uptake and biomass growth
Selective wasting
(Shear)
Notes: And how about shear as a selection pressure?
You see that I put ‘shear’ between brackets,
which already indicates that it will not be a main selection pressure.
(NEXT SLIDE)

## Slide 99: shear
To create smooth biofilms / granules
Notes: In the literature, there are definitely indications that applying shear will help to create smooth biofilms or granules.
(NEXT SLIDE)

## Slide 100: shear
To create smooth biofilms / granules
Energy inefficient
Not needed if diffusion is not limiting
Notes: However, it requires a lot of energy to create shear stress on the granule surface
and also it is not needed as long as you stick to the first requirement to grow granules,
which is to make sure that diffusion is not limiting,
and which you can do by separating substrate uptake and biomass growth
(NEXT SLIDE)

## Slide 101: How to grow granules?
Make sure that diffusion is not limiting!
 Separation of substrate uptake and biomass growth
Selective wasting
(Shear)
Plug-flow feeding
Notes: (pauze) Besides avoiding diffusion limitation and
besides applying selective wasting,
an additional selection pressure to grow granules is
plug-flow feeding
(NEXT SLIDE)

## Slide 102: Plug flow feeding
Feeding influent through settled granular sludge bed
Influent feed
Notes: In aerobic granular sludge reactors, the influent is fed
from the bottom of the reactor,
through the settled granular sludge bed
(NEXT SLIDE)

## Slide 103: Plug flow feeding
Feeding influent through settled granular sludge bed
  to minimize diffusion limitation
  to ensure best substrate uptake over the granule depth
Influent feed
Notes: In this way, diffusion limitation is minimzed
and the substrate can best be taken up over the whole depth of the granule
(NEXT SLIDE)

## Slide 104: Plug flow feeding
Moreover: granules at the bottom
- which are already the largest -
get even more food !
Influent feed
Feeding influent through settled granular sludge bed
  to minimize diffusion limitation
  to ensure best substrate uptake over the granule depth
Notes: Moreover, in this way,
the larger granules at the bottom of the reactor receive the most food,
while the slow-settling flocs at top receive less food.
So there is a self-stabilizing effect.
(NEXT SLIDE)

## Slide 105: How to grow granules?
and more…
– see lecture Edward van Dijk
Make sure that diffusion is not limiting!
 Separation of substrate uptake and biomass growth
Selective wasting
(Shear)
Plug-flow feeding
Notes: So, that were the most important tricks to grow granules.
However, there are even more selection presssures which can be applied.
For more information on that, I refer you to the lecture of Edward van Dijk.
(NEXT SLIDE)

## Slide 106
Biological Wastewater Treatment
Online Course Series
Notes: That’s all for me today.
Enjoy the rest of the course!