## Slide 1
Course on Membrane Bioreactors
Future Trends of
Membrane Bioreactors
Systems
Xia Huang
Notes: Hello everyone! I’m Professor Xia Huang from Tsinghua University. In this section, we are going to learn the future development trends of MBR systems.

## Slide 2: Future trends in MBRs systems
Challenges remain …
Future research should focus on?
  MBR: Promising alternative for wastewater treatment
  Advantages: reduce land usage, improve effluent quality
Fouling?
Cost reduction?
Synergy between
membrane-microbes?
Biological Wastewater Treatment
Online Course Series
Notes: After half a century of development, MBRs are acknowledged to be a very promising alternative for municipal and industrial wastewater treatment.
As mentioned above, they have several advantages over conventional activated sludge processes because of the involvement of membrane separation. In all, the application of MBRs can substantially reduce land usage and improve effluent quality, etc. As such, MBRs are an indispensable alternative in the field of wastewater treatment and reclamation.
However, challenges remain. Future research should focus on addressing the following issues:
Firstly, membrane fouling control;
Secondly, further reduction on capital and operational costs
Thirdly, improving the synergistic effects between membranes and microbes.

## Slide 3: Future trends in MBRs systems
  Controlling membrane fouling
  Urgent bottleneck: membrane fouling
  Require manual maintenance
  e.g. intensive membrane cleaning
  Result in additional burdens
Biological Wastewater Treatment
Online Course Series
  Clean MBR fiber
  Severely fouled
  MBR fiber
  It’s necessary to…
  Monitor operation data of large-scale MBR plants
  Understand fouling development patterns
  e.g. seasonal variations
Notes: Among all, fouling control is undoubtedly one of the most urgent bottlenecks in the further promotion of all membrane-based technologies.
The occurrence of membrane fouling can ultimately result in unexpected and irregular manual maintenance such as the implementation of intensive cleaning. This leads to additional burdens for an MBR plant. Thus, it is necessary to understand the fouling development patterns in large-scale MBR plants, such as the seasonal variations of membrane fouling rates.

## Slide 4: Future trends in MBRs systems
Image source: Niu et al. Artificial intelligence-incorporated membrane fouling prediction for membrane-based processes in the past 20 years: A critical review. Water Research, 2022 (216): 118299.
  Computer-aided diagnosis and control
    Collect data, understand patterns
    Diagnosis, with the help of artificial intelligence
    Design novel controlling scheme
  Controlling membrane fouling
Biological Wastewater Treatment
Online Course Series
Notes: Then, according to the big data of MBR plants, computer-aided diagnosis and control of membrane fouling (for example with the aid of artificial intelligence) can be realized in the near future.
By learning and predicting the changes of transmembrane pressure and flux, novel fouling control schemes could be developed.

## Slide 5: Future trends in MBRs systems
  Controlling membrane fouling
  Improved membrane cleaning
    More efficient cleaning agents
    New cleaning modes
  Other mechanically-assisted fouling control methods
    e.g. mechanical vibration
Biological Wastewater Treatment
Online Course Series
  Computer-aided diagnosis and control
    Collect data, understand patterns
    Diagnosis, with the help of artificial intelligence
    Design novel controlling scheme
Notes: In addition, because chemical cleaning is essential for flux recovery, future work should also focus on looking for more efficient cleaning agents and developing new cleaning modes.
Other mechanically-assisted fouling control methods such as mechanical vibration are a potential alternative.

## Slide 6: Future trends in MBRs systems
  Reducing costs
Biological Wastewater Treatment
Online Course Series
MBR Costs
Operational cost
Capital cost
Notes: Next, although the manufacture and construction costs of MBR have already been reduced, there are still some potentials for further reduction on costs. In fact, high capital and operational costs is another factor limiting the acceptance of MBRs by wastewater sectors.

## Slide 7: Future trends in MBRs systems
  Reducing costs
Biological Wastewater Treatment
Online Course Series
MBR Costs
    Low cost membrane (material, configuration, construction)
    Chemical-resistant membrane with long lifespan
Operational cost
Capital cost
Notes: A decrease in capital cost can be achieved through development of low-cost membranes or development of chemical-resistant membranes with a long lifespan.

## Slide 8: Future trends in MBRs systems
  Reducing costs
Biological Wastewater Treatment
Online Course Series
MBR Costs
    Optimize membrane scouring
    Update aeration modes
      Reduced fouling
      Increased mass transfer
      Decrease in aeration usage
Operational cost
Capital cost
Notes: The operational cost can be decreased by optimizing the membrane scouring and bioreactor aeration systems, which are linked with membrane fouling control and pollutant removal, respectively.
Regardless, the aeration modes should be updated in order to enhance the fouling control of membranes and to increase oxygen transfer in the mixed liquor, which can lead to a decrease in aeration usage.

## Slide 9: Future trends in MBRs systems
  Bacterial population: high diversity and concentration in MBRs
  Multiple microbial functions: endogenous denitrification, sludge reduction, growth of specialized micro-organisms
  Improve the synergistic effects
Microbes
Membranes
Biological Wastewater Treatment
Online Course Series
Notes: Owing to higher MLSS concentrations in MBRs than in conventional activated sludge processes, there is a larger potential to improve the synergistic effects between microbes and membranes.
For instance, there are opportunities to take advantage of bacterial populations with such a high concentration and high biodiversity.
Also, MBRs can allow the occurrence of multiple microbial functions, such as endogenous denitrification, sludge reduction, and the growth of specialized microorganisms.
In this way, the synergy between microbes and membranes could improve the pollutant removal and decrease operational costs of MBRs.
Today, MBRs are preferred in water-deficient regions or densely populated cities where land usage is relatively expensive.
MBRs can also be used for decentralized wastewater treatment (such as in rural areas), because MBRs, compared with conventional activated sludge processes, are easier for modularized installation, with high flexibility in process configuration.
Moreover, combined MBRs+RO processes are very appropriate for achieving zero liquid discharge during industrial wastewater treatment.
Because of the high selectivity of membranes and the strong biodegradation capacity of biomass, MBRs are also attractive for achieving resource and energy recovery from wastewater streams.

## Slide 10: Future trends in MBRs systems
  Bacterial population: high diversity and concentration in MBRs
  Multiple microbial functions: endogenous denitrification, sludge reduction, growth of specialized micro-organisms
  Improve the synergistic effects
  Suitable applications
  Regions: water-deficient, or densely populated cities
  Decentralized wastewater treatment (e.g. rural areas)
  Hybrid membrane process for zero-liquid discharge (e.g. MBR-RO)
  Energy and resource recovery
Microbes
Membranes
Biological Wastewater Treatment
Online Course Series
Notes: Owing to higher MLSS concentrations in MBRs than in conventional activated sludge processes, there is a larger potential to improve the synergistic effects between microbes and membranes.
For instance, there are opportunities to take advantage of bacterial populations with such a high concentration and high biodiversity.
Also, MBRs can allow the occurrence of multiple microbial functions, such as endogenous denitrification, sludge reduction, and the growth of specialized microorganisms.
In this way, the synergy between microbes and membranes could improve the pollutant removal and decrease operational costs of MBRs.
Today, MBRs are preferred in water-deficient regions or densely populated cities where land usage is relatively expensive.
MBRs can also be used for decentralized wastewater treatment (such as in rural areas), because MBRs, compared with conventional activated sludge processes, are easier for modularized installation, with high flexibility in process configuration.
Moreover, combined MBRs+RO processes are very appropriate for achieving zero liquid discharge during industrial wastewater treatment.
Because of the high selectivity of membranes and the strong biodegradation capacity of biomass, MBRs are also attractive for achieving resource and energy recovery from wastewater streams.

## Slide 11
Course on Membrane Bioreactors
Acknowledgements
The presenters express their great appreciation to Dr. Guihe Tao from PUB, Singapore’s National Water Agency, Dr. Jinsong Zhang from CITIC Envirotech Ltd., Dr. Min Luo from SUEZ Water Technologies & Solutions, and China Everbright International Ltd. for providing information about the full-scale case studies. We would also like to acknowledge Mr. Sang Yeob Kim and Mr. Mauricio Barreto, PhD students at IHE Delft Institute for Water Education, for their technical contribution to developing HL-MBR in case study. Thank BlueInGreen LLC, OVIVO Water-MBR Systems, and ECO Oxygen Technologies LLC for their financial support to conduct most of the research on HL-MBR presented in the case study.
Notes: The above is the entire content of this chapter. I guess you already had a comprehensive understanding of MBR technology at this moment. I hope you enjoyed this chapter. Thank you!