## Slide 1
Course on Membrane Bioreactors
Introduction to
Membrane Bioreactors
Xia Huang
Notes: In this section, we are going to have a deeper understanding towards MBR technology.

## Slide 2: Contents
  Membrane bioreactor history
  Membrane bioreactor features
  Membrane bioreactor configuration
  Membrane materials and modules
  Commercial membrane module makers
Biological Wastewater Treatment
Online Course Series
Notes: In specific, we will learn its development history, features, configurations, materials and modules, as well as commercial manufacturers.

## Slide 3: Contents
  Membrane bioreactor history
  Membrane bioreactor features
  Membrane bioreactor configuration
  Membrane materials and modules
  Commercial membrane module makers
Biological Wastewater Treatment
Online Course Series
Notes: So, here is the first part: MBR’s history.

## Slide 4: Membrane bioreactor (MBR) history
Judd S. and Judd C. (2011). The MBR Book: Principles and Applications of Membrane Bioreactors for Water and Wastewater Treatment, 2nd ed. Butterworth- Heinemann, Oxford.
Activated sludge process
UF membrane in lab-scale
Sidestream MBR
by Dorr-Oliver
Submerged MBR
by Yamamoto et al.
Booming development
Early 20th Century
= Sidestream mem-brane + Activated sludge
Limitation: high energy consumption
1960s
1989
1990s-present
Lower suction pressure
Absence of recirculation pump
Applied in domestic and industrial wastewater
Various membrane companies: Kubota, Mitsubishi Rayon, Norit X-Flow, GE-Zenon.
Biological Wastewater Treatment
Online Course Series
Notes: Since the discovery of activated sludge in the early 20th century, activated sludge processes have been widely used. However, they are limited by the difficulties in solid-liquid separation. In the meanwhile, UF membranes were developed in Europe and used in lab research with the purpose of separation of bacteria or biomolecules.
In the late 1960s, MBRs were developed by Dorr-Oliver with a combination of side-stream membranes and activated sludge, aiming to address the issue of solid/liquid separation in conventional activated sludge processes. This combined system was initially applied in Japan for small-scale municipal wastewater treatment.
Nevertheless, due to the high energy consumption of side-stream MBRs, the development of MBR urgently needs improvement and changes.
At this time, submerged MBR was created by Prof. Yamamoto in 1989, and became a breakthrough in MBR development. In comparison, submerged MBRs usually have lower energy consumption due to smaller suction pressure and the absence of recirculation pump. Since then, MBR-based processes have been widely accepted and applied in wastewater treatment.
An active player in MBR application in the 1990s was Kubota. It installed approximately 60 MBR plants in Japan in that era. After that, other membrane companies, including Mitsubishi Rayon, Norit X-Flow and GE-Zenon, have promoted the commercial application of MBRs. Since then, MBRs have been widely used throughout the world.

## Slide 5: Membrane bioreactor features
  Less land occupation and footprint
Notation: HRT - hydraulic retention time; SRT - solids retention time; MLSS - mixed liquor suspended solids.
  Higher permeate quality
  Less sludge production
Membrane process
Biological process
MBR
  No secondary clarification tank
  High volumetric loading rate
  Membrane rejection
  Biological degradation
  Independent control of SRT and HRT
  Longer SRT and higher MLSS concentration
Features
Advantages
  MF/UF
Biological Wastewater Treatment
Online Course Series
Notes: Since MBRs combines the benefits of both biological transformation and membrane separation, it possesses several advantages.
Firstly, both the elimination of the secondary clarification tank and the increased volumetric loading rate lead to the more efficient utility of lands. According to the reports, the land occupation can be reduced by 30-50% depending on the plant capacity of MBR, with less footprint generated.
Secondly, owing to membrane rejection and the enhanced biological degradation, lower concentrations of pollutants were left in the effluent. Thus, higher permeate quality could be achieved, which could meet the more and more stringent discharge regulations and the requirement of water reuse.
Thirdly, MBR allows the independent control of sludge- and hydraulic retention time, which are usually called as SRT and HRT. This feature leads to easier regulation of such parameters and much higher mixed liquor suspended solids concentrations. The MBR can be operated at a longer SRT, reducing the volume of sludge produced. Therefore, by applying MBR, less sludges are generated. This advantage is especially attractive in regions where waste sludge treatment has not been well conducted.
Today, owing to these features, MBRs are considered to be an important process for wastewater treatment. Additionally, MBR-based processes have been retrofitted largely with the use of novel membrane processes, such as membrane distillation-based MBRs and forward osmosis-based MBRs. MBR systems have also been expanded to other biological processes, such as aerobic granules, anammox, and particularly anaerobic processes.

## Slide 6: Membrane bioreactor configuration
Outlet
Inlet
Outlet
  Two main MBR configurations
Side-stream MBR（sMBR)
Submerged MBR（iMBR)
Bioreactor
Sludge
Membrane
Recirculated stream
Permeate
Inlet
Bioreactor
Permeate
Sludge
Positive pressure
Vacuum pressure
  iMBR: Less energy intensive
    Aeration side-effects: less fouling
    Online backflush and cleaning
    Less land occupation
Biological Wastewater Treatment
Online Course Series
Notes: Next, we are going to study the configuration types of MBR.
There are two main MBR configurations with different membrane units and different driven pressure for permeate: the side-stream MBR (or we usually call sMBR) with positive pressure, and submerged or immersed MBRs (abbreviated as iMBRs) with vacuum pressure.
As shown in the slide, in side-stream configuration, the membrane units are installed externally to the bioreactor, which is often located in a plant room. The biomass is either pumped directly through a number of membrane modules in series and back to the bioreactor, or pumped to a bank of modules. In this way, a second pump is used to circulate biomass through the modules in series. Cleaning and soaking of the membranes in this configuration is in-situ conducted, with the use of an installed cleaning tank, pump and pipework.
In contrary, for submerged configuration, the membrane units are installed in either the main bioreactor vessel or in a separate tank. In these MBRs, aeration can provide oxygen for biomass and can control membrane fouling by their scouring effects. The membranes can incorporate an online backflush system which reduces membrane surface fouling by pumping membrane permeate back through the membrane. Similarly, online chemical cleaning can also be conducted by pumping chemical solutions back to the modules without the need of the transfer of either membrane modules or mixed liquor.
In general, iMBRs are less energy-intensive than sMBRs, because of the side-effects of aeration for fouling control. However, despite the more favorable energy usage of submerged membranes, there continues to be a market for the side-stream configuration, particularly in smaller flow industrial applications (such as landfill leachate treatment), where membrane cleaning is more frequent.
The design of MBR processes should take full consideration of all the operating factors, including membrane flux, transmembrane pressure (TMP), energy usage, and cleaning frequency.

## Slide 7: Membrane bioreactor configuration
  Novel
  MBRs
Hybrid MBRs for nutrient removal
Special microbe-based MBRs
MBRs for wastewater reuse
MBRs for fouling control
    AGMBR (aerobic granular sludge MBR)
    HFMBR (hybrid biofilm MBR)
    Anammox MBR
    Fungi MBR
    MBR+RO
    MDBR (membrane distillation bioreactor)
    NFMBR (nanofiltration MBR)
    OMBR (osmotic MBR)
    AsMBR (air-sparging MBR)
    Airlift MBR
    MCBR (membrane coagulation bioreactor)
Biological Wastewater Treatment
Online Course Series
Notes: Nowadays, in order to fulfill different purposes of treatment, various novel MBR configurations are gradually developed, such as: aerobic granular sludge MBR (AGMBR), membrane adsorption bioreactor (MABR), osmotic MBR(OBR) and Annamox MBR.
In this way, special needs of fouling control, nutrient removal, wastewater reuse, specialized bacteria cultivation, flux enhancement etc., could be met.

## Slide 8: Membrane materials and module
Membrane modules
Hollow fiber (HF)
Flat sheet (FS)
Membrane materials
Ceramic
  Inorganic materials: Al, Si, Zn, Ti …
  Superior hydraulic, thermal and chemical resistance
Multi-tube (MT)
Polymeric: various polymers
  Cellulose acetate (CA)
  Polyvinylidene difluoride (PVDF)
  Polysulfone (PS)
  Polyethersulfone (PES)
  Polytetrafluoroethylene
  (PTFE)
  …
Biological Wastewater Treatment
Online Course Series
Notes: However, no matter how the configuration changes, the membrane materials of MBRs are generally the same. The material could either be polymeric or ceramic. Several membranes could be assembled into a module. Currently, the major form of membrane modules are hollow fiber, flat sheet and multi-tube.
For ceramic membranes, it is usually fabricated by inorganic materials, such as aluminum, zirconium, silica, and titanium oxide. Reports showed that ceramic membranes exhibit superior hydraulic, thermal and chemical resistance.
For commercial polymeric membranes, cellulose acetate, polyvinylidene difluoride, polysulfone, polyethersulfone and polytetrafluoroethylene are the most prevalently used polymers.

## Slide 9: Membrane materials and module
Membrane modules
Hollow fiber (HF)
Flat sheet (FS)
Membrane materials
Most commonly used:
polyvinylidene fluoride (PVDF)
  polyethylsulphone (PES)
Either polymeric or ceramic
Ideal properties:
  Good mechanical strength
  High porosity
  Chemical stability
  Anti-fouling
Multi-tube (MT)
Biological Wastewater Treatment
Online Course Series
Notes: A good membrane for MBR application should have the following characteristics:
(i) mechanically robust, which means it has enough strength to withstand frequent flushing and air scouring;
(ii) high porosity, with suitable pore size and narrow pore size distribution to provide high selectivity and high water permeability;
(iii) More importantly, the material should be resistant to chemical attack. In other words, it should be resistant to extreme pH and oxidant during chemical cleaning,
and (iv) ideally fouling-resistant.
Considering above factors, for the MBR market, PES and PVDF membranes are the dominant products.

## Slide 10: Contents
  Membrane bioreactor history
  Membrane bioreactor features
  Membrane bioreactor configuration
  Membrane materials and modules
  Commercial membrane module makers
Biological Wastewater Treatment
Online Course Series
Notes: Because of the unique feature of MBRs and the significant reduction in membrane price, MBRs have become increasingly and widely used for wastewater treatment in the last decade.

## Slide 11: Commercial module makers
  …
Booming development !
Biological Wastewater Treatment
Online Course Series
Notes: More than 40 companies globally provide membrane module products for MBR applications with various categorization.
Therefore, at the end of this section, let’s take a look at mainstream commercial membrane module products and their makers in current market.

## Slide 12: Suez ZeeWeed® HF membrane
Source: brochure of Suez ZeeWeed products (https://www.watertechnologies.com/products/zeeweed-ultrafiltration). | MGD: million gallons per day.
Total installed capacity has grown at an exponential rate
ZeeWeed 500: 1st vertical hollow fiber membrane on the market (introduced in 1993)
ZeeWeed 500 membrane train
with LEAPmbr®
aeration technique
ZeeWeed 500D Cassette
Nominal pore size = 0.035 μm
Total energy usage of (aeration + permeation) less than 0.06 kWh/m3
> 2300 MBRs globally, producing >7 billion gallon/day of clean water
Biological Wastewater Treatment
Online Course Series
Notes: Next, we are going to cast a glance at one of the earliest MBR membrane module, ZeeWeed® 500 produced by Zenon Environmental Inc., which was successively acquired by GE Water & Process Technologies and Suez in 2006 and 2017, respectively.
The ZeeWeed 500 module was also the first vertical hollow-fiber membrane on the market. It was firstly introduced to the market in 1993. The current ZeeWeed® 500 membrane can be used for applications ranging from drinking water to seawater desalination, but it is best known for use in MBR applications.
The ZeeWeed® 500 membrane for MBR uses a specifically formulated reinforced PVDF chemistry that results in a UF membrane with a nominal pore size of 0.035 μm. The current product features LEAPmbr® membrane and aeration technology, resulting in total energy usage (including aeration and permeation) of less than 0.06 kWh/m3.
After more than thirty years of development, today over 2,300 MBRs globally are using ZeeWeed® 500 membranes, representing more than one million operating modules in the field producing over 7 billion gallon/day of clean water.

## Slide 13: Koch PURON® pulsion MBR system
Source: brochure of Pulsion MBR system (https://www.kochseparation.com/).
Fixed only at the bottom
Immersed HF configuration
Centered aeration nozzle
Large bubble through
the buddle
Biological Wastewater Treatment
Online Course Series
Notes: First, I’m going to introduce the MBR system produced by PURON® company, which was formed in late 2001. This single-header ultrafiltration MBR changed industrial and municipal wastewater treatment since its launch. This patented module features reinforced PVDF hollow fibers fixed only at the bottom, virtually eliminating the clogging buildup of hair, fibrous materials and sludge solids.
Solids and particulates, including bacteria, remain on the outside, while permeate is drawn through the membrane to the inside of the fibers. The aeration nozzle is centered in the fiber bundle to scour the entire fiber length, minimizing power consumption. The next generation of PURON MBR, PULSION MBR modules offer up to 40% aeration energy reduction and 25% footprint reduction. This innovation pulses a large bubble through a chambered fiber bundle, creating a piston-like pumping action that results in lower air and aeration energy requirements than traditional scouring methods.

## Slide 14: KUBOTA Submerged Membrane Unit®
Source: brochure of KUBOTA Submerged Membrane Unit (https://www.kubota.com/products/solutions/lineup/index.html).
As of December 2019, Kubota has more than
6000 MBR installations all over the world.
Flat sheet module
Immersed FS configuration
Applied in the treatment plant
Micro-structure
Membrane Cartridge
    Employed in the treatment of municipal and industrial wastewater since 1990s
    Average pore size = 0.2 μm
Biological Wastewater Treatment
Online Course Series
Notes: In addition to hollow fiber MBR, the plat sheet ones have also been successfully commercialized for decades. One of the well-known manufacturers is KUBOTA Corporation from Japan.
KUBOTA submerged membrane Unit was developed in the late 1980s. This immersed flat sheet MBR system has been employed in plenty of MBR processes for sewage and industrial wastewater treatment all over the world since 1990s.
As illustrated in the slide, the Membrane Unit is consisted of a Membrane Case and a Diffuser Case. For Membrane Case, it houses multiple Membrane Cartridges with an average pore size of 0.2 μm. The Membrane Cartridge is Flat Sheet configuration with an effective filtration area ranging from 0.80 m2/cartridge to 1.45 m2/plate.
As of December 2019, Kubota has more than 6,000 MBR installations all over the world.

## Slide 15: Toray MEMBRAY® product
Source: brochure of Toray MBR flat-sheet products (http://www.toraywater.com/). | PET: polyethylene terephthalate.
Immersed FS configuration
    PVDF flat-sheet membrane on polyethylene terephthalate (PET) non-woven support layer
    Nominal pore size = 0.08 μm, sheet area = 0.7 – 1.4 m2
    NHP series: similar packing density as HF module
Comparison of membrane thickness
Flat sheet membrane element
Cassette
Module
NHP series:
2 mm
Conventional: 6 mm
Biological Wastewater Treatment
Online Course Series
Notes: Toray is another distinct membrane manufacturer from Japan.
Among its all product, Toray’s MEMBRAY® MBR membranes is a typical flat-sheet membrane module. It consists numerous PVDF flat-sheet membranes built on polyethylene terephthalate (PET) non-woven support layers with a nominal pore size of 0.08 μm.
As shown in the slide, usually 50 sheets of flat sheet membrane element make up one cassette. Each sheet has a membrane area of 0.7-1.4 m2. And then, 1~12 cassette form a module. Just imagine the filtration capacity of the whole module!
Recently, Toray has developed the new NHP series module. By applying much thinner membrane sheets, the NHP series have a similar packing density close to a hollow-fiber module, yet could still maintain the excellent features of a flat-sheet MBR module. This new module design provides higher productivity with a smaller footprint and higher cleaning efficiency at lower energy demand.

## Slide 16: Tubular Module: Pentair X-Flow
Source: introduction from the website of Pentair Inc. (https://xflow.pentair.com/en/products)
    Principle of Pentair X-Flow Airlift® module
    Side-stream MBR configuration
    PVDF, pore size = 0.03 μm
Vertical
Compact 33V Helix
    Latest upgraded technology:
    Feed flow reversal (FFR)
Detail
Tubular, provide ideal turbulent conditions
Assembly and application
Biological Wastewater Treatment
Online Course Series
Notes: Lastly, for tubular membrane modules, Pentair Inc. is one of the major suppliers.
In 2011, Pentair acquired Norit X-Flow. The Pentair Airlift® MBR system is preferred in a side-stream MBR configuration. The membrane modules are vertically arranged outside of the bioreactor tank and continuous aeration is introduced from the bottom. The membrane material is PVDF and the mean pore size is 0.03 μm.
In the past decade, Pentair X-Flow developed the Crossflow FFR technology. The Pentair X-Flow is applying an optimized diameter of the tubes in order to deal with the conditions in which these membranes are used. Where higher amounts of solids need to be separated from cleaned water, or turbulent conditions in the separating process offer great benefits, a tubular membrane system is the ideal choice.
The Crossflow FFR technology with the aid of absolute barrier of the Compact 33V Helix membrane elements provide an optimal UF performance able to deliver excellent quality effluent that can be reused while having a reliable system producing biogas with minimal operator interference.

## Slide 17: Commercial membrane module
How to choose the suitable MBR module?
Flat sheet, hollow fiber or multi-tube?
All three forms are widely used. The choice should take the following into consideration:
membrane area to module bulk volume ratio
mass transfer
energy consumption per unit of product water
cost of the membranes
cleaning implementation
Biological Wastewater Treatment
Online Course Series
Notes: After introducing all these diversified MBR system and membrane products, you may ask: which configuration is better? And how to choose the suitable MBR module?
Actually, after decades of development, at present FS, HF and MT modules are all often used in MBRs.
The choice of membrane modules should take the following into consideration: membrane area to module bulk volume ratio, mass transfer, energy consumption per unit of product water, cost of the membranes, and cleaning implementation.