## Slide 1
Course on Membrane Bioreactors
Membrane Fouling
Control
Fangang Meng
Yu-Xi Huang

## Slide 2: Contents
  Fouling control strategies
  Optimization of operation conditions
  Membrane cleaning
  Other control methods
Biological Wastewater Treatment
Online Course Series

## Slide 3: Comprehensive control strategies
Activate sludge
Wastewater
Interface
Membrane
Permeate
Feed pretreatment
Use of ultrafine screens
Sludge modification
Optimization of SRT or HRT  use of coagulants or adsorbents
Hydrodynamic conditions
Intermittent aeration sourcing  automatic aeration  mechanically-assisted aeration
Chemical cleaning
CEB  CIP  intensive cleaning
Sub-critical flux operation
Physical cleaning
Backwashing  relaxation  vibration  ultrasonic cleaning
Biological Wastewater Treatment
Online Course Series

## Slide 4: Optimization of operation conditions
Feed Pretreatment
The pretreatment (and primary treatment) facilities include a screen, a grit chamber, and a primary sedimentation tank.
Screen
screenings
Grease trap for individual applications
outlet
inlet
Aerated grit and grease removal tank
Fats, oil and grease
Outlet
inlet
Biological Wastewater Treatment
Online Course Series

## Slide 5: Optimization of operation conditions
Source: Buer, et al., Desalination, 2010, 250(3): 1073-1077.
Enhancement of hydrodynamic conditions
Improvement of aeration intensity can facilitate
physical cleaning due to the increase of
cross-flow velocity and shear stress
The ‘eco-aeration’ strategy using intermittent aeration with 10/30 intervals saves up to 50% of the energy consumed in aeration
Automatic aeration control
Biological Wastewater Treatment
Online Course Series

## Slide 6
Source: Kurita, et al., Separation and Purification Technology, 2015: 141, 207-213.
The addition of hard particles (granular-activated carbon and plastic beads) into the mixed liquor can considerably intensify the fluid dynamics
The addition of hard particles
The plastic beads which are fluidized by aeration scouring can create a cutting effect on bio-cake
The introduction of plastic particles or beads may cause membrane damage
Optimization of operation conditions
Biological Wastewater Treatment
Online Course Series
Enhancement of hydrodynamic conditions

## Slide 7: Optimization of operation conditions
Source: Cheng, et al., Water research, 2020, 168: 115195.
Optimization of membrane flux
Low flux can ensure a low fouling development rate, but with low water production
The critical flux for a given membrane varies with ambient
The critical flux in a given MBR plant should be periodically re-evaluated and the fouling control strategies should be updated
Critical flux determination is a prerequisite for MBR operation, as a sub-critical flux operation is usually preferred by
most membrane suppliers
Biological Wastewater Treatment
Online Course Series

## Slide 8: Fouling control
1
2
3
Membrane fouling control methods
Chemical cleaning
Acid (citric acid)、alkali (NaOH)、 oxidant (NaOCl)
Biological methods
Quorum quenching, SMP/EPS biodegradation, native/metazoan predation
Vibration/rotation, hydraulic bubble, Ultrasonic cleaning, etc
Physical cleaning
Biological Wastewater Treatment
Online Course Series

## Slide 9: Membrane cleaning
Physical cleaning
  Restores flux and reduces energy consumption
  Reduces chemical usage
  Improves effluent quality
  Enhances system flexibility
  Continuous maintenance
Biological Wastewater Treatment
Online Course Series

## Slide 10: Membrane cleaning
Source: Wang, et al., Journal of membrane science, 2014, 468: 276-307.
  A variety of backwashing frequencies and durations are used in MBRs.
  less frequent and longer backwashing (7-16 min filtration/30-60 s backwashing)
  more frequent and shorter backwashing (5-12 min filtration/5-20 s backwashing).
Vibration
Physical cleaning — Backwashing, relaxation
Backwashing
Biological Wastewater Treatment
Online Course Series

## Slide 11: Membrane cleaning
Source: Wang, et al., Journal of membrane science, 2014, 468: 276-307.
  Relaxation allows diffusive back transport of foulants away from membrane surfaces driven by a concentration gradient, and is often carried out in conjunction with aeration scouring to enhance the diffusion
Relaxation
Vibration
Physical cleaning — Backwashing, relaxation
Biological Wastewater Treatment
Online Course Series

## Slide 12: Membrane cleaning
Source: Zhang, et al., Journal of Membrane Science, 2021, 639: 119751.
Ultrasonic transducer
Ultrasonic transducer
Reactor
Reactor
Ultrasonic transducer
Reactor
Horn
Intermediate liquid
  Ultrasonic cleaning is effective in alleviating the concentration polarization and removing the cake layers on the membrane
  Advantage
  No chemical reagents
  Not interrupting the filtration process
  Key parameters
  Ultrasonic frequency
  Power density, and duration
Physical cleaning — Ultrasonic cleaning
Biological Wastewater Treatment
Online Course Series

## Slide 13: Membrane cleaning
Physical cleaning — Vibration / Rotation
Vibration and rotation of membranes can normally generate high shear or turbulence at the membrane surface, which can enable online cleaning of fouled membranes.
Biological Wastewater Treatment
Online Course Series

## Slide 14: Membrane cleaning
Chemical cleaning
CHEMICAL
PHYSICAL
BACKFLUSHING
BASE
CHEMICALLY
ENHACED
BACKWASH
with air
without air
RELAXTION
Caustic soda
Citric/oxalic
ACIDS
hydrochloric / sulphuric
Citric / oxalic
Oxidant
  Enhanced removal of stubborn foulants
  Targeted cleaning
  Cost-effective
  Prevents irreversible fouling
  Improved system efficiency
Biological Wastewater Treatment
Online Course Series

## Slide 15: Membrane cleaning
Source: Wang, et al., Journal of membrane science, 2014, 468: 276-307.
Biological Wastewater Treatment
Online Course Series
Chemical cleaning — Cleaning in place (CIP)
CIP is designed to maintain membrane permeability and reduce the frequency of offline cleaning
CIP is usually carried out at intervals of between 1 and 6 weeks in MBRs
The most common duration for such maintenance cleaning is 1-3 h
The prevalent cleaning reagent (NaOCl and citric acid) concentrations for CIP are 300-2,000 mg/L and 0.2-1.5 wt %

## Slide 16: Membrane cleaning
Source: Beswick M. University of British Columbia, 2017.
Chemical cleaning — Chemically enhanced backflush (CEB)
CEB adding a low concentration of cleaning
agents into the backflush water, the cleaning
efficiency of backflushing is enhanced
It is performed less frequently than normal physical backwashing, but more often compared to regular CIP
CEB can be carried out daily or up to every 7-14 d, but usually on a daily basis
The typical concentration for CEB using NaOCl is in the range of 100-500 mg/L
Biological Wastewater Treatment
Online Course Series

## Slide 17: Membrane cleaning
Source: Tian, et al., Environmental Science & Technology, 2022. 56, 17, 12563–12572; Tian, et al., Journal of Membrane Science, 2023, 669:121325
Chemical cleaning — Recovery cleaning
Transformation from “irrecoverable” to “recoverable”
  Remove irrecoverable foulants
  Prolong the service life of membranes
  Facilitating sustainable wastewater treatment
Biological Wastewater Treatment
Online Course Series

## Slide 18: Membrane cleaning
In the Future
Nevertheless, changes or damage to membranes caused by long-term chemical cleaning is unavoidable.
With respect to CIP and CEB, microbial activities and bulk sludge can also be impacted by the chemical reagents during membrane cleaning.
The waste stream should be paid more attention and especially the overdosing of cleaning chemicals should be avoided.
Biological Wastewater Treatment
Online Course Series

## Slide 19: Membrane cleaning
Fluidized GAC particles
Foulants
Adsorbent
Foulants
Coagulated particles
Membrane module
Distributor
Source: Wang, et al., Journal of Membrane Science, .2020. 595, 117570
Improving the filterability of mixed liquor
  PAC can not only adsorb biomolecules in the sludge, but also acts as a carrier for biomass growth and it reduces floc breakage
  The charge neutralization and bridging of coagulants, addition of an optimum coagulant concentration can induce lower SMP concentration, lower hydrophobicity, and better flocculation, which results in decreases in cake resistance and pore blocking
Morphology of the mesh
Fresh membrane module
Formation of dynamic membrane by foulant particles
Biological Wastewater Treatment
Online Course Series

## Slide 20: Other control methods
Source: Lee, et al., Environmental Science & Technology, 2016, 50(4), 1788-1795; Cui, et al., Water Science and Technology, 2021, 83(11): 2597-2614.
Biological methods
Quorum quenching
  QQ-based biological control method can prevent cell-cell or membrane-cell interactions in three possible ways
  disturbance of synthesis of QS signals or AIs
  degradation of QS signals or AIs
  interdiction of transport or acceptance of QS signals or AIs
  The bacteria on membranes can secrete molecules called quorum sensing (QS) signals or autoinducers (AIs) that can regulate their population densities and biofilm formation
Biological Wastewater Treatment
Online Course Series

## Slide 21: Other control methods
Source: Ham, et al., Chemosphere, 2021, 268: 128802.
Biological methods
protozoans and metazoans
Protozoans and metazoans, which are the major consumers of bacteria and ubiquitously occur in wastewater treatment plants, are very significant for fouling control
The movement of such worms leads to the formation of porous and spongelike structures of bio-cake
Biological Wastewater Treatment
Online Course Series

## Slide 22: Other control methods
Source: Hawari, et al., Journal of Environmental Science, 2015, 29, 139-145; Zhang, et al., Chemical Engineering Journal, 2015.273, 223-230.
Electrically‐assisted approaches
The electrocoagulation process can generate metal cations as a result of the electro-dissolution of soluble anodes made of aluminum or iron
charge neutralization and sorption of SMP and EPS
chemical oxidation of SMP and EPS
The electrophoresis (EP) induced by an
electric field yields an electric repulsive force between foulants and membranes
Feed
Biomass
Membrane
Electrodes
ac~o
Permeate
FDEP
FDEP
FDEP
Biological Wastewater Treatment
Online Course Series

## Slide 23: Other control methods
Potential fouling mitigation using nanomaterials‐based membranes
An interfacial hydration layer is produced on the membrane surface as a result of the interaction between hydrophilic hydrogen forming functional groups and the surrounding water molecules, which prevents the attachment of the foulants on the membrane surface.
Hydrophilic water soluble polymers are used as additives to improve the surface hydrophilicity
Biological Wastewater Treatment
Online Course Series

## Slide 24: Other control methods
Source: Qu, et al., Water Research, 2013, 47(12): 3931-3946.
Potential fouling mitigation using nanomaterials‐based membranes
Engineered nanomaterials (ENMs) possess distinguishing characteristics such as antimicrobial ability and hydrophilicity, thus resulting in multifunctional effects to alleviate membrane fouling
graphene oxide (GO)
reduced graphene oxide (rGO)
nanoparticles (Cu NPs)
silver nanoparticles (Ag NPs)
titanium dioxide nanoparticles (TiO2 NPs)
oxide nanoparticles (ZnO NPs)
Biological Wastewater Treatment
Online Course Series