## Slide 1
Course on Sulphur-based Wastewater Treatment
Introduction
Guanghao Chen
Di Wu

## Slide 2: Sulphur is a vital element for life
Sulphur is widely transformed and translocated via biological and chemical reactions in the biosphere.
It mainly in the form of
  Sulphur-containing amino acids (1% wt./dry wt.) in cells.
  Gypsum (CaSO4), metal sulphides (FeS2) in rocks and sediments (7,800·1018 gS), and
  Sulphate in seawater (1,280·1018 gS)
  …
Source: Muyzer and Stams (2008). Nature Reviews Microbiology, 6(6), 441-454.
Notes: Sulphur, the least common of the five macro-elements in the biosphere, is widely transformed and translocated via biological and chemical reactions in the biosphere.
It presents mainly in the form of
- mercapto groups in sulphur-containing amino acids (1 % wt./dry wt.) in cells.
- gypsum (CaSO4), metal sulphides (FeS2) in rocks and sediments (about 7,800 trillion metric tonnes sulphur),
- and sulphate in seawater (about 1,280 trillion metric tonnes sulphur).
Notably, large quantities of sulphur are emitted into the environment through natural processes such as seawater intrusion and volcanic eruption, as well as through industrial production.

## Slide 3: Sulphur pollution
Both natural and human-made ecosystems have increasingly suffered from sulphur pollution.
The detrimental impacts of sulphur pollution, including
  acid rain, odours from polluted rivers, landfills, or treatment systems, corrosion of steel and concrete, the release of heavy metals and acidity from oxygen-exposed sediments and mineral ores
Sulphate-laden wastewater is produced by various industries
  such as farming, flue-gas desulphurization (FGD) at power stations, pulp and paper-making, brewing, pharmaceutical, food production, fish farming, tanning, and petrochemical and mining industries.
Source: DOI:10.4236/ojce.2015.54038
Source: https://www.biocycle.net/managing-odors-in-organics-recycling/
Source:greenworld2010.blogspot.com
Source: https://en.wikipedia.org/wiki/Acid_mine_drainage
Notes: Over the recent decades, both natural and human-made ecosystems have increasingly suffered from sulfur pollution.
Typical forms of sulfur pollution include:
- Acid rain,
- odors from polluted rivers, landfills, or treatment systems,
- corrosion of steel and concrete,
- and the release of heavy metals and acidity from oxygen-exposed sediments and mineral ores.
Sulphate-laden wastewater is produced by various industries, such as farming, flue-gas desulphurization (FGD) at power stations, pulp and paper-making, brewing, pharmaceutical, food production, fish farming, tanning, and petrochemical and mining industries.

## Slide 4: Reducing sulphur-induced pollution
Significant efforts have recently been directed towards reducing sulphur-induced pollution.
It is estimated that the costs associated with sulphur-induced treatment account for 2% to 3% of global GDP (Kruger 2011; www.Clarity.io)
Managing sulphate-reducing bacteria (SRB) is crucial for addressing these issues
  → nevertheless, no effective methods exist to prevent sulphate reduction
Source:
Kruger et al., 2011. Wiley, Hoboken, NJ, USA; https://www.clarity.io/blog/a-deep-dive-economic-impacts-of-air-pollution
Example:
Notes: Significant efforts have recently been directed towards reducing sulfur-induced pollution.
It is estimated that the costs associated with sulfur-induced treatment account for 2% to 3% of global GDP.
Managing sulfate-reducing bacteria (SRB) is crucial for addressing these issues.
However, despite over fifty years of research and development, it has been conclusively determined that no effective methods exist to prevent sulfate reduction in anaerobic treatments (Lens et al., 1998). Attempts to selectively inhibit SRB using molybdate, transition elements, or antibiotics have failed in full-scale applications.

## Slide 5: Sulphur-based biotechnologies
Alternatively, a variety of environmental technologies that utilize sulphur cycle conversions has been developed, particularly for the treatment of sulphur-laden wastewater
Such as:
Biogenic sulphide processes for removing heavy metals from metal-laden wastewater and acid mine drainage (AMD) and biological desulfurization of natural gas, flue gas, and liquefied petroleum gas.
Elemental sulphur-dosed post-denitrification methods through induced autotrophic denitrification have recently been developed to improve total nitrogen (TN) removal.
Huisman et al., 2006. Hydrometallurgy 83, 106-113.
Cui et al., 2019. Applied Microbiology and Biotechnology 103, 6023-6039.
Notes: Alternatively, a varietly of environmental technologies that utilize sulfur cycle conversions has been developed, particularly for the treatment of sulphur-laden wastewater
alternative bioprocesses and biotechnologies involving SRB have been under development, such as biogenic sulfide processes for removing heavy metals from metal-laden wastewater and acid mine drainage (AMD) using technologies like THIOTEQ and SULPHATEQ, and biological desulfurization of natural gas, flue gas, and liquefied petroleum gas (Hao, 2014).
In treatment of domestic wastewater, elemental sulphur-dosed post-denitrification methods through induced autotrophic denitrification have recently been developed to improve total nitrogen (TN) removal (e.g. sulphur: the limestone autotrophic denitrification (SLAD) process) (Zhang and Lamphe, 1999). Such organic independent autotrophic denitrification is particularly attractive when retrofitting and upgrading existing wastewater treatment plants (WWTPs) treating carbon-deficient domestic wastewater that is typical in developing nations

## Slide 6: SANI® process
Moreover, a new biological wastewater treatment process, namely the sulphate reduction, Autotrophic denitrification, Nitrification Integrated (SANI®) process has been developed recently.
The concept of this novel biological treatment process builds on sulphate  sulphide  sulphate conversion-mediated organic carbon (C) and nitrogen (N) removal, which moves C and N removal integration into C, N, and S removal integration.
Notes: The novelty of this sulphur-based biological treatment system lies in the use of sulphidogenic bacteria, i.e. sulphate-reducing bacteria (SRB) for carrying out sulphidogenesis (sulphate reduction).
In this anaerobic reaction, sludge production becomes minimal because 96 % of organics can be theoretically converted into CO2 according to the process reaction chemistry and electron balance analysis.
The dissolved sulphide produced offers adequate electron donors driving the autotrophic denitrification reaction without organic carbon, producing minimal sludge as compared with a heterotrophic denitrification reaction which receives electrons from organic carbon. Integration of these two sulphur-based bioprocesses, the sulphate-reducing bioprocess and the sulphide-oxidizing (autotrophic denitrification) bioprocess, forms the SANI® process.

## Slide 7
As the first sulphur-based biological treatment process for mainstream wastewater treatment, the SANI® process has been developed to deal with saline wastewater with sludge being significantly minimized.
More importantly, the SANI® process offers an opportunity to use seawater for toilet flushing as an economic water resource for water-scarce populous coastal cities and islands. It could also assist in the energy-efficient treatment of sulphur-laden industrial wastewaters for nutrient removal.
Liu et al., 2016. Engineering 2, 460-469;
Zhang et al, 2023. Environmental Science & Technology 57, 5068-5078.
Ali et al, 2022. Water Reuse 12, 346.

## Slide 8: Sulphur-based Wastewater Treatment Course
This course offers an in-depth exploration of sulphur-based wastewater treatment technology, designed to equip participants with a thorough understanding of both fundamental principles and advanced applications in this field.
Upon successful completion of this course, you will be able to:
Biological sulphate reduction
Sulphur-driven autotrophic denitrification
Sulphur bioprocess for wastewater treatment
Chemical and biochemical sulphur cycle
Resource recovery from sulphur-based processes
Notes: This course offers an in-depth exploration of sulfur-based wastewater treatment technology, designed to equip participants with a thorough understanding of both fundamental principles and advanced applications in this field. The curriculum is structured to provide a comprehensive overview, practical insights, and the theoretical knowledge required to design, assess, and evaluate sulfur-based treatment systems effectively.
Upon successful completion of this course, you will be able to:
Explain the microbiological pathways, identify key microorganisms, and understand the critical factors in biological sulphate reduction (BSR), along with designing a standard BSR process.
Outline the biochemical reactions, pinpoint key microorganisms, and describe the main parameters of sulphur-driven autotrophic denitrification (SdAD), as well as design a typical SdAD process.
Identify resources recoverable from sulphur-based processes and design standard technology for sulphur-based resource recovery.
Discuss the use of sulphur biotechnology in wastewater treatment and utilize steady-state modelling tools for designing a SANI process.