## Slide 1
Course on Sulphur-based Wastewater Treatment
The Sulphur Cycle
Guanghao Chen
Di Wu

## Slide 2: The chemical sulphur cycle
http://dx.doi.org/10.5194/acpd-15-23931-2015

## Slide 3: The chemical sulphur cycle
Sulphur is a crucial element for both life and industry.
Despite making up only 0.07 wt% of the Earth's crust, substantial deposits of elemental sulphur and various sulphur-containing minerals (e.g., FeS2, PbS, ZnS, HgS, CuFeS2, Cu2S) are found.
Notes: Sulphur is a crucial element for both life and industry. Despite making up only 0.07 wt% of the Earth's crust, substantial deposits of elemental sulphur and various sulphur-containing minerals (for example, pyrite (FeS2), galena (PbS), zinc-blende (sphalerite) (ZnS), cinnabar (HgS), chalcopyrite (CuFeS2), and chalcocite Cu2S)) are found,

## Slide 4
Sulphur compounds are essential components of all organisms, and thus are present in all biomass and materials derived from these sources, such as wood, peat, coal, crude oil, and their derivatives.
The combustion of these materials releases sulphur dioxide (SO2) along with traces of carbonyl sulphide (COS). Plants assimilate COS as part of their sulphur metabolism.
Source: Atmospheric Research 260, 2021, 105709
The chemical sulphur cycle
Notes: Sulphur compounds are essential components of all organisms, and thus are present in all biomass and materials derived from these sources, such as wood, peat, coal, crude oil, and their derivatives.
The combustion of these materials releases sulphur dioxide (SO2) along with traces of carbonyl sulphide (COS). Plants assimilate COS as part of their sulphur metabolism.

## Slide 5: The chemical sulphur cycle
Dimethyl sulphide (DMS) is released in large quantities by phytoplankton in the oceans, while volcanoes emit hydrogen sulphide (H2S), SO2, and carbon dioxide (CO2).
In anoxic environments such as ponds, lakes, and coastal waters, sulphate reduction by ubiquitous sulphur bacteria also produces H2S.
Source:
PNAS. doi:10.1073/ pnas.1317120111
Annual Review of Ecology Evolution and Systematics 47(1):239-262
mSystems: https://doi.org/10.1128/msystems.00201-23
Notes: Dimethyl sulphide (DMS) is released in large quantities by phytoplankton in the oceans, while volcanoes emit hydrogen sulphide (H2S), SO2, and carbon dioxide (CO2).
In anoxic environments such as ponds, lakes, swamps, and coastal waters, sulphate reduction by ubiquitous sulphur bacteria also produces H2S. The human body contains 2 g of sulphur per kg, equating to 140 g for a person weighing 70 kg.

## Slide 6: oxidation, reduction and catenation
Sulphur chemistry is complex due to its numerous oxidation states
Source: http://iwaponline.com/ebooks/book-pdf/776070/wio9781789060966.pdf
Table - The oxidation states of sulphur atoms in common compounds.
Table - Ring sizes and chain-lengths n in sulphur-rich compounds.
The chemical sulphur cycle:
Notes: Sulphur chemistry is complex due to its numerous oxidation states. Sulphur atoms and ions can adopt coordination numbers ranging from 1 to 8, with oxidation states varying from -2 to +6. This table illustrates the nine typical oxidation states of sulphur. Most of these states play a role in aqueous systems where redox reactions occur, either as a result of microbiological activity or through non-enzymatic reactions following the system's thermodynamics.
Sulphur atoms can form two covalent bonds with other atoms or with themselves to create chain-like structures –S–S–S– of virtually unlimited length. These chains may be terminated by single atoms like H or Cl, by groups such as CH3 or SO3H, by ions like S, or they may loop back on themselves to form rings of various sizes. These examples are detailed in the Table. This Table presents values of n which have been determined in compounds isolated in pure form or detected in mixtures using high-performance liquid chromatography (HPLC), proton nuclear magnetic resonance (1H-NMR) spectroscopy, or ion chromatography. These findings suggest that there seems to be no upper limit to the values of n, although the synthesis of higher molecular weight species becomes increasingly challenging as their solubility and thermal stability decrease with higher values of n. Polymeric sulphur (PolyS) is insoluble in all solvents, except liquid sulphur, and is therefore considered to consist of very long chains and/or very large rings. However, prolonged extraction of PolyS with carbon disulphide at room temperature results in slow depolymerization, dissolving the polymer into a mixture of small homocycles such as S6, S7, and S8.

## Slide 7: Sulphuric acid and sulphates
H2SO4 is produced industrially on an enormous scale by catalytic oxidation of SO2 with air followed by dissolution of SO3 in H2SO4 to give polysulphuric acids H2SnO3n+1 which are subsequently diluted by water to sulphuric acid of desired concentration.
The sulphate anion is rather inert chemically and needs to be activated for biological reduction at ambient temperature
Sulphate Sulphate

## Slide 8
At ambient pressure and temperature, the element sulphur exists as many allotropes.
Each allotrope often exists in polymorphs (different crystal structures of the same covalently bonded Sn molecules) delineated by Greek prefixes (α, β, etc.).
S8 is the main constituent of most commercial samples of elemental sulphur; it can be prepared in pure form by recrystallization of commercial sulphur .
Cyclo-Sn
(n = 9–15, 18, 20)
Cyclo-heptasulphur
cyclo-S7
Cyclo-hexasulphur
cyclo-S6
Cyclo-octasulphur
cyclo-S8
Elemental sulphur and hydrophobic sulphur sols: sulphur allotropes
Notes: α-Sulphur
α-Sulphur is the form most commonly found in nature.[4] When pure it has a greenish-yellow colour (traces of cyclo-S7 in commercially available samples make it appear yellower). It is practically insoluble in water and is a good electrical insulator with poor thermal conductivity. It is quite soluble in carbon disulphide: 35.5 g/100 g solvent at 25 °C. It has an orthorhombic crystal structure.[4] α-Sulphur is the predominant form found in "flowers of sulphur", "roll sulphur" and "milk of sulphur".[19] It contains S8 puckered rings, alternatively called a crown shape. The S–S bond lengths are all 203.7 pm and the S-S-S angles are 107.8° with a dihedral angle of 98°.[16] At 95.3 °C, α-sulphur converts to β-sulphur.[4]
β-Sulphur
β-Sulphur is a yellow solid with a monoclinic crystal form and is less dense than α-sulphur. It is unusual because it is only stable above 95.3 °C; below this temperature it converts to α-sulphur. β-Sulphur can be prepared by crystallising at 100 °C and cooling rapidly to slow down formation of α-sulphur.[5] It has a melting point variously quoted as 119.6 °C[20] and 119.8 °C but as it decomposes to other forms at around this temperature the observed melting point can vary. The 119 °C melting point has been termed the "ideal melting point" and the typical lower value (114.5 °C) when decomposition occurs, the "natural melting point".[20]

## Slide 9
J. Am. Chem. Soc. 2022, 144, 1, 5–22
Liquid elemental sulphur is an industrial product of outstanding importance, being produced on a huge scale (>53 million tons annually).
It is used mainly for the manufacture of sulphuric acid but after solidification also for rubber vulcanization and the production of numerous sulphur compounds.
Elemental sulphur and hydrophobic sulphur sols: liquid sulphur
Molten sulphur Sulphur plastics
Notes: Sulphur vapor may exist either in equilibrium with solid and/or liquid sulphur (saturated vapor) or as a single phase at pressures lower than the saturation pressure (unsaturated vapor).
At temperatures of up to 1000°C saturated sulphur vapors consist of all molecules Sn with n ranging from 2 to 8 which are in equilibrium with each other (Rau et al., 1973).

## Slide 10
https://www.usgs.gov/media/images/fumarole-k-lauea-hawai-i-elemental-sulphur-vapor-escaping
Sulphur vapor may exist either in equilibrium with solid and/or liquid sulphur (saturated vapor) or as a single phase at pressures lower than the saturation pressure (unsaturated vapor).
At temperatures of up to 1,000°C saturated sulphur vapours consist of all molecules Sn with n ranging from 2 to 8 which are in equilibrium with each other (Rau et al., 1973).
Elemental sulphur and hydrophobic sulphur sols: gaseous sulphur
Notes: Liquid elemental sulphur is an industrial product of outstanding importance, being produced on a huge scale (>53 million tons annually). It is used mainly for the manufacture of sulphuric acid but after solidification also for rubber vulcanization and the production of numerous sulphur compounds.
Sulphur vapor may exist either in equilibrium with solid and/or liquid sulphur (saturated vapor) or as a single phase at pressures lower than the saturation pressure (unsaturated vapor).
At temperatures of up to 1000°C saturated sulphur vapors consist of all molecules Sn with n ranging from 2 to 8 which are in equilibrium with each other (Rau et al., 1973).

## Slide 11
All allotropes of sulphur are practically insoluble in water at 20°C.
Sulphur is a hydrophobic material – sulphur sols are termed hydrophobic or Weimanrn sulphur sols.
They have a milky-white appearance when freshly prepared and consist of tiny droplet of liquid sulphur dispersed in the aqueous phase.
Liquid sulphur → Crystalized sulphur droplets
Steudel R. (1996) Chemie in unserer Zeit, 30, 226–234
Elemental sulphur and hydrophobic sulphur sols:
S sols from elemental S
Notes: Steudel R. (1996) Chemie in unserer Zeit, 30, 226–234

## Slide 12
H2S (b.p. −60°C) is a colorless, extremely poisonous, noxious gas. The maximum allowed concentration of H2S at a workplace is only 10 ppmv.
H2S is a component of certain wastewater and waste gases. H2S is present in volcanic exhalations and is abundant in the water existing from hydrothermal vents on ocean fools.
H2S is most conveniently prepared from ionic metal sulphides by protonation of the anions with dilute acids under anoxic conditions. In anaerobic aqueous environments, H2S may be formed by sulphate-reducing bacteria.
Sulphides and polysulphides:
hydrogen sulphide and
sulphide ions

## Slide 13
Figure - Pourbaix diagram for sulphur in water at 25°C and 1.013 bar with the sum of the activities of all sulphur-containing ions equal to 0.1 mM.
The solubility of H2S in water at 20°C is only 0.40 g/100 g H2O (0.12 M) at a total pressure (H2S + H2O) of 1.013 bar. (The solubility decreases with increasing temperature)
In aqueous solution, the very weak acid H2S is only partly deprotonated depending on the pH value:
  H2S + H2O [H3O]+ + HS− K1 = 1.0·10−7 (20oC)
  HS− + H2O [H3O]+ + S2− K2 = 10−14 to 10−17 (20oC)

## Slide 14
Figure - Pourbaix diagram for sulphur in water at 25°C and 1.013 bar with the sum of the activities of all sulphur-containing ions equal to 0.1 mM.
The reactions of ‘sulphide’ in water at pH values up to 12 are practically the reactions of either H2S or of the hydrogen sulphide ion HS–. In a solution of pH = 7 with 1 mM total sulphide, the molar ratio HS–/H2S is 1:1 while at pH = 10 practically all sulphide is present as HS–.
Hydrogen sulphide ions react with certain metal cations to form insoluble sulphides, e.g. the black iron (II) sulphide FeS:
  Fe2+ + HS- FeS + H+

## Slide 15
Sulphide and polysulphides:
polysulphides and polysulphanes
Alkaline sulphide solution dissolve elemental sulphur with the formation of chain-like polysulphide anions which form equilibrium mixtures of many molecular sizes:
HS− + S8 [H−S−S7−S]− H+ + [S9]2−
HS− + [S9]2− H+ + 2[S5]2− HS− + [S5]2− H+ + 2[S3]2− [S9]2− + [S5]2− 2[S7]2−
Aqueous polysulphide solutions are subject to rapid autoxidation when exposed to air
+
Figure source: Chem. Soc. Rev., 2019, 48, 3279-3319
Notes: Alkaline sulphide solution dissolve elemental sulphur with the formation of chain-like polysulphide anions which form equilibrium mixtures of many molecular sizes
These reversible reactions strongly depend on the pH and on the total sulphur concentration. Low pH values result in the formation of H2S and precipitation of elemental sulphur, whereas very high pH values favor shorter chains over longer polysulphide anions. Polysulphide anions can therefore exist in water only at pH>6.
Both HS− and S2− anions are strong nucleophiles (Lewis bases) which are capable of opening S8 rings and which tend to also cleave the S–S bonds of chain-like species.
Elemental sulphur is produced only if the average sulphur content x of the polysulphide solution is larger than 2.
Thiosulphate is usually a component of aqueous and non-aqueous polysulphide solutions but also of solid polysulphides exposed to air.

## Slide 16
Sulphide and polysulphides:
oxidation of sulphide and
polysulphide ions by metal ions
The removal of sulphide ions from aqueous solutions by oxidation to elemental sulphur is one of the most important desulphurization processes. This process can be achieved either chemically or microbiologically (i.e. enzymatically).
In both cases transition metal complexes are involved. The metal ion must be able to exist in at least two oxidation states between which it can shuttle back and forth. Suitable metal ions are, for instance, iron(III/II), copper(II/I), manganese(IV/III/II), and vanadium (V/IV).
HS− + 2Mn+ S8 + H+ + 2M(n−1)+ (M: any redox-active metal)

## Slide 17
Sulphur dioxide, sulphite
and disulphite ions
Sulphur dioxide is one of the most important chemicals in industry since it is an intermediate in the large-scale production of sulphuric acid.
Combustion of coal, crude oil, diesel oil, heating oil, gasoline, and wood also generates SO2 since all solid and liquid fossil fuels contain sulphur compounds. Therefore, power plants using fossil fuels must have a flue gas desulphurization unit usually based on scrubbing of the flue gas by an aqueous slurry of Ca[OH]2 or Ca[CO3] producing gypsum Ca[SO4]·2H2O or by a solution of Na2(SO3) resulting in Na(HSO3) from which the SO2 can be recovered by heating.
Sulphite solutions are strong reducing agents that are oxidized by dioxygen, iron(III) salts or iodine to sulphate. In alkaline solution, the autoxidation is particularly fast. In practice, the reaction is strongly catalyzed by even traces of metal cations such as Cu2+, Mn2+, Fe3+ and Co2+ some of which are present in most aqueous systems.
https://www.thermaxglobal.com/air-pollution-control/flue-gas-desulphurization/

## Slide 18
Sulphur dioxide, sulphite
and disulphite ions
Enormous amounts of sulphur compounds are constantly emitted into the atmosphere from natural sources, mainly dimethyl sulphide Me2S (DMS, ca. 4·107 t/a) from the oceans. DMS is produced by phytoplankton (floating microorganisms) and is oxidized in air to SO2 and methane sulphonic acid MeSO3H (MSA).
The oxidation of DMS in the atmosphere is complex due to several parallel reaction channels. Ultimate products are MSA, SO2 , and sulphuric acid while dimethyl sulphoxide (DMSO) and dimethyl sulphone (DMSO2) are intermediates.
CH3−S(OH)−CH3 CH3−S−CH3 + OH [CH3−S−CH2] + H2O
Figure source: Environ. Sci. Technol. 2022, 56, 19, 13931–13944

## Slide 19
Thiosulphates and
thiosulphuric acid
Sodium thiosulphate is produced commercially by refluxing a concentrated aqueous Na2[SO3] solution with elemental sulphur:
Na2[SO3] + Na2[S2O3] (Nucleophilic displacement reactions)
In acidic solution, the ions [HS2O3]− and [S2O3]2− react with exchange of sulphur atoms to give a mixture of sulphane monosulphonate ions resulting in the growth of a chain of sulphur atoms (the dianions attack the monoanions):
[HS2O3]− + [S2O3]2− [HS3O3]− + [SO3]2−
[HS3O3]− + [S2O3]2− [HS4O3]− + [SO3]2−
After the sulphur chain of the anions [HSnO3]- has reached a length of at least 7, 8 or 9 atoms, the cyclic molecules S6, S7 and S8 can be split off.
[H−Sn−SO3] cyclo−Sn + [SO3H]- （n>5)
Figure source: Z. Anorg. Allg. Chem. 2018, 644, 574–579
Notes: This process is another example for a whole series of nucleophilic displacement reactions. The nucleophile [SO3]2− first attacks an S8 molecule with ring opening and initial formation of a chain-like sulphane monosulphonate dianion [S–S7–SO3]2−.
This ion is rapidly attacked by other sulphite ions with stepwise formation of thiosulphate ions until the sulphur chain has been turned into eight thiosulphate anions with one S–S bond each. Thus, the number of these bonds stays constant. According to photoelectron spectroscopy the oxidation states of the sulphur atoms in the thiosulphate anion are −2 and +6.

## Slide 20
Polythionates and
polythionic acids
Polythionates with anions of the type [O3S–Sn–SO3]2- are known as polysulphane disulphonates.
    Trithionate: SCl2 + 2[HSO3]− [S3O6]2− + 2HCl
    Tetrathionate: 2[S2O3]2− + I2 [S4O6]2− + 2I−
    Pentathionate: SCl2 + 2[HS2O3]− [S5O6]2− + 2HCl
    Hexathionate: S2Cl2 + 2[HS2O3]− [S6O6]2− + 2HCl
Polythionate salts are water soluble and metastable at acidic pH values, can only exist at acidic pH values and in the absence of strong nucleophiles and reducing agents. Strong oxidizing agents such as hydrogen peroxide or elemental chlorine convert polythionates into sulphate.
Polythionic acid

## Slide 21
Organic derivatives of the type R–Sn–R (organopolysulphanes)
Polysulphanes R2Sn are often termed polysulphides although they are not ionic materials such as sodium polysulphides, for instance. The recommended nomenclature for R–Sn–R is polysulphanes.
The widespread natural occurrence of tri- and higher polysulphanes with organic substituents has been recently demonstrated.