## Slide 1
Course on Sulphur-based Wastewater Treatment
Sulphate-reducing Bioprocesses
Guanghao Chen
Di Wu
Notes: For this chapter, we gather to discuss a topic of utmost importance in the field of wastewater treatment.
The transition from passive treatment to carbon- and energy-neutral treatment, while simultaneously recovering valuable resources.

## Slide 2
Sulphur-reducing bioprocess
Fundamentals
Key microorganisms driving sulphate reduction
Electron donors for sulphate-reducing bioprocess
Application
Factors affecting sulphate reduction

## Slide 3: Sulphate-reducing pathways
https://www.agqlabs.us.com/sulphates-in-the-water-source/
Notes: sulphate present in the ocean and other water bodies can undergo rapid biological conversions mediated by SRB that are ubiquitous in natural and engineered environments. SRB use oxidized forms of sulphurs (e.g. mainly elemental sulphur (S0), thiosulphate (S2O32-), and sulphate (SO42−)) as electron acceptors and sulphide as the end product (Muyzer and Stams, 2008).

## Slide 4: Sulphate-reducing pathways
SRB can grow on organic matter, e.g. acetate (CH3COO-), pyruvate, lactate and propionate, while energy was conserved mainly or exclusively via substrate-level phosphorylation.
SRB can also proliferate with hydrogen (H2) as the electron donor and SO42− as the electron acceptor in demonstration of the electron transport phosphorylation in the metabolism of SRB.
Alkylbenzene sulphonates, dimethylsulphoxide, NO3-, NO2-, iron (III), oxygen, fumarate, acrylate, arsenate, chromate, and uranium also can be electron acceptors for SRB.
Notes: SRB at one time were believed to be capable of growing only on organic matter, e.g. acetate (CH3COO-), pyruvate, lactate and propionate, while energy was conserved mainly or exclusively via substrate-level phosphorylation (see Eq. 7.1).
However, Badziong and Thauer (1978) reported that Desulphovibrio vulgaris proliferates with hydrogen (H2) as the electron donor and SO42− as the electron acceptor in demonstration of the electron transport phosphorylation in the metabolism of SRB for the first time (see Eq. 7.2).
As well as oxidized sulphur species, other competent electron acceptors for SRB are alkylbenzene sulphonates, dimethylsulphoxide, NO3-, NO2-, iron (III), oxygen, fumarate, acrylate, arsenate, chromate, and uranium (Rabus et al., 2013).

## Slide 5: Sulphate-reducing pathways
Considering the significance of biological sulphur conversion in environmental engineering, it is advisable to define the sulphate reduction in assimilatory and dissimilatory categories.
Before sulphur compounds can be assimilated into biosynthetic pathways, they need to be reduced to hydrogen sulphide (H2S).
The pathways catalysing the reduction of sulphate to sulphide for the purpose of incorporation into synthesized molecules are named the ‘pathways of assimilatory sulphate reduction’, whereas the pathways for the purpose of energy production are referred to as ‘pathways of dissimilatory sulphate reduction’.
Notes: Considering the significance of biological sulphur conversion in environmental engineering, it is advisable to define the sulphate reduction in assimilatory and dissimilatory categories.
Before sulphur compounds can be assimilated into biosynthetic pathways, they need to be reduced to hydrogen sulphide (H2S).
The pathways catalysing the reduction of sulphate to sulphide for the purpose of incorporation into synthesized molecules are named the ‘pathways of assimilatory sulphate reduction’, whereas the pathways for the purpose of energy production are referred to as ‘pathways of dissimilatory sulphate reduction’.

## Slide 6: Sulphate-reducing pathways – assimilatory sulphate reduction
Sulphate uptake and its incorporation in many biological systems.
Notes: sulphate uptake is accomplished through active transport mediated by a carrier enzyme system. The cellular metabolism of sulphate begins with a series of activation reactions; the reduction of sulphate to sulphite requires two electrons at a standard redox potential (E0') of -516 mV, which is higher than the physiological electron carriers (Thauer et al., 1977).
In this case, sulphate pro-actively participates in the formation of adenosine 5'-phosphosulphate (APS) or 3'-phosphoadenylyl-sulphate (PAPS). In many bacteria and lower eukaryotes, assimilatory sulphate reduction proceeds via activation of sulphate to APS by the enzyme of sulphate adenylyltransferase (i.e. ATP sulphurylase). Subsequently, three pathways proceed with the sulphite reduction (see Figure 7.2). The first pathway is in enteric bacteria, e.g. cyanobacteria and yeast; the produced APS is phosphorylated to generate PAPS, which is catalysed by the adenylyl-sulphate kinase (APS kinase), and the generated PAPS is then reduced to sulphite with the assistance of thioredoxin (or glutaredoxin)-dependent phosphoadenylyl-sulphate reductase (thioredoxin) (PAPS reductase), and finally a reduction of sulphite to sulphide, catalysed by the assimilatory sulphite reductase (NADPH). The second pathway is that enzymes of adenylyl-sulphate reductase (glutathione) and adenylyl-sulphate reductase (thioredoxin) catalyse the second step, i.e. direct reduction of APS to sulphite, and subsequently NADPH is used as an electron donor (for most bacteria) with the catalysis of plant sulphite reductases and the enzyme from Allochromatium vinosum to reduce sulphite to sulphide; in bacteria and plants sulphide is finally incorporated into O-acetyl-L-serine by cysteine synthase yielding L-cysteine and later converting L-methionine, which are the two major sulphur-containing precursor compounds. The third pathway is that a thioredoxin-dependent enzyme catalyses the direct reduction of APS to sulphite. Pathways 2 and 3 share similar procedures except for the APS reduction enzyme. In both of these pathways, sulphite is reduced to sulphide by the action of assimilatory sulphite reductase (ferredoxin) viz. a ferredoxin-dependent enzyme and a NADPH-dependent enzyme (Lillig et al., 2001).

## Slide 7: Sulphate-reducing pathways – dissimilatory sulphate reduction
Dissimilatory sulphate reduction (Dsr) is performed by prokaryotes (such as Archaeoglobi, Proteobacteria, Firmicutes, Nitrospirae and others)
Dsr can be considered as two phases:
  firstly, the reduction of sulphate to bisulphite through the intermediate compound APS, and
  secondly, the reduction of bisulphite to sulphide.
Notes: As one of the most common electron acceptors for anaerobic respiration, dissimilatory sulphate reduction is performed by prokaryotes, a heterogeneous group of bacteria and archaea consisting of diverse phyla, such as Archaeoglobi, Proteobacteria, Firmicutes, Nitrospirae and others, that can use sulphate as a terminal electron acceptor.
As all the steps in the sulphate reduction occur in the cytoplasm, similar to the assimilatory conversion, sulphate must be transported across the cytoplasmic membrane into the cells.
The overall process of dissimilatory sulphate reduction can be considered as two phases: firstly, the reduction of sulphate to bisulphite through the intermediate compound APS, and secondly, the reduction of bisulphite to sulphide. The biochemistry of the first phase, with respect to the pathway by which sulphate is reduced to sulphite, has been firmly established. However, in contrast, the pathway of bisulphite reduction to sulphide is still uncertain (see Figure 7.3).

## Slide 8: Biochemical reactions involved in sulphate-reducing bioprocesses
Notes: All of the main reactions associated with sulphur reactions involving living organisms are closely related to the sulphur and carbon cycles. On the other hand, the amount of carbon involved in the fluxes of the sulphur cycle through biogenic processes varies depending on the characteristics of the organisms undertaking the metabolism.
Four main types of reductions are involved in heterotrophic growth of SRB which include: (i) complete oxidation of acidified intermediates to CO2, (ii) incomplete oxidation of acidified intermediates to CH3COO-, (iii) syntrophic degradation of intermediates by acetogenic SRB that are subjected to the efficiency of hydrogen-utilizing bacteria; and (iv) fermentative growth of SRB in the presence of propionate and ethanol.

## Slide 9: Biochemical reactions involved in sulphate-reducing bioprocesses
Typical reactions involved in sulphidogenesis with electron donors from macromolecule (sugar) to micromolecule (CH3COO-) are summarized in Textbook Table 7.1.
Notes: Generally, 24 g of organic carbon is mineralized for each 32 g of reduced sulphate through acetyl CoA or a modified tricarboxylic acid cycle (TCA) pathway in heterotrophic sulphate reduction. Many intermediate products originating from anaerobic fermentation/hydrolysis can be metabolized by SRB, such as amino acids, sugars, long-chain fatty acids, aromatic compounds, lactate, butyrate, propionate and CH3COO- (see Figure 7.4).

## Slide 10
Sulphur-reducing bioprocess
Fundamentals
Key microorganisms driving sulphate reduction
Electron donors for sulphate-reducing bioprocess
Application
Factors affecting sulphate reduction

## Slide 11: Key microorganisms
Genus | Cell form | Electron acceptor for growth (other than SO42-) | Optimum temperature (°C)
Desulphovibrio | Vibrio | SO32-/S2O32-/fumarate/Fe(III)/MnO2/NO2-/NO3-/O2 | 30-38
Desulphomicrobium | Oval to rod | SO32-/S2O32-/NO2-/fumarate/ DMSO | 28-37
Desulphohalobium | Rod | SO32-/S2O32-/S0 | 37-40
Desulphonatronum | Vibro | SO32-/S2O32- | 37-40
Desulphobotulus | Vibrio | SO32- | 34
Desulphocella | Vibrio | - | 34
Desulphofaba | Vibrio | SO32-/S2O32- | 7
Desulphoregula | Rod | Desulphoviridin | 25-30
Desulphobulbus | Lemon/onion | SO32-/ S2O32- /NO2-/NO3-/O2/Fe(III)/ graphite | 28-39
Desulphocapsa | Rod | SO32-/S2O32-/ S0 | 20-30
Desulphofustis | Rod | SO32-/S0 | 28
Desulphorhopalus | Rod | SO32-S2O32-/NO3- | 18-19
Desulphotalea | Rod | SO32-/S2O32-/S0/Fe(III)-citrate | 10
Thermodesulphobacterium | Rod | SO32-/S2O32- | 65-70
Thermodesulphovibrio | Curved rod | SO32-/S2O32-/Fe(III)/arsenate | 65
Desulphosporosinus | Straight/curved rod | SO32-/S2O32-/S0/Fe(III) | 30-37
Desulphotomaculum | Vibrio | SO32-/S2O32-/S0 | 30-38; 50-65
Desulphomonile | Rod | 3-chlorobenzoatefumarate /SO32-/ S2O32-/ S0/ NO3- | 37
16 genera are incomplete organic oxidizers
Notes: SRB are a group of microbes composed of sulphate-reducing bacteria and sulphate-reducing archaea that can perform respiration with oxidized sulphur compounds in their energy metabolism.
With over a century's investigation, more than 120 species and 40 genera belonging to four bacterial classes and two archaeal classes have been recorded, namely (i) mesophilic -proteobacteria with the genera Desulphovibrio, Desulphobacterium, Desulphobacter and Desulphobulbus; (ii) thermophilic Nitrospirae with the genus Thermodesulphovibrio; (iii) Clostridia with the genera Desulphotomaculum and Ammonifex; (iv) thermophilic Thermodesulphobacteria with the genera Caldimicrobium and Thermodesulphobacterium; (v) archaeal Thermoprotei with the genus Caldivirga; and (vi) archaeal Archaeoglobi with the genus Archaeoglobus.
16 genera are incomplete organic oxidizers, 22 genera are complete oxidizers, and the remaining 2 genera, i.e. Desulphotomaculum and Desulphomonile, cannot be simply aligned in either of the two divisions as they appear to have both complete and incomplete oxidizing species.
Besides the common oxidized sulphur compounds, NO3-, NO2-, ferric, manganese oxide and other compounds (e.g. fumarate, DMSO) can also serve as an electron acceptor for some SRB species.
Regarding their physiological property, most SRB genera belong to mesophiles with growth temperature ranging from 25 to 40 oC. Growth temperature is a fundamental variable governing the possible application of SRB-based technologies for environmental remediation or industrial production. For instance, Desulphovibrio, Desulphobulbus, Desulphomicrobium and Desulphobacter are the most commonly found SRB genera for sulphur-laden wastewater treatment. Desulphovibrio, Desulphobulbus and Desulphomicrobium belong to the group of incomplete organics oxidizers, while Desulphobacter is the only dominant complete organics oxidizer identified. Thus, CH3COO- residual of sulphate-reducing bioreactors is an inherent feature of SRB.
SRB are a group of microbes composed of sulphate-reducing bacteria and sulphate-reducing archaea that can perform respiration with oxidized sulphur compounds in their energy metabolism.
With over a century's investigation, more than 120 species and 40 genera belonging to four bacterial classes and two archaeal classes have been recorded, namely (i) mesophilic δ-proteobacteria with the genera Desulphovibrio, Desulphobacterium, Desulphobacter and Desulphobulbus; (ii) thermophilic Nitrospirae with the genus Thermodesulphovibrio; (iii) Clostridia with the genera Desulphotomaculum and Ammonifex; (iv) thermophilic Thermodesulphobacteria with the genera Caldimicrobium and Thermodesulphobacterium; (v) archaeal Thermoprotei with the genus Caldivirga; and (vi) archaeal Archaeoglobi with the genus Archaeoglobus.
16 genera are incomplete organic oxidizers, 22 genera are complete oxidizers, and the remaining 2 genera, i.e. Desulphotomaculum and Desulphomonile, cannot be simply aligned in either of the two divisions as they appear to have both complete and incomplete oxidizing species.
Besides the common oxidized sulphur compounds, NO3-, NO2-, ferric, manganese oxide and other compounds (e.g. fumarate, DMSO) can also serve as an electron acceptor for some SRB species.
Regarding their physiological property, most SRB genera belong to mesophiles with growth temperature ranging from 25 to 40 oC. Growth temperature is a fundamental variable governing the possible application of SRB-based technologies for environmental remediation or industrial production. For instance, Desulphovibrio, Desulphobulbus, Desulphomicrobium and Desulphobacter are the most commonly found SRB genera for sulphur-laden wastewater treatment. Desulphovibrio, Desulphobulbus and Desulphomicrobium belong to the group of incomplete organics oxidizers, while Desulphobacter is the only dominant complete organics oxidizer identified. Thus, CH3COO- residual of sulphate-reducing bioreactors is an inherent feature of SRB.

## Slide 12: Key microorganisms
Genus | Cell form | Electron acceptor for growth (other than SO42-) | Optimum temperature (°C)
Desulphothermus | Rod to curved | SO32-/S2O32- | 60-65
Desulphobacter | Rod to ellipsoidal | SO32-/S2O32- | 28-32
Desulphobacterium | Oval to rod | SO32-/S2O32-/fumarate | 20-35
Desulphobacula | Oval to curved | SO32-/S2O32- | 28
Desulphococcus | Sphere | SO32-/S2O32- | 28-36
Desulphofrigus | Rod | SO32-/S2O32-/Fe(III)-citrate | 10
Desulphonema | Filaments | SO32-/S2O32-/NO3- | 30-32
Desulphosarcina | Irregular shape/aggregate | SO32-/S2O32-/S0 | 33
Desulphospira | Curved | SO32-/S2O32-/S0 | 26-30
Desulphotignum | Rod to curved | SO32-/S2O32-/CO2 | 28-32
Desulphatibacillum | Rod | SO32-/S2O32- | 28-30
Desulpharculus | Vibrio | SO32-/S2O32- | 35-39
Desulphorhabdus | Rod to ellipsoid | SO32-/S2O32- | 37
Desulphovirga | Rod | SO32-/S2O32-/S0 | 35
Desulphobacca | Oval to rod | SO32-/S2O32- | 37
Desulphospira | Curved | SO32-/S2O32-/S0 | 26-30
Desulphacinum | Oval | SO32-/S2O32-/S0 | 60
Desulphonauticus | Curved rod | SO32-/S2O32-/S0 | 45
Desulphonatronovibrio | Vibrio | SO32-/S2O32-/S0/O2 | 37
Thermodesulphorhabdus | Rod | SO32- | 60
Thermodesulphobium | Rod | S2O32-/NO2-/NO3- | 55
Archaeoglobus | Irregular coccoid | SO32-/S2O32- | 82-83
22 genera are complete oxidizers
Notes: SRB are a group of microbes composed of sulphate-reducing bacteria and sulphate-reducing archaea that can perform respiration with oxidized sulphur compounds in their energy metabolism.
With over a century's investigation, more than 120 species and 40 genera belonging to four bacterial classes and two archaeal classes have been recorded, namely (i) mesophilic -proteobacteria with the genera Desulphovibrio, Desulphobacterium, Desulphobacter and Desulphobulbus; (ii) thermophilic Nitrospirae with the genus Thermodesulphovibrio; (iii) Clostridia with the genera Desulphotomaculum and Ammonifex; (iv) thermophilic Thermodesulphobacteria with the genera Caldimicrobium and Thermodesulphobacterium; (v) archaeal Thermoprotei with the genus Caldivirga; and (vi) archaeal Archaeoglobi with the genus Archaeoglobus.
16 genera are incomplete organic oxidizers, 22 genera are complete oxidizers, and the remaining 2 genera, i.e. Desulphotomaculum and Desulphomonile, cannot be simply aligned in either of the two divisions as they appear to have both complete and incomplete oxidizing species.
Besides the common oxidized sulphur compounds, NO3-, NO2-, ferric, manganese oxide and other compounds (e.g. fumarate, DMSO) can also serve as an electron acceptor for some SRB species.
Regarding their physiological property, most SRB genera belong to mesophiles with growth temperature ranging from 25 to 40 oC. Growth temperature is a fundamental variable governing the possible application of SRB-based technologies for environmental remediation or industrial production. For instance, Desulphovibrio, Desulphobulbus, Desulphomicrobium and Desulphobacter are the most commonly found SRB genera for sulphur-laden wastewater treatment. Desulphovibrio, Desulphobulbus and Desulphomicrobium belong to the group of incomplete organics oxidizers, while Desulphobacter is the only dominant complete organics oxidizer identified. Thus, CH3COO- residual of sulphate-reducing bioreactors is an inherent feature of SRB.
SRB are a group of microbes composed of sulphate-reducing bacteria and sulphate-reducing archaea that can perform respiration with oxidized sulphur compounds in their energy metabolism.
With over a century's investigation, more than 120 species and 40 genera belonging to four bacterial classes and two archaeal classes have been recorded, namely (i) mesophilic δ-proteobacteria with the genera Desulphovibrio, Desulphobacterium, Desulphobacter and Desulphobulbus; (ii) thermophilic Nitrospirae with the genus Thermodesulphovibrio; (iii) Clostridia with the genera Desulphotomaculum and Ammonifex; (iv) thermophilic Thermodesulphobacteria with the genera Caldimicrobium and Thermodesulphobacterium; (v) archaeal Thermoprotei with the genus Caldivirga; and (vi) archaeal Archaeoglobi with the genus Archaeoglobus.
16 genera are incomplete organic oxidizers, 22 genera are complete oxidizers, and the remaining 2 genera, i.e. Desulphotomaculum and Desulphomonile, cannot be simply aligned in either of the two divisions as they appear to have both complete and incomplete oxidizing species.
Besides the common oxidized sulphur compounds, NO3-, NO2-, ferric, manganese oxide and other compounds (e.g. fumarate, DMSO) can also serve as an electron acceptor for some SRB species.
Regarding their physiological property, most SRB genera belong to mesophiles with growth temperature ranging from 25 to 40 oC. Growth temperature is a fundamental variable governing the possible application of SRB-based technologies for environmental remediation or industrial production. For instance, Desulphovibrio, Desulphobulbus, Desulphomicrobium and Desulphobacter are the most commonly found SRB genera for sulphur-laden wastewater treatment. Desulphovibrio, Desulphobulbus and Desulphomicrobium belong to the group of incomplete organics oxidizers, while Desulphobacter is the only dominant complete organics oxidizer identified. Thus, CH3COO- residual of sulphate-reducing bioreactors is an inherent feature of SRB.

## Slide 13
Sulphur-reducing bioprocess
Fundamentals
Key microorganisms driving sulphate reduction
Electron donors for sulphate-reducing bioprocess
Application
Factors affecting sulphate reduction

## Slide 14: Electron donors
Diverse carbon sources and electron donors drive the metabolism of SRB according to the type of the organisms’ growth (autotrophic or heterotrophic).
Most electron donors are fermentation products, monomers, or cell components from other sources.
Heterotrophic SRB utilize organic compounds as the electron donors and carbon sources, through a series of enzymatic catalyses.
The concentration of organic substrate is normally quantitatively expressed in COD in a bio-reaction; stoichiometrically 0.67 mol of COD are needed for complete reduction of 1 mol sulphate.
In a system with deficient COD, extra electron donors or carbon sources must be added to drive the complete reduction of sulphate when sulphate is the target for removal.
Notes: Diverse carbon sources and electron donors drive the metabolism of SRB according to the type of the organisms’ growth (autotrophic or heterotrophic). Most electron donors are fermentation products, monomers, or cell components from other sources.

## Slide 15: Electron donors
Electron donor | Reaction | Sulphate reduction rate (gSO42-/L.d) | Advantages (+) and disadvantages (−)
H2/CO | 4H2 + SO42- → S2- + 4H2O 4CO + SO42- → S2- + 4CO2 | 0.4-1.9 | + Low cost; Most SRB can use H2 as energy source; No organic residual in the effluent; Sufficient supply − Toxicity of CO towards SRB; H2 mass transfer limits the reaction rate; Induce competition with other organisms (methanogens)
H2/CO2 | 4H2 + SO42- + CO2 → HS- + HCO3- + 3H2O 4H2 + 2CO2 → CH3COO- + 2H2O + H+ CH3COO− + SO42−→ HS− + 2HCO3− | 4.5-30.0 | + SRB can outcompete methanogens for H2; No organic residual in the effluent − Induce competition with other organisms (methanogens, homoacetogenic bacteria); Formation of methane lower H2 utilization efficiency; H2 safety requirements
Synthetic gas (H2 + CO2 + CO) | 4H2 + SO42- → S2- + 4H2O 4CO + SO42- → S2- + 4CO2 4H2 + SO42- +CO2 → HS- + HCO3- + 3H2O | 9.6-14.0 | + Low cost ; Some SRB have a much higher tolerance for CO than those documented byprevious studies − Availability may be limited
Methane | CH4 + SO42− → HCO3− + HS− + H2O | 0.4·10-3-0.24 | + Sufficient reserve − Low biomass growth rate
Notes: Heterotrophic SRB utilize organic compounds as the electron donors and carbon sources, through a series of enzymatic catalyses. The concentration of organic substrate is normally quantitatively expressed in COD in a bio-reaction; stoichiometrically 0.67 mol of COD are needed for complete reduction of 1 mol sulphate. In a system with deficient COD, extra electron donors or carbon sources must be added to drive the complete reduction of sulphate when sulphate is the target for removal.
Due to the diversity of SRB species, a mixture of electron donors is recommended for SRB growth. The mixture of different types of waste containing both relatively readily biodegradable (animal manure, compost, sludge) and recalcitrant cellulosic materials (sawdust or wood chips) gives a better removal efficiency of organics and sulphate by SRB. This implies that locally available organic wastes, i.e. food/seafood processing industries, animal manure, sewage sludge, molasses, and compost providing complex organic matters, can serve as effective electron donor sources, while agricultural waste, reed canary grass (Phalaris arundinacea), sawdust, wood chips, rice straw and leaf compost provide suitable high cellulosic organic matters (Hao et al., 2014).

## Slide 16: Electron donors
Electron donor | Reaction | Sulphate reduction rate (gSO42-/L.d) | Advantages (+) and disadvantages (−)
Methanol | 4CH3OH + 3SO42− → 4HCO3− + 3HS− + 4H2O + H+ | 0.4-20.5 | + Relatively low cost; Require a simple design reactor; SRB can outcompete methanogens at high temperatures (55-70°C) − Methanogens dominate the community under mesophilic conditions; Only a few SRB strains can utilize methanol
Ethanol | C2H5OH + 0.5SO42− → CH3COO− + 0.5HS− + 0.5H+ + H2O CH3COO− + SO42− → 2HCO3− + HS− 4H2 + SO42− + H+ → HS− + 4H2O. | 0.45-21.00 | + Relatively cheap reagent; Easily converted by SRB − Low biomass yield; Incomplete oxidation to CH3COO- leading to high effluent COD concentration
Formate | SO42− + 4HCOO− + H+ → HS− + 4HCO− | ≤29 | + Produce less CH3COO- during formate utilization; Many SRB capable of growing on H2 can also grow on formate as a sole energy source; A safe alternative for H2 – Methanogens outcompete SRB at 65-75oC
Notes: Heterotrophic SRB utilize organic compounds as the electron donors and carbon sources, through a series of enzymatic catalyses. The concentration of organic substrate is normally quantitatively expressed in COD in a bio-reaction; stoichiometrically 0.67 mol of COD are needed for complete reduction of 1 mol sulphate. In a system with deficient COD, extra electron donors or carbon sources must be added to drive the complete reduction of sulphate when sulphate is the target for removal.
Due to the diversity of SRB species, a mixture of electron donors is recommended for SRB growth. The mixture of different types of waste containing both relatively readily biodegradable (animal manure, compost, sludge) and recalcitrant cellulosic materials (sawdust or wood chips) gives a better removal efficiency of organics and sulphate by SRB. This implies that locally available organic wastes, i.e. food/seafood processing industries, animal manure, sewage sludge, molasses, and compost providing complex organic matters, can serve as effective electron donor sources, while agricultural waste, reed canary grass (Phalaris arundinacea), sawdust, wood chips, rice straw and leaf compost provide suitable high cellulosic organic matters (Hao et al., 2014).

## Slide 17: Electron donors
Electron donor | Reaction | Sulphate reduction rate (gSO42-/L.d) | Advantages (+) and disadvantages (−)
Acetate | CH3COO− + SO42− → HS− + 2HCO3− | ≤65 | – Methanogens can outcompete SRB for CH3COO-; Only a few SRB can oxidize CH3COO-; CH3COO- inhibit sulphate reduction at concentrations above 15 mmol/l; Low yield
Lactate | CH3CHOHCOOH + 0.5H2SO4 → CH3COOH + CO2 + 0.5H2S + H2O | 0.36-5.76 | + Wide spectrum of SRB can grow on lactate; Generate a large amount of alkalinity; Relieve the sulphide toxicity; Preferred carbon source for SRB – High cost
Glucose/acetate | Glucose + SO42- → HS- + 2 CH3COO- + 2HCO3- + 3H+ | 0.9-2.2 | – Low pH of system due to fermentation
Notes: Heterotrophic SRB utilize organic compounds as the electron donors and carbon sources, through a series of enzymatic catalyses. The concentration of organic substrate is normally quantitatively expressed in COD in a bio-reaction; stoichiometrically 0.67 mol of COD are needed for complete reduction of 1 mol sulphate. In a system with deficient COD, extra electron donors or carbon sources must be added to drive the complete reduction of sulphate when sulphate is the target for removal.
Due to the diversity of SRB species, a mixture of electron donors is recommended for SRB growth. The mixture of different types of waste containing both relatively readily biodegradable (animal manure, compost, sludge) and recalcitrant cellulosic materials (sawdust or wood chips) gives a better removal efficiency of organics and sulphate by SRB. This implies that locally available organic wastes, i.e. food/seafood processing industries, animal manure, sewage sludge, molasses, and compost providing complex organic matters, can serve as effective electron donor sources, while agricultural waste, reed canary grass (Phalaris arundinacea), sawdust, wood chips, rice straw and leaf compost provide suitable high cellulosic organic matters (Hao et al., 2014).

## Slide 18: Electron donors
Electron donor | Reaction | Sulphate reduction rate (gSO42-/L.d) | Advantages (+) and disadvantages (−)
Sucrose/peptone | C12H22O11 + 5H2O + 4SO42– → 4CO2 + 8H2 + 4HS– + 8HCO3– + 4H+ 8H2 + 2SO42– + 2H+ → 2HS– + 8H2O | 0.6-12.4 | + Sucrose acidification is not inhibited by sulphide; Suitable carbon and energy sources for SRB – CH3COO- accumulated in the effluent
Molasses | C12H22O11 + H2O → 4CH3CHOHCOOH CH3CHOHCOOH + 0.5H2SO4 → CH3COOH + CO2 + 0.5H2S + H2O | 1.20-7.22 | + Inexpensive and abundantly available; The acidification products can easily be used by SRB – Partial complex compounds in molasses are barely decomposed resulting in high COD in the effluent; The accumulation of un-biodegradable compounds; Not suitable for SRB growth; Accumulation of volatile fatty acids
Fructose | C6H12O6 + SO42- → 2CH3COO- + HS- + 2HCO3- + 3H+ | - | – Only few SRB use fructose; The SRB growth on fructose is slow
Benzene/benzoate | C6H5COO− + 0.75SO42− + 4H2O → 3CH3COO− + 0.75HS− + HCO3− + 2.25H+ C6H5COO− + 3.75SO42− + 4H2O → 7HCO3− + 3.75HS− + 2.25H+ | 0.038 | + Can be completely oxidized to CO2 without extracellular intermediates – Long degrading time; Cannot be used by some SRB species
Notes: Heterotrophic SRB utilize organic compounds as the electron donors and carbon sources, through a series of enzymatic catalyses. The concentration of organic substrate is normally quantitatively expressed in COD in a bio-reaction; stoichiometrically 0.67 mol of COD are needed for complete reduction of 1 mol sulphate. In a system with deficient COD, extra electron donors or carbon sources must be added to drive the complete reduction of sulphate when sulphate is the target for removal.
Due to the diversity of SRB species, a mixture of electron donors is recommended for SRB growth. The mixture of different types of waste containing both relatively readily biodegradable (animal manure, compost, sludge) and recalcitrant cellulosic materials (sawdust or wood chips) gives a better removal efficiency of organics and sulphate by SRB. This implies that locally available organic wastes, i.e. food/seafood processing industries, animal manure, sewage sludge, molasses, and compost providing complex organic matters, can serve as effective electron donor sources, while agricultural waste, reed canary grass (Phalaris arundinacea), sawdust, wood chips, rice straw and leaf compost provide suitable high cellulosic organic matters (Hao et al., 2014).

## Slide 19: Electron donors
Electron donor | Reaction | Sulphate reduction rate (gSO42-/L.d) | Advantages (+) and disadvantages (−)
Algal extracellular products/algal biomass | - | 0.0030-0.0058 | + Low-cost carbon source; Easily utilized by SRB; No available limitation – Cannot be used directly, need fermentative bacteria to collaborate together; May cause high COD in the effluent
Cheese whey | - | 0.34 | + Low-cost carbon source; No negative impact on the bacteria – Cannot be used directly, need fermentative bacteria to collaborate together; May cause high COD in the effluent
Watermelon rind | - | 0.15-0.24 | + Low cost – Availability may be limited; May cause high COD in the effluent
Notes: Heterotrophic SRB utilize organic compounds as the electron donors and carbon sources, through a series of enzymatic catalyses. The concentration of organic substrate is normally quantitatively expressed in COD in a bio-reaction; stoichiometrically 0.67 mol of COD are needed for complete reduction of 1 mol sulphate. In a system with deficient COD, extra electron donors or carbon sources must be added to drive the complete reduction of sulphate when sulphate is the target for removal.
Due to the diversity of SRB species, a mixture of electron donors is recommended for SRB growth. The mixture of different types of waste containing both relatively readily biodegradable (animal manure, compost, sludge) and recalcitrant cellulosic materials (sawdust or wood chips) gives a better removal efficiency of organics and sulphate by SRB. This implies that locally available organic wastes, i.e. food/seafood processing industries, animal manure, sewage sludge, molasses, and compost providing complex organic matters, can serve as effective electron donor sources, while agricultural waste, reed canary grass (Phalaris arundinacea), sawdust, wood chips, rice straw and leaf compost provide suitable high cellulosic organic matters (Hao et al., 2014).

## Slide 20: Electron donors
Electron donor | Reaction | Sulphate reduction rate (gSO42-/L.d) | Advantages (+) and disadvantages (−)
Phalaris-arundinacea | - | 2.2-3.3 | + Low cost; Suitable for bioremediation application – May cause high COD in the effluent
Mixture of wood chips, leaf compost and poultry manure | - | 0.01 | 
Mushroom compost, wood chips, sawdust, and rice straw | - | 0.33-0.57 | 
Primary sewage sludge | - | 2.4 | + Low cost – Some organic matters cannot be used directly; May cause high COD in the effluent
Animal manure | - | 40.3 | + Low cost; Efficient biodegradable substrate – Availability may be limited
Notes: Heterotrophic SRB utilize organic compounds as the electron donors and carbon sources, through a series of enzymatic catalyses. The concentration of organic substrate is normally quantitatively expressed in COD in a bio-reaction; stoichiometrically 0.67 mol of COD are needed for complete reduction of 1 mol sulphate. In a system with deficient COD, extra electron donors or carbon sources must be added to drive the complete reduction of sulphate when sulphate is the target for removal.
Due to the diversity of SRB species, a mixture of electron donors is recommended for SRB growth. The mixture of different types of waste containing both relatively readily biodegradable (animal manure, compost, sludge) and recalcitrant cellulosic materials (sawdust or wood chips) gives a better removal efficiency of organics and sulphate by SRB. This implies that locally available organic wastes, i.e. food/seafood processing industries, animal manure, sewage sludge, molasses, and compost providing complex organic matters, can serve as effective electron donor sources, while agricultural waste, reed canary grass (Phalaris arundinacea), sawdust, wood chips, rice straw and leaf compost provide suitable high cellulosic organic matters (Hao et al., 2014).

## Slide 21
Sulphur-reducing bioprocess
Fundamentals
Key microorganisms driving sulphate reduction
Electron donors for sulphate-reducing bioprocess
Application
Factors affecting sulphate reduction

## Slide 22: Sulphur-laden wastewater treatment
Wastewater containing sulphate and organics: sulphate-reducing processes can be applied for removal and reuse of sulphur compounds from sulphur-laden wastewaters (e.g. leather tanning, kraft pulping, food processing, etc.), and from FGD wastewater.
For high organic strength sulphur-laden wastewaters (e.g. starch, organic acid, ignin, etc.), SRB are primarily intended for removing sulphate from wastewater and concurrently enhancing alkalinity via the carbonization of organic matters.
Notes: In the case of China, the COD/TN ratio of municipal wastewater ranges between 5.4-10.9, which is lower than the 8-12 required for satisfactory removal of nutrients (nitrogen and phosphorus) (Sun et al., 2016).

## Slide 23: Sulphur-laden wastewater treatment
FGD wastewater lacks sufficient organics for sulphate reduction, demanding external electron donors, such as H2 and citrate, etc., to be supplied to drive sulphate reduction.
Under a micro-aeration or bio-sulphide oxidation condition, the produced sulphide can be recovered as elemental sulphur.
Full-scale applications in treatment of FGD wastewater and other sulphur-laden industrial wastewaters have been applied in China, Brazil and the Netherlands.
Notes: FGD wastewater lacks sufficient organics for sulphate reduction, demanding external electron donors, such as H2 and citrate, etc., to be supplied to drive sulphate reduction. The FGD and its wastewater treatment can be described by the following equations:
Under a micro-aeration or bio-sulphide oxidation condition, the produced sulphide can be recovered as elemental sulphur. Full-scale applications in treatment of FGD wastewater and other sulphur-laden industrial wastewaters have been applied in China, Brazil and the Netherlands.
In Brazil, a sulphidogenic sequencing batch biofilm reactor was adopted for treating sulphonation process wastewater at a sulphate-loading rate of up to 1.3 kgSO42-/h, with domestic sewage and ethanol introduced as the external carbon source.

## Slide 24: Sulphur-laden wastewater treatment
SRB are applied for metal removal/remediation from surface water and industrial-mining wastewater (see figure on the left).
SRB-based processes for treatment of wastewater containing dissolved metals involve biological and chemical treatment stages. (see figure on the right).
Notes: (c) Wastewater containing metal without a sulphur source but with electron donors; and D) wastewater containing sulphate and metal.
SRB are applied for metal removal/remediation from surface water and industrial-mining wastewater (see Figure 7.5C). SRB-based processes for treatment of wastewater containing dissolved metals involve biological and chemical treatment stages. In the biological treatment stage, biological sulphate reduction is utilized to generate sulphide via dosing with H2 or organic or sulphur depending on the types of metal-laden wastewater; at the subsequent chemical treatment stage dissolved H2S forms metal sulphide to be separated via gravity settling and dewatering for refining (see Figure 7.5D). There are other related processes for treatment of metal-containing wastewater reported by Van Houten et al. (2009) and DiLoreto et al. (2016).

## Slide 25
Sulphur-reducing bioprocess
Fundamentals
Key microorganisms driving sulphate reduction
Electron donors for sulphate-reducing bioprocess
Application
Factors affecting sulphate reduction

## Slide 26: Influencing factors
Factor | Effect(s) | Condition(s) preferred
Influent components |  | 
Sulphate concentration | Affects SRB growth and activity; Can be outcompeted by other organisms at a low concentration; High concentrations inhibit SRB activity | Typical COD/SO42- values range between 0.7 and 1.5
Trace element | Fe, Cu, Zn, Co, Mo, Ni are needed in electron transport; Synthesis of redox-active metalloenzymes; High Mo level inhibits SRB metabolism | High levels of Fe in culture media are necessary due to sulphide precipitation; *Mo above 2 mM completely inhibits SRB
Metal concentration | Elevated heavy-metal concentration can reduce or terminate SRB activity | Desired concentration and the order of decreasing toxicity (mg/l) Cu <4, Cd <11, Ni <13, Zn <16.5, Cr <35, Pb <80
NO3- concentration | NO3- is a major inhibitor in the growth and activity of SRB | The impact level: 70 mM NO3- significantly inhibits growth; Long-term injection of 0.25-0.33 mM inhibits the number and activity of SRB
pH | Affects the growth and activity; Influences the SRB species diversity and competition with methanogens; Affects quantity of dissolved sulphide | pH range for SRB: 5.5-10
Salinity | Influences the species of SRB present; sulphate-reducing rate is inversely correlated with salinity | Optimum salinity range 6-12 %
* Negative impact limitation.
Notes: In the case of China, the COD/TN ratio of municipal wastewater ranges between 5.4-10.9, which is lower than the 8-12 required for satisfactory removal of nutrients (nitrogen and phosphorus) (Sun et al., 2016).

## Slide 27: Influencing factors
Factor | Effect(s) | Condition(s) preferred
Operational conditions |  | 
Substrate/sulphate | Affects growth, activity and microbial diversity; Proper C/S ratio enables SRB to out-compete other organisms | Optimal COD/SO42- ratio for COD removal is 0.6-1.2 and for sulphate removal is 2.4-4.8
Oxidation-reduction potential (ORP) | Affects the competition between SRB and other organisms e.g. methanogens; Affects the activity of SRB | Suitable ORP for SRB is -50 to -300 mV; Optimal ORP readings of -270 mV using a standard hydrogen probe
Temperature | Controls the activity and growth; Initial cultivation temperature affects SRB diversity; Lower H2S solubility at high temperature | SRB tolerate temperatures between -5 and 75 oC Optimum temperature for most SRB ranges between 28-40 oC
Sludge retention time (SRT) | Affects the reactor’s performance and sludge production; Affects the competition between SRB and methanogens/homoacetogenic bacteria | Elevated SRTs delay the methanogens being out-competed, and methanogens can be rapidly removed by applying a short SRT
Hydraulic retention time (HRT) | Influences SRB activity; Biomass concentration; Competition with other organisms | Overall optimum HRT of 20-30 h for SRB activity
H2S concentration | High H2S directly and reversibly affects SRB, and inhibits the activity | Nitrogen purging; *Decrease the activity when H2S is higher than 60-70 mg/l
Mixing condition | Mixing frequency significantly impacts SRB activity; Affects the SRB distribution and detachment causing hydraulic loss of biomass | 
* Negative impact limitation.
Notes: In the case of China, the COD/TN ratio of municipal wastewater ranges between 5.4-10.9, which is lower than the 8-12 required for satisfactory removal of nutrients (nitrogen and phosphorus) (Sun et al., 2016).

## Slide 28: Influencing factors: COD/SO42- mass ratio
In most SRB-driving heterotrophic reductions, the electron donor and the carbon source often share the same compounds except that H2 and/or CO are also involved.
The mass ratio of COD/SO42- is recognized as a key factor in these reactions because this ratio regulates the competition between SRB and other organisms for substrate.
For instance, 0.6-1.2 is suitable for COD removal while 2.4-4.8 is favourable for sulphate removal; in between 1.7 and 2.7 there is active competition for organic substrate utilization between SRB and methanogens; at <1.5 SRB activity is dominated.
Competition between SRB and methanogens can also be influenced by a specific organic substrate or a type of electron donor, owing to the different kinetic properties of SRB and other elector donors; in the case of trimethylamine and methionine as substrate, methanogens will out-compete SRB.
Notes: In the case of China, the COD/TN ratio of municipal wastewater ranges between 5.4-10.9, which is lower than the 8-12 required for satisfactory removal of nutrients (nitrogen and phosphorus) (Sun et al., 2016).