## Slide 1
Course on Sulphur-based Wastewater Treatment
Sulphur-driven Autotrophic Denitrification
Guanghao Chen
Di Wu
Notes: For this chapter, we gather to discuss a topic of utmost importance in the field of wastewater treatment.
The transition from passive treatment to carbon- and energy-neutral treatment, while simultaneously recovering valuable resources.

## Slide 2: Outline
Course on Sulphur-based Wastewater Treatment
Introduction
Biochemical reaction in the SdAD
Microorganisms in the SdAD process
Biochemistry of the SdAD process
Operational conditions governing the SdAD process

## Slide 3
Heterotrophic denitrification typically requires the supply of organic matters as the electron donor, this usually results in higher sludge production, thus higher operational costs, and increases the residual organics in the treated effluents.
The inorganic-based autotrophic denitrification bioprocess has attracted increasing attention in the last decade, especially sulphur-driven autotrophic denitrification (SdAD).
https://doi.org/10.1080/10934529.2021.2004839
Introduction
Notes: In the case of China, the COD/TN ratio of municipal wastewater ranges between 5.4-10.9, which is lower than the 8-12 required for satisfactory removal of nutrients (nitrogen and phosphorus) (Sun et al., 2016).
In treatment of domestic wastewater ## Depletion of groundwater resources, concerns with nutrient enrichment in natural water bodies, decreases in carbon footprint, and stringent discharge limits for nutrients are all encouraging the development of new bioprocesses for nitrogen removal from water and wastewater streams (Kostrytsia et al., 2018b).
Since heterotrophic denitrification typically requires the supply of organic matters as the electron donor, this usually results in higher sludge production, thus higher operational costs, and increases the residual organics in the treated effluents.
Therefore, the inorganic-based autotrophic denitrification bioprocess has attracted increasing attention in the last decade, especially sulphur-driven autotrophic denitrification (SdAD).
This is carried out by chemolithoautotrophic denitrifying microorganisms, i.e. sulphur-oxidizing bacteria (SOB) such as Thiobacillus denitrificans. These are capable of utilizing various inorganic sulphur matters in reduced forms (e.g. S0, TDSd, S2O32-, and SO32-) as the electron donors for denitrification of NO3- and NO2- as well as CO2 sequestration (Cardoso et al., 2006).

## Slide 4
The SdAD process possesses several inherent advantages such as:
No requirement for an exogenous organic carbon source;
It eliminates problems associated with residual organics;
A lower biomass yield coefficient relative to a conventional heterotrophic denitrification process (i.e. 0.15-0.57 g autotrophic biomass production vs. 0.71-1.2 g heterotrophic biomass production per g of NO3--N denitrified), thus reducing sludge production for costly treatment and disposal;
A significant reduction in nitrous oxide (N2O) accumulation and emission during denitrification when sufficient sulphur is available.
Introduction
Notes: In the case of China, the COD/TN ratio of municipal wastewater ranges between 5.4-10.9, which is lower than the 8-12 required for satisfactory removal of nutrients (nitrogen and phosphorus) (Sun et al., 2016).
no requirement for an exogenous organic carbon source;
it eliminates problems associated with residual organics;
a lower biomass yield coefficient relative to a conventional heterotrophic denitrification process (i.e. 0.15-0.57 g autotrophic biomass production vs. 0.71-1.2 g heterotrophic biomass production per 1 g of NO3--N denitrified (Yang et al., 2016a)), thus reducing sludge production for costly treatment and disposal;
a significant reduction in nitrous oxide (N2O) accumulation and emission during denitrification when sufficient sulphur is available (Yang et al., 2016a); and
it facilitates simultaneous removal of NO3-/NO2- and sulphur compounds (Moraes et al., 2012).

## Slide 5
SdAD can be a cost-effective alternative to conventional heterotrophic denitrification in treatment of carbon-deficient sulphur-laden water and wastewaters, such as landfill leachate, aquaculture wastewater, wastewater from the petrochemical industry, effluent polishing of anaerobic reactors, biogas desulphurization, anti-corrosion treatment of sewer systems, and anti-souring treatment of oil reservoirs and petroleum refinery facilities.
https://www.pcimembranes.com/landfill-leachate-treatment/
https://www.tangsonsbio.com/case-24-aquaculture-wastewater-treatment.html
https://petroknowledge.com/courses/oil-refinery-petrochemical-industry-wastewater-treatment
http://www.zhengzeenv.com/Product/Product2/0R3620186.html
Introduction
Notes: In the case of China, the COD/TN ratio of municipal wastewater ranges between 5.4-10.9, which is lower than the 8-12 required for satisfactory removal of nutrients (nitrogen and phosphorus) (Sun et al., 2016).

## Slide 6: Outline
Course on Sulphur-based Wastewater Treatment
Introduction
Biochemical reaction in the SdAD
Microorganisms in the SdAD process
Biochemistry of the SdAD process
Operational conditions governing the SdAD process

## Slide 7: Biochemical reaction in the SdAD
Considering the significance of biological sulphur oxidation in the SdAD process, it is essential to understand the biochemical reactions involved in this process.
The stoichiometric biochemical reactions related to simultaneous sulphur oxidation and denitrification from NO3- and NO2- under anoxic conditions are listed below (see Textbook eqs. 7.7-7.12).
(in consideration of complete denitrification and neglecting the biomass growth)
Notes: In this chapter, we define the sum of H2S (aq), HS- and S2- as the total dissolved sulphide (TDSd), whereas elemental sulphur indicates either chemical (S0chem) (i.e. exogenously added) or biogenic (S0bio) (i.e. endogenously produced) elemental sulphur. The complete oxidation of sulphide to SO42- (see Eq. 7.7), where eight electrons per atom of sulphur oxidize, are donated from sulphide to oxygen.
In the sulphide-oxidizing process, sulphide, as an electron donor, can be oxidized to biogenic elemental sulphur (S0bio) or to sulphate (SO42-).
This reaction is among the most energetic reactions for chemoautotrophs (Di Capua et al., 2019). The complete sulphide oxidation with nitrogen oxides (NOx-) as electron acceptor is thermodynamically favourable as indicated by the standard Gibbs free energy changes (see eqs. 7.7 and 7.8).
However, elemental sulphur formation as an intermediate of autotrophic denitrification depends on sulphide concentration, especially when NO3- is the electron acceptor (Cardoso et al., 2006). This could be attributable to the conversion of sulphide to biogenic elemental sulphur (S0bio) consuming four times less NOx- than its complete oxidation to SO42- (see eqs. 7.7, 7.8, 7.11 and 7.12), resulting in a preferential process under electron acceptor limitation.
In these conditions, the oxidation of excess sulphide is favoured due to its higher bioavailability to denitrifiers compared with S0bio that accumulates over time. Based on the biochemical reactions with the intermediate formation of sulphur compounds, NO2- reduction is evidently thermodynamically more favourable than NO3- reduction from the higher negative standard Gibbs free energy changes (see eqs. 7.11 and 7.12).

## Slide 8: Biochemical reaction in the SdAD
Generally, the actual amount of sulphur compounds consumed is 30-38 % higher than the stoichiometric values, considering the cell growth of SOB.
The stoichiometric biochemical reactions for complete denitrification from NO3- in the use of inorganic sources as well as consideration of the associated biomass growth in anabolism are showed in Textbook Eq.. 7.13-7.15.
Based on the stoichiometries of sulphide-, S0chem- and S2O32--based denitrification, reduction of 1 mgNO3--N generates 5.58, 7.83 and 11.07 mg SO42-, respectively.
This may limit the application of SdAD technology in restoring ground and surface waters contaminated by NO3- and NO2-.
Notes: It is worth noting that the fraction of electrons contributed to growth is neglected in the above eqs. 7.7, 7.9 and 7.10. Generally, the actual amount of sulphur compounds consumed is 30-38 % higher than the stoichiometric values, considering the cell growth of SOB.
Consequently, eqs. 7.7, 7.9 and 7.10 are extended to eqs. 7.13, 7.14 and 7.15 to represent the stoichiometric biochemical reactions for complete denitrification from NO3- in the use of inorganic sources as well as consideration of the associated biomass growth in anabolism. The biomass growth yield (Y, gcells/gNO3--N) of sulphur-oxidizing denitrifiers depends on the types of sulphur compounds consumed in the biochemical reactions, as shown in the following equations (Mora et al., 2014).
Based on the stoichiometries of sulphide-, S0chem- and S2O32--based denitrification (see eqs. 7.7, 7.8 and 7.9), reduction of 1 mgNO3--N generates 5.58, 7.83 and 11.07 mg SO42-, respectively. This may limit the application of SdAD technology in restoring ground and surface waters contaminated by NO3- and NO2-.

## Slide 9: Outline
Course on Sulphur-based Wastewater Treatment
Introduction
Biochemical reaction in the SdAD
Microorganisms in the SdAD process
Biochemistry of the SdAD process
Operational conditions governing the SdAD process

## Slide 10: Microorganisms in the SdAD process
Microbial consortia involved in the SdAD process are phylogenetically diverse and mainly consist of sulphur-oxidizing and nitrate-reducing bacteria, predominantly belonging to phyla Proteobacteria, Firmicutes, Chloroflexi and Chlorobi.
The microorganisms belonging to the genera Thiobacillus, Thiomonas and Sulphurimonas are the most well-known SOB for autotrophic denitrification which obtains energy for denitrification and biomass synthesis mainly from sulphur oxidation. The microbial composition and diversity of SOB vary significantly depending upon the type of electron donor.
Notes: Microbial consortia involved in the SdAD process are phylogenetically diverse and mainly consist of sulphur-oxidizing and nitrate-reducing bacteria, predominantly belonging to phyla Proteobacteria, Firmicutes, Chloroflexi and Chlorobi (Zhang et al., 2015). The microorganisms belonging to the genera Thiobacillus, Thiomonas and Sulphurimonas are the most well-known SOB for autotrophic denitrification which obtains energy for denitrification and biomass synthesis mainly from sulphur oxidation. The microbial composition and diversity of SOB vary significantly depending upon the type of electron donor. Several predominant genera and their optimum growth conditions driven by different electron donors are summarized in Table 7.6, which are Thiobacillus and Sulphurimonas as obligate and/or facultative chemolithotrophs. Facultative chemolithotrophic SOB can grow autotrophically or mixotrophically on complex organic compounds as their concurrent carbon and energy sources (Muyzer et al., 2013). To date, many SOB species have been isolated from sediments, hydrothermal vents, oceans, soda lakes and hypersaline lakes, and several of them are found in the SdAD process. Table 7.7 summarizes these SOB and their optimum growth conditions. SOB species can grow at different pH values, e.g. Thiomicrospira grow from pH 5.5 to 8.5, and Thiobacillus denitrificans prefer neutral conditions. Some SOB are acidophiles and can grow at a pH lower than 5.0 and some (e.g. Thialkalivibrio nitratireducens and Thiobacillus versutus) only grow in an alkaline environment. For most SOB their optimal growth temperatures are around 30 oC, while a few SOB have a wide range of optimal growth temperature, e.g. Paracoccus grow under either psychrophilic or thermophilic conditions.

## Slide 11: Microorganisms in the SdAD process
Several predominant genera and their optimum growth conditions driven by different electron donors are summarized in Textbook Table 7.6
Table 7.6 Predominant genera of the bacterial consortium involved in the SdAD process driven by different electron donors. |  |  |  |  |  | 
Electron donor | Predominant genus | Relative abundance (%) | Type of reactor | pH | Temperature (oC) | Electron acceptor
S0chem | Thiobacillus Ignavibacteriales Sulphurimonas Longilinea | 45.1 25.4 7.0 4.1 | AnFB-MBR | - | 25-31 | NO3-
TDSd | Thiobacillus Sulphurimonas Paracoccus | 32.6 31.3 0.1 | GSAD | 7.3-7.7 | 28-32 | NO3-
TDSd | Acinetobacter Thiobacillus Thiothrix | 12.8 3.6 1.6 | Up-flow biofilter | 7.2-7.3 | 5-35 | NO3-
S2O32- | Chlorobaculum Thiobacillus Sulphurimonas | 9.7 8.7 1.2 | Up-flow biofilter | 6.7-7.0 | 5-35 | NO3-
S0chem | Dechloromonas Thiobacillus Thauera | 18.0 8.7 2.2 | Up-flow biofilter | 6.5-7.0 | 5-35 | NO3-
TDSd: total dissolved sulphide (H2S, HS-, S2-); S0chem: chemically-added elemental sulphur; AnFB-MBR: anaerobic fluidized-bed membrane bioreactor; GSAD: granular-sludge autotrophic denitrification; SBR: sequencing batch reactor; MBBR: moving-bed biofilm reactor. |  |  |  |  |  | 
Notes: Microbial consortia involved in the SdAD process are phylogenetically diverse and mainly consist of sulphur-oxidizing and nitrate-reducing bacteria, predominantly belonging to phyla Proteobacteria, Firmicutes, Chloroflexi and Chlorobi (Zhang et al., 2015). The microorganisms belonging to the genera Thiobacillus, Thiomonas and Sulphurimonas are the most well-known SOB for autotrophic denitrification which obtains energy for denitrification and biomass synthesis mainly from sulphur oxidation. The microbial composition and diversity of SOB vary significantly depending upon the type of electron donor. Several predominant genera and their optimum growth conditions driven by different electron donors are summarized in Table 7.6, which are Thiobacillus and Sulphurimonas as obligate and/or facultative chemolithotrophs. Facultative chemolithotrophic SOB can grow autotrophically or mixotrophically on complex organic compounds as their concurrent carbon and energy sources (Muyzer et al., 2013).

## Slide 12: Microorganisms in the SdAD process
Table 7.6 Predominant genera of the bacterial consortium involved in the SdAD process driven by different electron donors. |  |  |  |  |  | 
Electron donor | Predominant genus | Relative abundance (%) | Type of reactor | pH | Temperature (oC) | Electron acceptor
S0chem | Thiobacillus Sulphurimonas Thioahalobacter | 22.6 11.8 11.0 | SBR | 7.0-8.5 | 35 | NO3-
S0chem | Sulphurimonas Thauera Simplicispira Pseudomonas | 82.2 2.7 2.3 1.6 | - | 7.5 | 25 | NO3-
TDSd, S2O32- | Maribius Paracoccus Thiobacillus Sedimenticola Thioalbus Sulphurimonas | 11.3 10.0 9.3 8.3 7.6 1.0 | MBBR | 7.2-7.8 | 21-23 | NO3-
S0chem | Thiobacillus Sulphurimonas | 11.0 5.4 | - | 8.0 | 31-35 | NO3-
TDSd: total dissolved sulphide (H2S, HS-, S2-); S0chem: chemically-added elemental sulphur; AnFB-MBR: anaerobic fluidized-bed membrane bioreactor; GSAD: granular-sludge autotrophic denitrification; SBR: sequencing batch reactor; MBBR: moving-bed biofilm reactor. |  |  |  |  |  | 
Notes: Microbial consortia involved in the SdAD process are phylogenetically diverse and mainly consist of sulphur-oxidizing and nitrate-reducing bacteria, predominantly belonging to phyla Proteobacteria, Firmicutes, Chloroflexi and Chlorobi (Zhang et al., 2015). The microorganisms belonging to the genera Thiobacillus, Thiomonas and Sulphurimonas are the most well-known SOB for autotrophic denitrification which obtains energy for denitrification and biomass synthesis mainly from sulphur oxidation. The microbial composition and diversity of SOB vary significantly depending upon the type of electron donor. Several predominant genera and their optimum growth conditions driven by different electron donors are summarized in Table 7.6, which are Thiobacillus and Sulphurimonas as obligate and/or facultative chemolithotrophs. Facultative chemolithotrophic SOB can grow autotrophically or mixotrophically on complex organic compounds as their concurrent carbon and energy sources (Muyzer et al., 2013). To date, many SOB species have been isolated from sediments, hydrothermal vents, oceans, soda lakes and hypersaline lakes, and several of them are found in the SdAD process. Table 7.7 summarizes these SOB and their optimum growth conditions. SOB species can grow at different pH values, e.g. Thiomicrospira grow from pH 5.5 to 8.5, and Thiobacillus denitrificans prefer neutral conditions. Some SOB are acidophiles and can grow at a pH lower than 5.0 and some (e.g. Thialkalivibrio nitratireducens and Thiobacillus versutus) only grow in an alkaline environment. For most SOB their optimal growth temperatures are around 30 oC, while a few SOB have a wide range of optimal growth temperature, e.g. Paracoccus grow under either psychrophilic or thermophilic conditions.

## Slide 13: Microorganisms in the SdAD process
To date, many SOB species have been isolated from sediments, hydrothermal vents, oceans, soda lakes and hypersaline lakes, and several of them are found in the SdAD process.
Textbook Table 7.7 summarizes these SOB and their optimum growth conditions.
Notes: To date, many SOB species have been isolated from sediments, hydrothermal vents, oceans, soda lakes and hypersaline lakes, and several of them are found in the SdAD process. Table 7.7 summarizes these SOB and their optimum growth conditions. SOB species can grow at different pH values, e.g. Thiomicrospira grow from pH 5.5 to 8.5, and Thiobacillus denitrificans prefer neutral conditions. Some SOB are acidophiles and can grow at a pH lower than 5.0 and some (e.g. Thialkalivibrio nitratireducens and Thiobacillus versutus) only grow in an alkaline environment. For most SOB their optimal growth temperatures are around 30 oC, while a few SOB have a wide range of optimal growth temperature, e.g. Paracoccus grow under either psychrophilic or thermophilic conditions.

## Slide 14: Microorganisms in the SdAD process
An analysis of the predominant genera gives a deeper comprehension of the microbial community composition and function in the SdAD process under different operational conditions (such as the initial concentrations of sulphur and NO3-, reactor temperature, pH and HRT)
Electron-donating substrates also play an important role in determining the microbial community structure.
  For instance, Chlorobaculum, Thiobacillus and Sulphurimonas are the predominant genera in a S2O32--driven SdAD system, while Acinetobacter, Thiobacillus and Thiothrix are predominant in a sulphide-driven SdAD system.
Notes: An analysis of the predominant genera gives a deeper comprehension of the microbial community composition and function in the SdAD process under different operational conditions. Microbial community composition can be shaped significantly by changing operational parameters, such as the initial concentrations of sulphur and NO3-, reactor temperature, pH and HRT. Electron-donating substrates also play an important role in determining the microbial community structure. For instance, Chlorobaculum, Thiobacillus and Sulphurimonas are the predominant genera in a S2O32--driven SdAD system, while Acinetobacter, Thiobacillus and Thiothrix are predominant in a sulphide-driven SdAD system. Some genera in low relative abundance can change to a higher relative abundance depending on the type of electron donor, for instance, Thauera has a much higher relative abundance (2.2 %) in a S0chem-based SdAD system than that in a S2O32--based SdAD system (0.4 %) (see Table 7.6). Moreover, different functional microorganisms can be enriched respectively at a low, medium or high sulphide-loading rate, which is an important factor affecting the microbial communities in a simultaneous desulphurization and denitrification SdAD process (Yu et al., 2014). The pH value in the biological reactor also affects the enrichment of microorganisms, thereby NO3– removal efficiency depends on different operational pH values with different types of sulphur substrate (e.g. electron donor) in a SdAD system. SOB-enriched activated sludge can also be granulated in a continuous-flow SdAD bioreactor, with predominant microbial populations (Betaproteobacteria and Epsilonproteobacteria) that are quite different from flocculent sludge (Actinobacteria and Alphaproteobacteria) (Yang et al., 2016a).

## Slide 15: Microorganisms in the SdAD process
Some genera in low relative abundance can change to a higher relative abundance depending on the type of electron donor.
  For instance, Thauera has a much higher relative abundance (2.2%) in a S0chem-based SdAD system than that in a S2O32--based SdAD system (0.4%).
Moreover, different functional microorganisms can be enriched respectively at a low, medium or high sulphide-loading rate, which is an important factor affecting the microbial communities in a simultaneous desulphurization and denitrification SdAD process.
Notes: An analysis of the predominant genera gives a deeper comprehension of the microbial community composition and function in the SdAD process under different operational conditions. Microbial community composition can be shaped significantly by changing operational parameters, such as the initial concentrations of sulphur and NO3-, reactor temperature, pH and HRT. Electron-donating substrates also play an important role in determining the microbial community structure. For instance, Chlorobaculum, Thiobacillus and Sulphurimonas are the predominant genera in a S2O32--driven SdAD system, while Acinetobacter, Thiobacillus and Thiothrix are predominant in a sulphide-driven SdAD system. Some genera in low relative abundance can change to a higher relative abundance depending on the type of electron donor, for instance, Thauera has a much higher relative abundance (2.2 %) in a S0chem-based SdAD system than that in a S2O32--based SdAD system (0.4 %) (see Table 7.6). Moreover, different functional microorganisms can be enriched respectively at a low, medium or high sulphide-loading rate, which is an important factor affecting the microbial communities in a simultaneous desulphurization and denitrification SdAD process (Yu et al., 2014). The pH value in the biological reactor also affects the enrichment of microorganisms, thereby NO3– removal efficiency depends on different operational pH values with different types of sulphur substrate (e.g. electron donor) in a SdAD system. SOB-enriched activated sludge can also be granulated in a continuous-flow SdAD bioreactor, with predominant microbial populations (Betaproteobacteria and Epsilonproteobacteria) that are quite different from flocculent sludge (Actinobacteria and Alphaproteobacteria) (Yang et al., 2016a).

## Slide 16: Biochemistry of SdAD process
The pH value in the biological reactor also affects the enrichment of microorganisms, thereby NO3– removal efficiency depends on different operational pH values with different types of sulphur substrate (e.g. electron donor) in a SdAD system.
SOB-enriched activated sludge can also be granulated in a continuous-flow SdAD bioreactor, with predominant microbial populations (Betaproteobacteria and Epsilonproteobacteria) that are quite different from flocculent sludge (Actinobacteria and Alphaproteobacteria).
Notes: An analysis of the predominant genera gives a deeper comprehension of the microbial community composition and function in the SdAD process under different operational conditions. Microbial community composition can be shaped significantly by changing operational parameters, such as the initial concentrations of sulphur and NO3-, reactor temperature, pH and HRT. Electron-donating substrates also play an important role in determining the microbial community structure. For instance, Chlorobaculum, Thiobacillus and Sulphurimonas are the predominant genera in a S2O32--driven SdAD system, while Acinetobacter, Thiobacillus and Thiothrix are predominant in a sulphide-driven SdAD system. Some genera in low relative abundance can change to a higher relative abundance depending on the type of electron donor, for instance, Thauera has a much higher relative abundance (2.2 %) in a S0chem-based SdAD system than that in a S2O32--based SdAD system (0.4 %) (see Table 7.6). Moreover, different functional microorganisms can be enriched respectively at a low, medium or high sulphide-loading rate, which is an important factor affecting the microbial communities in a simultaneous desulphurization and denitrification SdAD process (Yu et al., 2014). The pH value in the biological reactor also affects the enrichment of microorganisms, thereby NO3– removal efficiency depends on different operational pH values with different types of sulphur substrate (e.g. electron donor) in a SdAD system. SOB-enriched activated sludge can also be granulated in a continuous-flow SdAD bioreactor, with predominant microbial populations (Betaproteobacteria and Epsilonproteobacteria) that are quite different from flocculent sludge (Actinobacteria and Alphaproteobacteria) (Yang et al., 2016a).

## Slide 17: Outline
Course on Sulphur-based Wastewater Treatment
Introduction
Biochemical reaction in the SdAD
Microorganisms in the SdAD process
Biochemistry of the SdAD process
Operational conditions governing the SdAD process

## Slide 18
TDSd, S0chem and S2O32- are the most common electron donors for SOB. The metabolic pathways and functional enzymes involved in oxidation of sulphur compounds and energy conservation by SOB have been biochemically characterized, as shown in Textbook Figure 7.6.
The three main pathways:
the sulphur-oxidizing (Sox)-independent pathway involving distinctive oxidases and hydrolases for TDSd, S0chem and S2O32- oxidation;
the tetrathionate (SI4) pathway of S2O32- oxidation; and
the Sox-dependent multiple enzymatic pathway.
Biochemistry of SdAD process:
sulphur-oxidizing enzymes
Notes: TDSd, S0chem and S2O32- are the most common electron donors for SOB. The metabolic pathways and functional enzymes involved in oxidation of sulphur compounds and energy conservation by SOB have been biochemically characterized, as shown in Figure 7.6. The three main pathways that have been identified so far are: (i) the sulphur-oxidizing (Sox)-independent pathway involving distinctive oxidases and hydrolases for TDSd, S0chem and S2O32- oxidation; (ii) the tetrathionate (SI4) pathway of S2O32- oxidation; and (iii) the Sox-dependent multiple enzymatic pathway. The initial bio-oxidation of sulphide can be mediated by the sulphide: quinone oxidoreductase (SQR), a flavoprotein responsible for obligatory biological sulphide oxidation in the photo- and chemolithotrophic bacteria. Moreover, flavocytochrome c sulphide dehydrogenase (FCSD), which shares an ancestor with SQR that has a similar functional pathway, is an alternative sulphur-oxidizing enzyme located in the periplasm. The primary product of the SQR reaction is soluble polysulphide which is finally converted into sulphur globules (i.e. S0bio) by a purely chemical, spontaneous process. The periplasmically-formed sulphur globules can be further transported into the cytoplasm by a sulphur-carrier enzymatic system (SCS) and oxidized into SO32- by Dsr. The subsequent oxidation from SO32- to SO42- primarily uses one of the two confirmed sub-pathways performed by two types of sulphite dehydrogenases. The first sub-pathway employs the sulphite oxidase that oxidizes SO32- and transfers the electrons to cytochrome c; in the second sub-pathway, sulphur chemolithotrophs oxidize SO32- to SO42- through the reverse activity of the enzyme APS (adenosine phosphosulphate) reductase.

## Slide 19
The initial bio-oxidation of sulphide can be mediated by the sulphide: quinone oxidoreductase (SQR), a flavoprotein responsible for obligatory biological sulphide oxidation in the photo- and chemolithotrophic bacteria.
Moreover, flavocytochrome c sulphide dehydrogenase (FCSD), which shares an ancestor with SQR that has a similar functional pathway, is an alternative sulphur-oxidizing enzyme located in the periplasm.
Textbook Figure 7.6
Biochemistry of SdAD process:
sulphur-oxidizing enzymes
Notes: TDSd, S0chem and S2O32- are the most common electron donors for SOB. The metabolic pathways and functional enzymes involved in oxidation of sulphur compounds and energy conservation by SOB have been biochemically characterized, as shown in Figure 7.6. The three main pathways that have been identified so far are: (i) the sulphur-oxidizing (Sox)-independent pathway involving distinctive oxidases and hydrolases for TDSd, S0chem and S2O32- oxidation; (ii) the tetrathionate (SI4) pathway of S2O32- oxidation; and (iii) the Sox-dependent multiple enzymatic pathway. The initial bio-oxidation of sulphide can be mediated by the sulphide: quinone oxidoreductase (SQR), a flavoprotein responsible for obligatory biological sulphide oxidation in the photo- and chemolithotrophic bacteria. Moreover, flavocytochrome c sulphide dehydrogenase (FCSD), which shares an ancestor with SQR that has a similar functional pathway, is an alternative sulphur-oxidizing enzyme located in the periplasm. The primary product of the SQR reaction is soluble polysulphide which is finally converted into sulphur globules (i.e. S0bio) by a purely chemical, spontaneous process. The periplasmically-formed sulphur globules can be further transported into the cytoplasm by a sulphur-carrier enzymatic system (SCS) and oxidized into SO32- by Dsr. The subsequent oxidation from SO32- to SO42- primarily uses one of the two confirmed sub-pathways performed by two types of sulphite dehydrogenases. The first sub-pathway employs the sulphite oxidase that oxidizes SO32- and transfers the electrons to cytochrome c; in the second sub-pathway, sulphur chemolithotrophs oxidize SO32- to SO42- through the reverse activity of the enzyme APS (adenosine phosphosulphate) reductase.

## Slide 20
S2O32- oxidation can also be carried out by the Sox-independent enzyme system via the intermediate formation of tetrathionate catalyzed by thiosulphate: quinone oxidoreductase, and then followed by tetrathionate degradation into SO32- via hydrolysis mediated by cytoplasmic polythionate hydrolase.
This S2O32- oxidation pathway via polythionate formation is commonly found in several β and γ proteobacteria, especially in obligatory chemolithotrophs (e.g. Acidithiobacillus).
Textbook Figure 7.6
Biochemistry of SdAD process:
sulphur-oxidizing enzymes
Notes: S2O32- oxidation can also be carried out by the Sox-independent enzyme system via the intermediate formation of tetrathionate catalyzed by thiosulphate: quinone oxidoreductase, and then followed by tetrathionate degradation into SO32- via hydrolysis mediated by cytoplasmic polythionate hydrolase. This S2O32- oxidation pathway via polythionate formation is commonly found in several β and γ proteobacteria, especially in obligatory chemolithotrophs (e.g. Acidithiobacillus).
The Sox-dependent enzyme complex, namely the Sox α-proteobacterial multiple enzyme complex, is governed by a conserved Sox operon. The cluster of soxXYZABCD genes encodes the structural components of the sulphur-oxidizing microbial system. These seven genes make the four proteins (SoxXA, SoxYZ, SoxB, and SoxCD) required for sulphur-dependent cytochrome c reduction. This multiple enzyme complex can oxidize various reductive sulphur substrates (e.g. TDSd, S2O32-, and S0) into SO42-. For detailed information of the biochemical sulphur oxidation pathways and enzymes, please refer to the book authored by Hell et al. (2008).

## Slide 21
The Sox-dependent enzyme complex, namely the Sox α-proteobacterial multiple enzyme complex, is governed by a conserved Sox operon.
The cluster of soxXYZABCD genes encodes the structural components of the sulphur-oxidizing microbial system. These seven genes make the four proteins (SoxXA, SoxYZ, SoxB, and SoxCD) required for sulphur-dependent cytochrome c reduction.
This multiple enzyme complex can oxidize various reductive sulphur substrates (e.g. TDSd, S2O32-, S0) into SO42-.
Figure source: ISME J 14, 2261–2274 (2020).
Textbook Figure 7.6
Biochemistry of SdAD process:
sulphur-oxidizing enzymes
Notes: S2O32- oxidation can also be carried out by the Sox-independent enzyme system via the intermediate formation of tetrathionate catalyzed by thiosulphate: quinone oxidoreductase, and then followed by tetrathionate degradation into SO32- via hydrolysis mediated by cytoplasmic polythionate hydrolase. This S2O32- oxidation pathway via polythionate formation is commonly found in several β and γ proteobacteria, especially in obligatory chemolithotrophs (e.g. Acidithiobacillus).
The Sox-dependent enzyme complex, namely the Sox α-proteobacterial multiple enzyme complex, is governed by a conserved Sox operon. The cluster of soxXYZABCD genes encodes the structural components of the sulphur-oxidizing microbial system. These seven genes make the four proteins (SoxXA, SoxYZ, SoxB, and SoxCD) required for sulphur-dependent cytochrome c reduction. This multiple enzyme complex can oxidize various reductive sulphur substrates (e.g. TDSd, S2O32-, and S0) into SO42-. For detailed information of the biochemical sulphur oxidation pathways and enzymes, please refer to the book authored by Hell et al. (2008).

## Slide 22: Biochemistry of the SdAD process: nitrogen-reducing enzymes
Biological autotrophic denitrification is a combination of four microbial nitrogen-reductive reactions: dissimilatory NO3- reduction, NO2- reduction, NO reduction, and N2O reduction.
Textbook Figure 7.7
All the steps within this metabolic pathway are catalyzed by complex multisite metalloenzymes, which requires 10 mol electrons and 12 mol H+ for complete reduction of 1 mol NO3- to N2.
Notes: Biological autotrophic denitrification is a combination of four microbial nitrogen-reductive reactions: dissimilatory NO3- reduction, NO2- reduction, NO reduction, and N2O reduction. All the steps within this metabolic pathway are catalyzed by complex multisite metalloenzymes, which requires 10 mol electrons and 12 mol H+ for complete reduction of 1 mol NO3- to N2. In the first step, the two electron reduction of NO3- to NO2- is catalyzed by molybdenum-containing nitrate reductase (Nar). The enzyme is either located in the cytoplasm (Nar GH) or in the periplasm (Nap AB). NO2- is further reduced to NO in the second step catalyzed by nitrite reductase (Nir) located in the periplasm (see Figure 7.7). In the third step, two molecules of nitric oxide are conjugated to form N2O and water with the addition of two electrons. This reaction is catalyzed by a membrane-bound nitric oxide reductase (Nor) that comprises heme c, heme b and non-heme iron cofactors. Finally, a copper-containing metalloenzyme, i.e. nitrous oxide reductase (Nos), is responsible for the last step of denitrification, i.e. N2O reduction into dinitrogen (N2) (see Figure 7.7). For more detailed information on the structure and function of nitrogen oxide-reducing enzymes, readers can refer to the books by Van Spanning et al. (2007) and Moura et al. (2016).

## Slide 23: Biochemistry of the SdAD process: nitrogen-reducing enzymes
In the first step, the two electron reduction of NO3- to NO2- is catalyzed by molybdenum-containing nitrate reductase (Nar). The enzyme is either located in the cytoplasm (Nar GHI) or in the periplasm (Nap AB).
Figure source: https://teamaquafix.com/aerobic-denitrifier/
Notes: Biological autotrophic denitrification is a combination of four microbial nitrogen-reductive reactions: dissimilatory NO3- reduction, NO2- reduction, NO reduction, and N2O reduction. All the steps within this metabolic pathway are catalyzed by complex multisite metalloenzymes, which requires 10 mol electrons and 12 mol H+ for complete reduction of 1 mol NO3- to N2. In the first step, the two electron reduction of NO3- to NO2- is catalyzed by molybdenum-containing nitrate reductase (Nar). The enzyme is either located in the cytoplasm (Nar GH) or in the periplasm (Nap AB). NO2- is further reduced to NO in the second step catalyzed by nitrite reductase (Nir) located in the periplasm (see Figure 7.7). In the third step, two molecules of nitric oxide are conjugated to form N2O and water with the addition of two electrons. This reaction is catalyzed by a membrane-bound nitric oxide reductase (Nor) that comprises heme c, heme b and non-heme iron cofactors. Finally, a copper-containing metalloenzyme, i.e. nitrous oxide reductase (Nos), is responsible for the last step of denitrification, i.e. N2O reduction into dinitrogen (N2) (see Figure 7.7). For more detailed information on the structure and function of nitrogen oxide-reducing enzymes, readers can refer to the books by Van Spanning et al. (2007) and Moura et al. (2016).

## Slide 24: Biochemistry of the SdAD process: nitrogen-reducing enzymes
NO2- is further reduced to NO in the second step catalyzed by nitrite reductase (Nir) located in the periplasm.
Figure source: https://teamaquafix.com/aerobic-denitrifier/
Notes: Biological autotrophic denitrification is a combination of four microbial nitrogen-reductive reactions: dissimilatory NO3- reduction, NO2- reduction, NO reduction, and N2O reduction. All the steps within this metabolic pathway are catalyzed by complex multisite metalloenzymes, which requires 10 mol electrons and 12 mol H+ for complete reduction of 1 mol NO3- to N2. In the first step, the two electron reduction of NO3- to NO2- is catalyzed by molybdenum-containing nitrate reductase (Nar). The enzyme is either located in the cytoplasm (Nar GH) or in the periplasm (Nap AB). NO2- is further reduced to NO in the second step catalyzed by nitrite reductase (Nir) located in the periplasm (see Figure 7.7). In the third step, two molecules of nitric oxide are conjugated to form N2O and water with the addition of two electrons. This reaction is catalyzed by a membrane-bound nitric oxide reductase (Nor) that comprises heme c, heme b and non-heme iron cofactors. Finally, a copper-containing metalloenzyme, i.e. nitrous oxide reductase (Nos), is responsible for the last step of denitrification, i.e. N2O reduction into dinitrogen (N2) (see Figure 7.7). For more detailed information on the structure and function of nitrogen oxide-reducing enzymes, readers can refer to the books by Van Spanning et al. (2007) and Moura et al. (2016).

## Slide 25: Biochemistry of the SdAD process: nitrogen-reducing enzymes
In the third step, two molecules of nitric oxide are conjugated to form N2O and water with the addition of two electrons. This reaction is catalyzed by a membrane-bound nitric oxide reductase (Nor) that comprises heme c, heme b and non-heme iron cofactors.
Figure source: https://teamaquafix.com/aerobic-denitrifier/
Notes: Biological autotrophic denitrification is a combination of four microbial nitrogen-reductive reactions: dissimilatory NO3- reduction, NO2- reduction, NO reduction, and N2O reduction. All the steps within this metabolic pathway are catalyzed by complex multisite metalloenzymes, which requires 10 mol electrons and 12 mol H+ for complete reduction of 1 mol NO3- to N2. In the first step, the two electron reduction of NO3- to NO2- is catalyzed by molybdenum-containing nitrate reductase (Nar). The enzyme is either located in the cytoplasm (Nar GH) or in the periplasm (Nap AB). NO2- is further reduced to NO in the second step catalyzed by nitrite reductase (Nir) located in the periplasm (see Figure 7.7). In the third step, two molecules of nitric oxide are conjugated to form N2O and water with the addition of two electrons. This reaction is catalyzed by a membrane-bound nitric oxide reductase (Nor) that comprises heme c, heme b and non-heme iron cofactors. Finally, a copper-containing metalloenzyme, i.e. nitrous oxide reductase (Nos), is responsible for the last step of denitrification, i.e. N2O reduction into dinitrogen (N2) (see Figure 7.7). For more detailed information on the structure and function of nitrogen oxide-reducing enzymes, readers can refer to the books by Van Spanning et al. (2007) and Moura et al. (2016).

## Slide 26: Biochemistry of the SdAD process: nitrogen-reducing enzymes
Finally, a copper-containing metalloenzyme, i.e. nitrous oxide reductase (Nos), is responsible for the last step of denitrification, i.e. N2O reduction into dinitrogen (N2).
Figure source: https://teamaquafix.com/aerobic-denitrifier/
Notes: Biological autotrophic denitrification is a combination of four microbial nitrogen-reductive reactions: dissimilatory NO3- reduction, NO2- reduction, NO reduction, and N2O reduction. All the steps within this metabolic pathway are catalyzed by complex multisite metalloenzymes, which requires 10 mol electrons and 12 mol H+ for complete reduction of 1 mol NO3- to N2. In the first step, the two electron reduction of NO3- to NO2- is catalyzed by molybdenum-containing nitrate reductase (Nar). The enzyme is either located in the cytoplasm (Nar GH) or in the periplasm (Nap AB). NO2- is further reduced to NO in the second step catalyzed by nitrite reductase (Nir) located in the periplasm (see Figure 7.7). In the third step, two molecules of nitric oxide are conjugated to form N2O and water with the addition of two electrons. This reaction is catalyzed by a membrane-bound nitric oxide reductase (Nor) that comprises heme c, heme b and non-heme iron cofactors. Finally, a copper-containing metalloenzyme, i.e. nitrous oxide reductase (Nos), is responsible for the last step of denitrification, i.e. N2O reduction into dinitrogen (N2) (see Figure 7.7). For more detailed information on the structure and function of nitrogen oxide-reducing enzymes, readers can refer to the books by Van Spanning et al. (2007) and Moura et al. (2016).

## Slide 27: Biochemistry of the SdAD process: electron distribution and competition in the SdAD process
Textbook Figure 7.7
The electron distribution pathway in the SdAD process is shown in Textbook Figure 7.7. Dissolved sulphide can be converted into S0bio by the SQR or into SO42- by the Sox enzyme complex. The electrons generated from the oxidation of inorganic sulphur electron donors facilitate the membrane-bound Nar to perform NO3- reduction to NO2-.
Notes: Biological autotrophic denitrification is a combination of four microbial nitrogen-reductive reactions: dissimilatory NO3- reduction, NO2- reduction, NO reduction, and N2O reduction. All the steps within this metabolic pathway are catalyzed by complex multisite metalloenzymes, which requires 10 mol electrons and 12 mol H+ for complete reduction of 1 mol NO3- to N2. In the first step, the two electron reduction of NO3- to NO2- is catalyzed by molybdenum-containing nitrate reductase (Nar). The enzyme is either located in the cytoplasm (Nar GH) or in the periplasm (Nap AB). NO2- is further reduced to NO in the second step catalyzed by nitrite reductase (Nir) located in the periplasm (see Figure 7.7). In the third step, two molecules of nitric oxide are conjugated to form N2O and water with the addition of two electrons. This reaction is catalyzed by a membrane-bound nitric oxide reductase (Nor) that comprises heme c, heme b and non-heme iron cofactors. Finally, a copper-containing metalloenzyme, i.e. nitrous oxide reductase (Nos), is responsible for the last step of denitrification, i.e. N2O reduction into dinitrogen (N2) (see Figure 7.7). For more detailed information on the structure and function of nitrogen oxide-reducing enzymes, readers can refer to the books by Van Spanning et al. (2007) and Moura et al. (2016).

## Slide 28: Biochemistry of the SdAD process: electron distribution and competition in the SdAD process
Textbook Figure 7.7
The competition between different nitrogen oxide reductases (i.e. Nar, Nir, Nor, and Nos) commonly exists in the respiratory chain of denitrification.
Compete for the electrons among Nar, Nir, Nor, and Nos regulates the electron distribution among the denitrification steps and determines the possible accumulation of nitrogen compounds.
Notes: Biological autotrophic denitrification is a combination of four microbial nitrogen-reductive reactions: dissimilatory NO3- reduction, NO2- reduction, NO reduction, and N2O reduction. All the steps within this metabolic pathway are catalyzed by complex multisite metalloenzymes, which requires 10 mol electrons and 12 mol H+ for complete reduction of 1 mol NO3- to N2. In the first step, the two electron reduction of NO3- to NO2- is catalyzed by molybdenum-containing nitrate reductase (Nar). The enzyme is either located in the cytoplasm (Nar GH) or in the periplasm (Nap AB). NO2- is further reduced to NO in the second step catalyzed by nitrite reductase (Nir) located in the periplasm (see Figure 7.7). In the third step, two molecules of nitric oxide are conjugated to form N2O and water with the addition of two electrons. This reaction is catalyzed by a membrane-bound nitric oxide reductase (Nor) that comprises heme c, heme b and non-heme iron cofactors. Finally, a copper-containing metalloenzyme, i.e. nitrous oxide reductase (Nos), is responsible for the last step of denitrification, i.e. N2O reduction into dinitrogen (N2) (see Figure 7.7). For more detailed information on the structure and function of nitrogen oxide-reducing enzymes, readers can refer to the books by Van Spanning et al. (2007) and Moura et al. (2016).

## Slide 29: Biochemistry of the SdAD process: electron distribution and competition in the SdAD process
Textbook Figure 7.7
The sulphur substrates can possess different oxidation rates and subsequent electron flows in the electron transport chain.
Electron competition among the nitrogen oxide reductases affect the reduction rates of the nitrogen oxides and to be responsible for accumulation of the intermediates (i.e. NO2– and N2O).
Notes: Biological autotrophic denitrification is a combination of four microbial nitrogen-reductive reactions: dissimilatory NO3- reduction, NO2- reduction, NO reduction, and N2O reduction. All the steps within this metabolic pathway are catalyzed by complex multisite metalloenzymes, which requires 10 mol electrons and 12 mol H+ for complete reduction of 1 mol NO3- to N2. In the first step, the two electron reduction of NO3- to NO2- is catalyzed by molybdenum-containing nitrate reductase (Nar). The enzyme is either located in the cytoplasm (Nar GH) or in the periplasm (Nap AB). NO2- is further reduced to NO in the second step catalyzed by nitrite reductase (Nir) located in the periplasm (see Figure 7.7). In the third step, two molecules of nitric oxide are conjugated to form N2O and water with the addition of two electrons. This reaction is catalyzed by a membrane-bound nitric oxide reductase (Nor) that comprises heme c, heme b and non-heme iron cofactors. Finally, a copper-containing metalloenzyme, i.e. nitrous oxide reductase (Nos), is responsible for the last step of denitrification, i.e. N2O reduction into dinitrogen (N2) (see Figure 7.7). For more detailed information on the structure and function of nitrogen oxide-reducing enzymes, readers can refer to the books by Van Spanning et al. (2007) and Moura et al. (2016).

## Slide 30: Outline
Course on Sulphur-based Wastewater Treatment
Introduction
Biochemical reaction in the SdAD
Microorganisms in the SdAD process
Biochemistry of the SdAD process
Operational conditions governing the SdAD process

## Slide 31: Operational conditions governing the SdAD process: sulphur substrates and nitrogen oxides
S0chem is a commonly used electron donor in the SdAD process since it is cost-effective, easily available and less toxic compared with other sulphur substrates.
Compared with S0chem, S0bio is more reactive and bioavailable for autotrophic microorganisms.
Notes: S0chem is a commonly used electron donor in the SdAD process since it is cost-effective, easily available and less toxic compared with other sulphur substrates. Sulphur-limestone typically offers a dual source of S0chem and alkalinity for SdAD application and enables SOB-enriched biofilm to develop on the S0chem particles packed in a bioreactor. However, the main drawback of S0chem is its low aqueous solubility and its low mass transfer rate in the reactor, thus impeding the electron transportation and autotrophic denitrification. Hence a biofilm reactor with S0chem as carrier is often recommended for improving the mass transfer efficiency of the reactor. Compared with S0chem, S0bio is more reactive and bioavailable for autotrophic microorganisms, owing to the orthorhombic structure of sulphur crystal covered by a hydrophilic layer of naturally-charged polymers (Kostrytsia et al., 2018a).

## Slide 32: Operational conditions governing the SdAD process: sulphur substrates and nitrogen oxides
TDSd is employed as the electron donor for wastewater treatment.
Its SdAD rate is greater than that with S0chem.
Notes: TDSd has been employed as the electron donor in connecting FGD with the SANI® process for wastewater treatment (Jiang et al., 2013), because its SdAD rate is greater than that with S0chem, as shown in Table 7.8. It should be noted that TDSd is toxic to SOB when its concentration exceeds 200 mgS/l, affecting Nar activity (Fajardo et al. 2014; Lu et al., 2018). Therefore, in TDSd-based SdAD reactors a NO3- volumetric loading rate is recommended to be lower than that with S0chem or S0bio.

## Slide 33: Operational conditions governing the SdAD process: sulphur substrates and nitrogen oxides
S2O32−, present in some industrial effluents acts as the most effective substrate
Notes: S2O32−, present in some industrial effluents (e.g. the mining industry) acts as the most effective sulphur substrate for SdAD (Cardoso et al., 2006; Di Capua et al., 2019) and the least inhibitory to SOB whose tolerance can be up to 2,200 mgS/l (Di Capua et al., 2016; Cui et al., 2019), 10 times greater than that of TDSd. However, the instability of S2O32- (i.e. it is readily decomposed) may limit its application as an electron donor source. For large-scale engineering applications, selection of the most suitable substrate should be based on kinetics, cost, availability to microorganisms, applicability and potential toxicity. Apart from NO3-, NO2- can also be used as an electron acceptor. During the reduction of NO3-, NO2- is an inhibitory intermediate and its accumulation depends on the S/N mass ratio and the concentration of NO3- (An et al., 2010). The accumulation of NO2- greatly inhibits the denitrification process even at a low concentration of 200 mgNO2--N/l (Claus and Kutzner, 1985).

## Slide 34
The S/N mass ratio is closely correlated with the accumulation of intermediates (i.e. N2O, NO2- and S0bio). When the S/N mass ratio is close to 2.1 gS/gN, it starts significantly reducing the emission of N2O, a potent greenhouse gas, in the SdAD process with sulphide as the electron donor.
At a low S/N mass ratio, the lack of an electron source can lead to the accumulation of NO2-, which inhibits denitrification.
A higher S/N mass ratio favours S0bio as the main final product, while SO42- is the preferential product of TDSd oxidation accompanied by complete denitrification when the S/N mass ratio is below the stoichiometric value (1.4 gS/gN).
A minimum S/N mass ratio of 1.6 gS/gN is necessary for achieving >90 % NO3- removal, which is higher than the theoretical stoichiometric S/N mass ratio of 1.4 gS/gN.
Operational conditions governing the SdAD process: sulphur-to-nitrogen (S/N) mass ratio
Notes: The S/N mass ratio is closely correlated with the accumulation of intermediates (i.e. N2O, NO2- and S0bio). When the S/N mass ratio is close to 2.1 gS/gN, it starts significantly reducing the emission of N2O, a potent greenhouse gas, in the SdAD process with sulphide as the electron donor (Yang et al., 2016b). At a low S/N mass ratio, the lack of an electron source can lead to the accumulation of NO2-, which inhibits denitrification (Cui et al., 2019). A higher S/N mass ratio favours S0bio as the main final product, while SO42- is the preferential product of TDSd oxidation accompanied by complete denitrification when the S/N mass ratio is below the stoichiometric value (1.4 gS/gN). A minimum S/N mass ratio of 1.6 gS/gN is necessary for achieving >90 % NO3- removal, which is higher than the theoretical stoichiometric S/N mass ratio of 1.4 gS/gN (Wang et al. 2009; Lu et al., 2012b).

## Slide 35
Biomass types (i.e. activated sludge, biofilms and granules) in different bioreactor configurations, such as UASB (up-flow anaerobic sludge bed) and biofilm reactor, i.e. PBR (packed-bed reactor) and MBBR (moving-bed biofilm reactor), significantly influence the biomass concentration and the denitrification rate.
Operational conditions governing the SdAD process: different sludge types
Notes: Biomass types (i.e. activated sludge, biofilms and granules) in different bioreactor configurations, such as UASB (up-flow anaerobic sludge bed) and biofilm reactor, i.e. PBR (packed-bed reactor) and MBBR (moving-bed biofilm reactor), significantly influence the biomass concentration and the denitrification rate. It is important to maintain high biomass to improve the denitrification rate. Biofilm reactor is proven to be robust and to perform well in SdAD. PBR is particularly suitable for the NO3- removal at a lowconcentration, since a long retention time (>3 h) is required for complete denitrification. MBBR is suitable for maintaining high biomass content of slow-growing SOB (Cui et al., 2018). Even under severe NO3- limitation, MBBR can still achieve complete NO3- removal and it has high resiliency (Khanongnuch et al., 2019). Another method to improve the performance of the SdAD process is to granulate the SOB, which can facilitate both high biomass concentration and robustness for efficient and stable autotrophic denitrification (Yang et al., 2016a). Details of different bioreactor configurations and their applications in the SdAD process are summarized in Table 7.8.
The key to successful application of this process is to attain sufficient slow-growing SOB communities in the reactor.
Biofilm or a granular sludge reactor are preferred. The SdAD process can used to upgrade or retrofit existing WWTPs treating sulphur-laden wastewater or normal wastewater by dosing the appropriate amount of sulphur substrates into an existing or additional anoxic tank for enhancing TN removal.
It could also be applicable in the treatment of pharmaceuticals in wastewater as SOB possess a high tolerance against various pharmaceutical compounds during biodegradation by SOB (Jia et al., 2017).
In addition to municipal wastewater, the SdAD process probably contributes to TN removal in the restoration of groundwater and surface water, the treatment of landfill leachate and brackish water, and biogas desulphurization wastewater.

## Slide 36
Alkalinity: The ratio of alkalinity-to-removed nitrogen should be kept at approximately 4.00-4.46 mgCaCO3/mgN to correspond to the SOB optimal pH range of 6 to 8 (Oh et al., 2001). When S0chem is used as the electron donor, 4.6 g of alkalinity (as CaCO3) is consumed per gNO3--N removed. Some easily available alkaline sources such as limestone, calcite, dolomite, and oyster shell can be considered for addition. In cases of sulphur-limestone systems, the optimal volumetric ratio of the limestone to S0chem is 1:1-1:3 m3/m3.
Oxygen: Oxygen affects the growth of autotrophic denitrifiers. DO concentration between 0.1-0.3 mgO2/L can inhibit the Nos activity, while >1.6 mgO2/L completely inhibits the SdAD process.
Temperature: For most autotrophic denitrifiers, the suitable temperature range is generally 25-35 oC. The SdAD process with sulphide as the electron donor achieves the highest denitrification efficiency (>97%) at 35 oC, which, however, decreases to 36-59 % when temperature decreases to 15 oC.
Operational conditions
governing the SdAD process: environmental factors - alkalinity, oxygen, and temperature
Notes: The ratio of alkalinity-to-removed nitrogen should be kept at approximately 4.00-4.46 mgCaCO3/mgN (Zhang and Shan, 1999; Oh et al., 2003) to correspond to the SOB optimal pH range of 6 to 8 (Oh et al., 2001). When S0chem is used as the electron donor, 4.6 g of alkalinity (as CaCO3) is consumed per gNO3--N removed (Kim and Bae, 2000). Some easily available alkaline sources such as limestone, calcite, dolomite, and oyster shell can be considered for addition. In cases of sulphur-limestone systems, the optimal volumetric ratio of the limestone to S0chem is 1:1-1:3 m3/m3. Oxygen affects the growth of autotrophic denitrifiers. DO concentration between 0.1-0.3 mgO2/l can inhibit the Nos activity, while >1.6 mgO2/l completely inhibits the SdAD process (Cui et al., 2019). For most autotrophic denitrifiers, the suitable temperature range is generally 25-35 oC (Shao et al., 2010; Fajardo et al., 2014). The SdAD process with sulphide as the electron donor achieves the highest denitrification efficiency (>97 %) at 35 oC, which, however, decreases to 36-59 % when temperature decreases to 15 oC (Fajardo et al., 2014).

## Slide 37
Notes: The key to successful application of this process is to attain sufficient slow-growing SOB communities in the reactor.
Biofilm or a granular sludge reactor are preferred. The SdAD process can used to upgrade or retrofit existing WWTPs treating sulphur-laden wastewater or normal wastewater by dosing the appropriate amount of sulphur substrates into an existing or additional anoxic tank for enhancing TN removal.
It could also be applicable in the treatment of pharmaceuticals in wastewater as SOB possess a high tolerance against various pharmaceutical compounds during biodegradation by SOB (Jia et al., 2017).
In addition to municipal wastewater, the SdAD process probably contributes to TN removal in the restoration of groundwater and surface water, the treatment of landfill leachate and brackish water, and biogas desulphurization wastewater.