## Slide 1
Course on Sulphur-based Wastewater Treatment
SANI® Process: Case Study
Guanghao Chen
Di Wu
Notes: For this chapter, we gather to discuss a topic of utmost importance in the field of wastewater treatment.
The transition from passive treatment to carbon- and energy-neutral treatment, while simultaneously recovering valuable resources.

## Slide 2: The Hong Kong water tale
Hong Kong’s population density is as high as 6,659 people/km2, which imposes a high water stress of only 143 m3/cap.year far below the world’s absolute water scarcity level of 1,000 m3/cap.year.
To tackle this survival issue, Hong Kong started using seawater for toilet flushing (SWTF) in the late 1950s and now this covers 85% of the population, saving approximately 280 million m3 of precious freshwater per annum, equivalent to approximately 20% of the total freshwater demand.
Notes: It is widely recognized that over 50% of lost or wasted resources in a city find their way into wastewater,
making it a prime focus for resource recovery efforts.
In our pursuit of sustainable wastewater treatment, it is crucial to explore energy-saving strategies and methods for resource recovery from processes involving the conversion of sulphur

## Slide 3
A typical SWTF system in Hong Kong starts with abstraction of seawater from a suitable seafront site, passing through a coarse screen with mesh size 5-10 mm to protect the pumps, followed by subsequent in-situ electro-chlorination (3-6 mg/L chlorine) to disinfect and control microbial growth in the supply networks.
The energy consumption of SWTF including abstraction, pre-treatment and distribution is estimated at 0.32 kWh/m3, significantly lower than that of water reclamation from biologically-treated domestic sewage using membrane filtration or a membrane bioreactor coupled with the reverse osmosis (RO) process (0.8-1.2 kWh/m3 and 1.2-1.5 kWh/m3, respectively), as well as seawater desalination (2.5-4.0 kWh/m3).
The Hong Kong water tale
Notes: A typical SWTF system in Hong Kong starts with abstraction of seawater from a suitable seafront site, passing through a coarse screen with mesh size 5-10 mm to protect the pumps, followed by subsequent in-situ electro-chlorination (3-6 mg/l chlorine) to disinfect and control microbial growth in the supply networks.
The energy consumption of SWTF including abstraction, pre-treatment and distribution is estimated at 0.32 kWh/m3, significantly lower than that of water reclamation from biologically-treated domestic sewage using membrane filtration or a membrane bioreactor coupled with the reverse osmosis (RO) process (0.8-1.2 kWh/m3 and 1.2-1.5 kWh/m3, respectively), as well as seawater desalination (2.5–4.0 kWh/m3).
Mild steel and ductile iron-piping lines coated with internal cement-mortar lining are applied in the mains pipes, whereas in buildings and housings polyethylene pipes are mainly employed to solve corrosion problems

## Slide 4
To maximize energy efficiency, Hong Kong International Airport (HKIA, 70 million total passengers/year) developed a triple-water-supply (TWS) system by extending the dual-water system to grey water reuse in combination with seawater building cooling.
This TWS system can save up to 52% of the freshwater demand at HKIA. This system is rated to be one of the most energy-efficient water systems in the world.
The Hong Kong water tale
Notes: It is widely recognized that over 50% of lost or wasted resources in a city find their way into wastewater,
making it a prime focus for resource recovery efforts.
In our pursuit of sustainable wastewater treatment, it is crucial to explore energy-saving strategies and methods for resource recovery from processes involving the conversion of sulphur

## Slide 5: Principles of the SANI® process
Notes: The SWTF practice results in, on average, 167 mgSO42--S/l and 5,000 mgCl-/l in Hong Kong saline sewage (Van Loosdrecht et al., 2012), inevitably causing odour issues in the sludge treatment. An ideal solution is to minimize sludge production. Based on this rationale, a novel sulphur-based process for saline wastewater treatment, namely the SANI® process, was developed by the authors from lab-, pilot- and full-scale studies between 2004 and 2017 (Lau et al., 2006; Wang et al., 2009; Lu et al., 2012b; Wu et al, 2016). Comparison between the conventional biological nitrogen removal (BNR) process and the SANI® process in terms of process concept and reactions are shown in Figure 7.9 and Table 7.9, respectively.
Since the introduction of the nitrogen removal process in the 1960s, biological wastewater treatment has relied on the electron flow from organic carbon to oxygen through an integrated carbon and nitrogen cycle, as shown in Figure 7.9a. However, the conventional BNR process generates a large quantity of excess sludge due to high theoretical sludge yields resulting from organics removal by aerobic and anoxic oxidation (more details in Table 7.9). In contrast, the SANI® process integrates anaerobic organic removal by sulphate reduction and anoxic nitrogen removal by autotrophic denitrification for NO3- removal, minimizing biological sludge production as much as possible (see the theoretical sludge yields of the relevant reactions in Table 7.9). Stoichiometric study has showed that biological sludge production of this new BNR can potentially be 1/10 of conventional BNR (Lu et al., 2012b). In this novel process, organic carbon is oxidized to CO2 by SRB which increases the reactor pH to up to 8.0 at which the vast majority of H2S generated from the anaerobic reaction dissolves in the aqueous phase of the sulphate-reducing bioreactor (Poinapen and Ekama, 2010a). This thereby provides an adequate amount of dissolved sulphide (the electron donor) for subsequent autotrophic denitrification, during which sulphide is converted back to SO42- by SOB. The TDSd residue, if any, could be completely oxidized to sulphate during aerobic nitrification. From the electron transfer point of view, the SANI® process extends a carbon-nitrogen-cycle-based BNR process into a sulphur-carbon-nitrogen-cycle-based BNR process (see Figure 7.9b), which offers an opportunity for sludge-minimized treatment of saline and brackish or sulphur-laden wastewater.

## Slide 6: Principles of the SANI® process
Notes: The SWTF practice results in, on average, 167 mgSO42--S/l and 5,000 mgCl-/l in Hong Kong saline sewage (Van Loosdrecht et al., 2012), inevitably causing odour issues in the sludge treatment. An ideal solution is to minimize sludge production. Based on this rationale, a novel sulphur-based process for saline wastewater treatment, namely the SANI® process, was developed by the authors from lab-, pilot- and full-scale studies between 2004 and 2017 (Lau et al., 2006; Wang et al., 2009; Lu et al., 2012b; Wu et al, 2016). Comparison between the conventional biological nitrogen removal (BNR) process and the SANI® process in terms of process concept and reactions are shown in Figure 7.9 and Table 7.9, respectively.
Since the introduction of the nitrogen removal process in the 1960s, biological wastewater treatment has relied on the electron flow from organic carbon to oxygen through an integrated carbon and nitrogen cycle, as shown in Figure 7.9a. However, the conventional BNR process generates a large quantity of excess sludge due to high theoretical sludge yields resulting from organics removal by aerobic and anoxic oxidation (more details in Table 7.9). In contrast, the SANI® process integrates anaerobic organic removal by sulphate reduction and anoxic nitrogen removal by autotrophic denitrification for NO3- removal, minimizing biological sludge production as much as possible (see the theoretical sludge yields of the relevant reactions in Table 7.9). Stoichiometric study has showed that biological sludge production of this new BNR can potentially be 1/10 of conventional BNR (Lu et al., 2012b). In this novel process, organic carbon is oxidized to CO2 by SRB which increases the reactor pH to up to 8.0 at which the vast majority of H2S generated from the anaerobic reaction dissolves in the aqueous phase of the sulphate-reducing bioreactor (Poinapen and Ekama, 2010a). This thereby provides an adequate amount of dissolved sulphide (the electron donor) for subsequent autotrophic denitrification, during which sulphide is converted back to SO42- by SOB. The TDSd residue, if any, could be completely oxidized to sulphate during aerobic nitrification. From the electron transfer point of view, the SANI® process extends a carbon-nitrogen-cycle-based BNR process into a sulphur-carbon-nitrogen-cycle-based BNR process (see Figure 7.9b), which offers an opportunity for sludge-minimized treatment of saline and brackish or sulphur-laden wastewater.

## Slide 7: SANI® process development: laboratory case study
To prove the SANI® process concept, a laboratory study was conducted in Hong Kong. The influent contained 265 mgCOD/L (mainly glucose, CH3COO- and yeast extract), 30 mgNH4+-N/L, 400-600 mg/L of SO42- and 3,000-4,000 mg/L of salinity, similar to the effluent quality of a primary sedimentation tank at a typical saline sewage biological treatment plant in Hong Kong.
Notes: To prove the SANI® process concept, a laboratory study was conducted. The influent contained 265 mgCOD/l (mainly glucose, CH3COO- and yeast extract), 30 mgNH4+-N/l, 400-600 mg/l of SO42- and 3,000-4,000 mg/l of salinity, similar to the effluent quality of a primary sedimentation tank at a typical saline sewage biological treatment plant in Hong Kong.
In this system, organic carbon is first oxidized to CO2 by SRB in the sulphate-reducing up-flow sludge blanket (SRUSB) (Reactor 1). This process subsequently increases the pH to an alkaline level (>7.5-8) due to sulphate (strong acid) being reduced to sulphide (weak acid), dissolving the product hydrogen sulphide in water mainly in the form of TDSd for autotrophic denitrification in the subsequent anoxic bio-filter (Rector 2), where NO3- is reduced to N2. Through this reaction dissolved sulphide will be converted back to SO42- by SOB. The remaining NH4+ and residual sulphide are oxidized to NO3- and SO42- during nitrification in the aerobic bio-filter (Reactor 3), of which effluent is recirculated to Reactor 2 for nitrogen removal at a recirculation rate of 3Q (Q = influent flow rate), similar to a conventional biological nitrogen removal process.
To enable the three bio-reactions (see eqs. 7.18, 7.19 and 7.20) to carry out individually and effectively, Reactor 1 adopted a typical up-flow anaerobic sludge blanket, and Reactors 2 and 3 were packed with polypropylene plastic media (specific surface area: 215 m2/m3) for biofilm development. The system achieved 95 % COD, 99 % NO3-, and 74 % TN removal without excess sludge withdrawal throughout the entire operation period (Wang et al., 2009). The HRT of the aerobic and anoxic bio-filters and the recirculation ratio (R) between these two reactors played an important role in achieving the efficient performance of pollutant removal and sludge minimization. To further understand this novel process, a steady-state model was developed from COD, nitrogen and sulphur mass and charge (electron) balances as well as stoichiometries of sulphate reduction, autotrophic denitrification and autotrophic nitrification (Lu et al., 2009). The modelling approach is detailed in Section 7.4.4. In principal the model prediction agreed well with the measured data in terms of the removal of COD, NO3- and SO42-, sulphide production, and effluent total suspended solids (TSS). The mass balance analyses of COD, sulphur and nitrogen in the three reactors provided a good cross-check for the experimental findings and modelling results. The main performance of the lab-scale SANI® system is summarized in Table 7.10.

## Slide 8: SANI® process development: pilot case study
In order to further demonstrate the feasibility of the SANI® process, a pilot-scale study was further conducted with 10 m3/d of real saline sewage mainly from Hong Kong International Airport. The SANI® pilot plant was continuously operated for 225 days at steady state and achieved average 87% COD, 87% TSS and 57% TN removal. (low nitrogen removal efficiency was mainly attributed to the high fraction of non-biodegradable soluble organic nitrogen (NSON) in the incoming sewage). About 90 % of biological sludge reduction was achieved and no sludge was purposely withdrawn during 225-day plant operation.
Lu et al., 2011; 2012

## Slide 9: SANI® process development: large scale demonstration
Based on the experience of the pilot-scale study, the SANI® process was scaled up to 1,000 m3/d to demonstrate its application potential in Hong Kong.
The demonstration plant confirmed that a total HRT of 12-13 h is feasible; reduced 60-70 % of the sludge production in comparison with the local WWTPs.
Notes: Based on the experience of the pilot-scale study, the SANI® process was scaled up to 1,000 m3/d to demonstrate its application potential in Hong Kong. It was built in two vacated rectangular primary sedimentation tanks (SD1 and SD2) at the Sha Tin Wastewater Treatment Works (STWTW) in collaboration with the local wastewater board: the Hong Kong Drainage Services Department (DSD) (see Figure 7.12 and Table 7.12). The demonstration plant consisted of four SRUSB reactors (green) for organic removal in SD1 and one MBBR for nitrogen removal in SD2. In the MBBR, autotrophic denitrification accounted for 54 % reactor space and nitrification occupied 46 % reactor space. MBBR is a compact technology for wastewater treatment. In this plant, degritted raw saline wastewater passed through 6 mm coarse screen bars and then a fine-mesh sieve (FMS, 350 µm) to replace the primary treatment. Part of the MBBR effluent was further treated by chemical coagulation and settled as a post-treatment option for demonstration purpose (for example, dosed with 12 mgAl/l alum and 1 mg/l anion polymer and operated at 1 h HRT). Later, the full effluent was treated by dissolved air flotation. It should be noted that TSS in the effluent of MBBR was 40-80 mgTSS/l on average, significantly lower than a conventional MBBR system, e.g. around 200 mgTSS/l (Ødegaard, 2006), attributable to the significant sludge minimization of the SANI® process.
The demonstration plant was continuously operated between 2013-2017, in the following phases: a) the plant start-up period (Phase I: days 1-125); (b) a steady-state period with an average flow rate of 800 m3/d (Phase II: days 126-213); and c) a dynamic operation period with a diurnal peaking factor of 1.3 at an average flow of 720 m3/d, i.e. maximum flow approaching 1,000 m3/d (Phase III: days 214-250), as detailed in Table 7.12. Later on, the demonstration plant was operated in a continuously flowrate of 1,000 m3/d approximately. The demonstration plant confirmed that a total HRT (nominal) of 12-13 h is feasible, which would reduce 30- 40 % of the total HRT of conventional BNR systems at the local WWTPs.
The average effluent quality (including post-treatment) is: 15±5 mgTSS/l, 5.6±1.8 mgBOD5/l, 8.4±1.6 mgTN/l, and 0.9±0.3 mgTP/l (see Table 7.13). The (biological) sludge production rate was determined to be 0.35±0.08 gTSS/gBOD5 (or 0.19±0.05 gTSS/gCOD). The demonstration plant reduced 60-70 % of the sludge production in comparison with the local WWTPs (0.9-1.3 gTSS/gBOD5).