## Slide 1
Course on Wastewater Disinfection
Background/Introduction
Ernest R. Blatchley III
Lyles School of
Civil Engineering
Environmental and
Ecological Engineering

## Slide 2: Wastewater Disinfection: History
1893: Chlorination applied in Hamburg, Germany
1906: Ozone applied in France
1909: Liquid chlorine becomes available
1916: UV applied in France
1961: Chlorine residual controllers
1970s-1980s: Open-channel UV systems, EPA support
Use of peracids
Image from: https://www.mercurynews.com/2011/11/09/end-of-chlorine-gas-at-silicon-valleys-largest-sewage-treatment-plant/
Sources:
Lofrano and Brown (2010) “Wastewater Management Through the Ages: A History of Mankind,” Science of the Total Environment, 408, 5254-5264.
Whitby and Scheible (1984) “The History of UV and Wastewater,” IUVA News, 6, 3, 15-24.

## Slide 3: Wastewater Disinfection: Goals
Reduce concentration of viable or infective wastewater pathogens
Reduce human exposure to viable or infective wastewater pathogens
Reduce the risk of disease transmission associated with wastewater pathogens
Image from: https://www.cdc.gov/ncezid/dfwed/pdfs/nat-covis-surv-overview-508c.pdf
Image from: https://www.cdc.gov/parasites/crypto/index.html
Image from: https://phil.cdc.gov/details.aspx?pid=10010
Vibrio
cholerae
Cryptosporidium
parvum
Adenovirus

## Slide 4: Disinfection Requirements
Required extent of inactivation influenced by:
  Influent quality
  Quality of undisinfected wastewater (upstream treatment)
  Intended uses of disinfected wastewater
Wide range of intended uses
  Surface water discharge (no contact or contact)
  Irrigation (non-edible, edible crops)
  Direct potabilization
Image from: https://www.acs.org/pressroom/newsreleases/2013/september
Image from: https://www.pub.gov.sg/watersupply/fournationaltaps/newater

## Slide 5: Disinfection ≠ Sterilization
Disinfection
Inactivation of viable or infective pathogens
Often involves reduction of ≥ 3 log10 units of resistant pathogens
Sterlization
“Complete” elimination of all microbes
Sometimes referred to as process that yields reduction of ≥ 6 log10 units of resistant pathogens
Image adapted from: https://foodsafepal.com/wp-content/uploads/2022/12/sanitization-vs-disinfection-vs-sterilization-1024x474.webp

## Slide 6: Disinfection is not Always Applied
Omitted in many countries
  Dilution
  Natural attenuation
Applied seasonally in some temperate locations
  Goal is to minimize human contact, disease transmission
  Minimal direct contact in cold-weather months
Image from: https://naturemuseum.org/2021/02/what-happens-to-the-chicago-river-in-the-winter/
Image from: https://www.choosechicago.com/blog/arts-culture-entertainment/10-things-you-should-absolutely-do-on-the-chicago-riverwalk/

## Slide 7: Principles of Wastewater Disinfection Extend to Other Media
Drinking water
Swimming pools
Ballast water
Food processing
Surfaces
Medical devices
Air

## Slide 8: Summary
Wastewater disinfection is practiced to reduce the risk of disease transmission associated with wastewater pathogens
Common disinfectants include:
  Chlorine
  Ultraviolet radiation
  Peracetic acid
Wastewater disinfection processes are variable, depending on location, season, intended uses of treated water
Principles of disinfection extend to other media