## Slide 1
Course on Wastewater Disinfection
DBP Formation, Implications for Toxicity
Ernest R. Blatchley III

## Slide 2
Disinfection Byproducts (DBPs)
Disinfectants promote inactivation of microbial/viral pathogens
Reactions that lead to microbial/viral inactivation are diverse, usually involve damage to one or more critical biomolecules
  Nucleic acids
  Proteins
  Enzymes
Disinfectants also promote other reactions, some of which lead to formation of DBPs, degradation of other compounds
Some DBPs are hazardous to human health and/or the environment
Risks posed by microbial/viral pathogens tend to be acute
Risks posed by DBPs tend to be chronic
Acceptable concentrations of these agents must be determined by balance between risks
Current regulations and practice focus on DBPs in drinking water, but the same principles can (should) be applied in municipal wastewater disinfection
Image from: https://www.pitara.com/science-for-kids/
5ws-and-h/how-do-humans-balance-on-two-legs/

## Slide 3: Reasons to Consider DBP Formation in Wastewater
Chemistry responsible for DBP formation is not unique to drinking water
Precursor concentrations in wastewater are often higher than in drinking water supplies
Wastewater discharges are part of the hydrologic cycle (“we all live downstream”)
Effluent toxicity

## Slide 4
Nature of DBPs
Depend on source water composition
  Surface water
  Groundwater
Depend on disinfectant
  Chlorine
  Ozone
  UV
  Combinations
Depend on intended uses of water
  Potable
  Wastewater discharge
  Wastewater reuse
  Swimming/recreation
Image from: https://www.membratec.ch/
water/ideal-drinking-water-116.html
Image from: https://www.lecanadian.com/
headline-news/wastewater-discharge-
streams-can-lead-rapid-antibiotic-resistance-
bacterial-infections-disease.html
Image from: https://www.suez.com/en/
our-offering/local-authorities/
what-are-you-looking-for/water-
management/wastewater-treatment-
and-reuse/reuse-wastewater

## Slide 5
DBPs from Chemical Disinfectants
Images adapted from: Richardson, S.L. (2002) “The role of GC-MS and LC-MS in the discovery of
drinking water disinfection by-products,” Journal of Environmental Monitoring, 4, 1, 1-9.
Fraction of Total Organic Halogen (TOX)
Fraction of Assimilable Organic Carbon (AOC)

## Slide 6
Common DBPs, Sentinel Compounds
Trihalomethanes (TTHMs)
Haloacetic acids (HAA5)
TTHMs and HAA5 represent a large fraction of known DBPs
Variable in their toxicity
Brominated forms tend to be more toxic than analogous chlorinated forms
Large fraction of toxicity associated with other DBPs
In some respects, regulated DBPs are indicator chemicals

## Slide 7
Other DBPs
N-nitrosamines (e.g., NDMA)
Extremely potent carcinogen
  Notification (CA): 10 ng/L
  Public health goal (CA): 3 ng/L
Difficult to remove by air stripping, adsorption
Effectively degraded by UV
Bromate
Formed by reactions with strong oxidants (especially O3), bromide
Carcinogen
  EPA Maximum Contaminant Level (MCL) = 10 g/L
  WHO Guideline = 10 g/L

## Slide 8: Chloramine Photolysis
N-Cl bond is photolabile
N-Cl bond photolysis yields reactive intermediates
Other bonds are susceptible to photodecay
Photochemistry, secondary chemistry can be important
Images from: Blatchley (2023) Photochemical Reactors: Theory, Methods, and Applications of Ultraviolet Radiation, Wiley, Hoboken, NJ.

## Slide 9: Chlorine/UV Application to Amino Acids
Images from: Weng and Blatchley (2013) “Ultraviolet-Induced Effects on Chloramine and Cyanogen Chloride Formation from Chlorination of Amino Acids,” Environmental Science & Technology, 47, 9, 3943-4960.
Glycine
L-Arginine
L-Histidine
CNCl

## Slide 10: Summary
All disinfection processes have the potential to alter chemical composition, toxicological consequences
Disinfection processes require a balance between risks associated with microbial pathogens and chemical contaminants
Most DBPs are undefined; we rely on sentinel DBPs
Disinfection processes can alter toxicity (improvement or degradation)
Designers of disinfection systems should be aware of implications beyond inactivation of pathogens