## Slide 1
Course on Wastewater Disinfection
Disinfection Applications, Case Studies
Ernest R. Blatchley III
Lyles School of
Civil Engineering
Environmental and
Ecological Engineering

## Slide 2: Metropolitan Water Reclamation District of Greater Chicago (MWRD)
Seven water reclamation facilities: treat roughly 450 x 109 gallons (1.7 x 109 m3) per year
Long history of creativity
Thought leaders in wastewater management
Tunnel and Reservoir Plan (TARP), aka “Deep Tunnel” project
Challenged conventional thinking on disinfection
Image from: https://news.wttw.com/2020/11/04/behind-scenes-virtual-tour-showcases-mwrd-work-chicago-river-reversal
Image from: https://mwrd.org/tunnel-and-reservoir-plan-tarp

## Slide 3: Timeline of MWRD Decisions Related to Effluent Disinfection Information from Leu-Hing et al. (1984) Wastewater Disinfection: A Review of Technical and Legal Aspects in Illinois, WPCF Pre-Conference Workshop, New Orleans, LA
1972 – Illinois Pollution Control Board (IPCB) adopts year-round effluent and water quality standards for Fecal Coliforms
  Effluent: 400 cfu/100 mL
  Water Quality: 200 cfu/100 mL
1974 – Chlorination initiated at MWRD facilities
1975 – Fish kills observed in receiving streams; adverse health effects associated with chlorination DBPs
1976 – US EPA deletes Fecal Coliform standard from definition of 2° treatment
1977 – Illinois EPA proposes revisions to effluent and water quality standards

## Slide 4: Timeline of MWRD Decisions Related to Effluent Disinfection Information from Leu-Hing et al. (1984) Wastewater Disinfection: A Review of Technical and Legal Aspects in Illinois, WPCF Pre-Conference Workshop, New Orleans, LA
EPA decision on Fecal Coliform standards:
“The benefits achieved by disinfection should be weighed against the environmental risks and costs. It is intended that the use of chlorine disinfection would be considered only when there are public health hazards to be controlled. The exclusive use of chlorine for disinfection should not be continued where protection of aquatic life is of primary consideration.”
Illinois EPA proposed revisions to water quality standards
  No waterborne disease outbreaks were traceable to wastewater discharge, before or after initiation of chlorination
  Fecal coliforms are poor indicators; chloramines are ineffective against viruses
  Adverse effects of chlorine on aquatic life; toxicity of free/combined chlorine and DBPs
  Alternatives to chlorine were emerging; UV and ozone

## Slide 5: MWRD Research
Chlorination yielded little or no change in receiving stream microbiology at 1st downstream withdrawal location (Peoria, IL; 150 miles [240 km])
  Bacteria
  Enteric viruses
Chlorination had adverse effects of aquatic life downstream of discharge
Economic analysis indicated that costs of disinfection far outweighed benefits
1982 IPCB Decision
Effluent disinfection required only when discharge was within 20 miles (30 km) upstream of:
  Public water supply
  Food processing supply
  Licensed bathing beach, during swimming season (May 1 – November 15)

## Slide 6: MWRD Facilities, Current Status
Facility Name | Avg Flow MGD (m3/hr) | Disinfection | Receiving Stream
Calumet | 354 (56,000) | Chlor/Dechlor | Little Calumet River
John E. Egan | 30 (4700) | Chlor/Dechlor | Upper Salt Creek
Hanover Park | 12 (1900) | Chlor/Dechlor | DuPage River
James C. Kirie | 52 (8200) | Chlor/Dechlor | Higgins Creek
Lemont | 2.3 (360) | Chlor/Dechlor* | Chicago Sanitary and Ship Canal
Terrence J. O’Brien | 230 (36,000) | UV | North Shore Channel
Stickney | 1200 (190,000) | None | Chicago Sanitary and Ship Canal
*Wet weather flow is disinfected at the Lemont WRP

## Slide 7: Stickney WRP
Largest wastewater treatment facility in the world
Capacity: 1.44 BGD (227,000 m3/hr)
No disinfection
“The IEPA conducted a thorough use attainability analysis of the Chicago Area Waterway System and determined that the Chicago Sanitary and Ship Canal, where the Stickney WRP discharges, was not designated as primary contact and therefore, disinfection at the Stickney WRP is not necessary.”
Image from: https://legacy.mwrd.org/irj/portal/anonymous/stickney

## Slide 8: Chicago Sanitary and Ship Canal
Completed in 1900; ~45 km long
Reverses flow in Chicago River
Diverts wastewater discharge from Lake Michigan to Mississippi River watershed
Allows commercial ships to move from Great Lakes to Mississippi River waterway
Images from: https://www.loc.gov/resource/hhh.il0976.sheet/?sp=2&st=image
Image from: https://www.smith-root.com/barriers/sites/chicago-sanitary-and-ship-canal-2a

## Slide 9: Pure Water Southern California
Partnership between Metropolitan Water District of Southern California and the Los Angeles County Sanitation Districts
Objective: augment existing water supplies with reclaimed wastewater
Target = 150 MGD (24,000 m3/hr)
Region characterized by
  Intense droughts
  Rapidly expanding human population
Grace F. Napolitano Pure Water Southern California Innovation Center
Information and image from:
https://www.mwdh2o.com/building-local-supplies/pure-water-southern-california/

## Slide 10: Grace F. Napolitano Pure Water Southern California Innovation Center
Stage 1: Membrane Bioreactors
Stage 2: Reverse Osmosis
Stage 3: UV/AOP (Cl:UV or H2O2/UV)
Images from: https://www.mwdh2o.com/building-local-supplies/pure-water-southern-california/
Comprehensive treatment
Removal or alteration of most dissolved, particulate pollutants
Extensive disinfection (99.9999% removal or inactivation)
Degradation of micropollutants, PPCPs, etc.

## Slide 11: Summary
Wastewater disinfection is needed when human exposure to wastewater pathogens is likely (i.e., not all situations)
MWRD (Chicago) has been a thought leader in wastewater management, including disinfection
Increasing demand for water promotes reuse (up to and including direct potabilization)