## Slide 1
Course on Wastewater Disinfection
Contact Chamber Design
Ernest R. Blatchley III
Lyles School of
Civil Engineering
Environmental and
Ecological Engineering

## Slide 2
Efficacy of Chemical Disinfection Processes
Treatment objectives often call for 3-6 log10 units of inactivation
Process behavior governed by combined effects of:
  Transport processes
  Mixing behavior
  Intrinsic kinetics
Process requirements mandate efficient hydrodynamics
  Approach plug flow
  Minimize short-circuiting, dead zones
Narrow Residence Time Distribution (RTD)
  Tracer testing
  CFD
Image from: Angeloudis et al. (2015) “Predicting the
disinfection efficiency range in chlorine contact tanks
through a CFD-based approach, Water Research, 60, 188-129.

## Slide 3: Numerical Simulation of Disinfection Process Dynamics
Image from: https://navier-flow-
consultants.com/chlorine-contact-tanks/

## Slide 4
Other Chemical Disinfectant Contact Chambers
Image from: Bin, A.K. and Roustan, M. (2000) “Mass Transfer
In Ozone Reactors,” Proceedings, Fundamental and Engineering
Concepts for Ozone Reactor Engineering, Toulouse, France, 99-131.
Deep U-Tube
Image from: https://www.thewatertreatments.com/disinfection/chlorinators/
Long, Straight Pipe
Depth > 10 m

## Slide 5
CFD Simulations
Numerical simulations
  Equations of motion, continuity
  Turbulence closure model
  Reaction terms
Define geometry, operating conditions of reactor
Provides detailed descriptions of transport behavior
Can be important for accurate simulations of disinfection efficacy
Applied to a wide range of disinfectants
Image from: Wei et al. (2020) “Development of a CFD-Based Artificial Neural
Network Metamodel in a Wastewater Disinfection Process with Peracetic Acid,”
Journal of Environmental Engineering, ASCE, 146, 12: 04020140.

## Slide 6: Chemical Disinfection Contact Chamber Characteristics
Principles are generally applicable to chemical disinfection systems
Long, narrow reactors approach plug flow conditions
Serpentine reactors provide benefits
  Common internal walls
  Lower construction costs
  Smaller footprint
Turns introduce dead zones
Designs involving few, long channels preferred (narrow RTD)
Disinfectant
Disinfectant

## Slide 7
Characteristics of UV Disinfection Systems
Image from: Ahmed, Y.M.; Jongewaard, M; Li, M.; Blatchley III, E.R. (2018) “Ray Tracing for Fluence Rate Simulations in Ultraviolet Photoreactors,” Environmental Science & Technology, 52, 8, 4738-4745.
Strong spatial gradients in local fluence rate
  Equally strong spatial gradients in local photochemical reaction rate
  Not uncommon to see variation of E (reaction rate) of 10-100x over a distance of 5-10 cm
Operate in turbulent regime
Some particles will receive a large UV dose
  Trajectory close to a lamp
  High fluence rate, low velocity (long exposure time)
Some particles will receive a small UV dose
  Trajectory no close to a lamp
  Low fluence rate, high velocity (short exposure time)
Simulations of reactor performance often conducted by CFD + Fluence Rate Field Model + Kinetic Model

## Slide 8: Dose Distribution Function
“Dose” (aka Fluence) is the Master Variable in photochemical reactors (not time)
For an individual particle, UV dose received depends on trajectory through the irradiated zone
  Particles that pass close to UV source will receive large dose
  Particles that do not come close to a source will receive small dose
Process performance depends on the dose distribution
Image courtesy of Trojan Technologies, Inc.

## Slide 9
Flow Field Simulation

## Slide 10
Velocity Contours

## Slide 11
Dose Calculation Lagrangian Numerical Model

## Slide 12: UV Disinfection System Characteristics
Process performance (disinfection efficacy) depends on:
  Influent target concentration
  Intrinsic kinetics of target inactivation
  Dose distribution
Hydraulic behavior can be critical with open-channel systems
  Free surface changes (head loss)
  Stepped channels can be used
  Downstream control of liquid level
    “Flap gate”
    Elongated weir

## Slide 13: Multi-Channel Systems: Influent Distribution
Large systems often involve multiple channels
  Flow variability
  Maintenance
  Redundancy
Uniform distribution among “active” channels is critical to performance
Inclusion of flow resistance at upstream end (momentum distribution)
Similar to “flow straighteners” used in wind tunnels
Images courtesy of Malcolm Pirnie/ARCADIS, Indianapolis, IN

## Slide 14: Summary
Contemporary analysis and design of disinfection systems is based on numerical simulations
  Transport behavior, mixing
  Disinfection kinetics
  Chemical, biochemical, photochemical reactions
Contact chambers for chemical disinfection (chlorine, PAA) should promote plug-flow conditions
  Low dispersion number
  Narrow RTD
UV photoreactor performance is governed by UV dose distribution
  Narrow dose distribution is desirable
  Reactor design is generally conducted by manufacturers based on CFD-E field modeling