## Slide 1
Course on Wastewater Treatment Development
Future Directions
Ernest R. Blatchley III

## Slide 2: Mixed Disinfectants
PAA + Chlorine
  Common contact chamber
  Synergistic disinfection
  PAA stability
Chlorine + UV
  Different mechanisms of inactivation
  Complementary disinfection
  Advanced oxidation
  Diurnal, seasonal variations in flow rate
PAA + UV
  Different mechanisms of inactivation
  Complementary disinfection
  Advanced oxidation
  Diurnal, seasonal variations in flow rate
Some processes involve formation of reactive intermediates (radicals)
Image from: Guo et al. (2022) “UV/Chlorine Process: An Efficient Advanced Oxidation Process with Multiple Radicals and Functions in Water Treatment,” Accounts of Chemical Research, 55, 286-297.
Image from: Zhang and Huang (2020) “Modeling the Kinetics of UV/Peracetic Acid Advanced Oxidation Process, Environmental Science & Technology, 54, 7579-7590.

## Slide 3: Water Reuse
Increasing water demand
  Population growth
  Urbanization
  Climate change
Increased reliance on water supplies of marginal quality
Alteration of hydrologic cycle
  Recovery, reuse of marginal water supplies
  Requires enhanced treatment
    Particles – physical separation
    Micropollutants – chemical transformation (AOPs, ARPs)
    Microbial pathogens – disinfection
Wastewater effluents can represent a reliable water source
Image from: www.epa.gov/waterreuse/basic-information-about-water-reuse

## Slide 4: Stochastic Analysis
Input parameter variability: flow rate, transmittance, lamp power, number of operating channels
Examine effects of input parameter variability on process performance
Predict variability of process performance
Optimize system performance
  Operating conditions required to meet treatment requirements
  Minimize cost
  Improve reliability
Similar approaches have been developed for other disinfectants
Relevant for large, municipal facilities
Case# | Flow (m3/hr) | NCh | NB/channel | Flow/Channel (m3/hr/channel) | Velocity (m/s)
1 | 7880 | 7 | 1 | 1120 | 0.15
2 | 23,600 | 7 | 1 | 3370 | 0.47
3 | 7880 | 7 | 2 | 1120 | 0.15
4 | 23,600 | 7 | 2 | 3370 | 0.47
Operating conditions tested in Monte Carlo simulations.
From: Ahmed, Y.M.; Ortiz, A.P.; Blatchley III, E.R. (2019) “Stochastic Evaluation of Disinfection Performance in Large-Scale, Open-Channel, UV Photoreactors,” Journal of Environmental Engineering, ASCE, 145, 10, Article number 04019071.

## Slide 5: Conventional Sources of UV-C Radiation
UV is a common alternative to chlorination/dechlorination
Most UV systems are based on mercury vapor lamps
  Low pressure (254 nm)
  Medium pressure (polychromatic)
Electrically efficient sources for UV-C generation, but …
Concerns about the presence of Hg
  Toxicity
  Minamata Convention
Data courtesy of Trojan Technologies

## Slide 6: Alternative UV-C Source: UV LEDs
Output spectrum depends on diode composition
LED output is “selectable”
Current devices are
  Relatively low output power
  Relatively low wall plug efficiency
Advantages
  Instant on/off
  Selectable output wavelength(s)
  Directional devices
Future: rapid improvements in power, efficiency, cost
Image from: https://led-ld.nichia.co.jp/en/product/uv_uvc.html
Data provided by AquiSense

## Slide 7: Alternative UV-C Source: Excimer Lamps
Output spectrum depends on excimer composition
Excimer lamp output is “selectable”
Current devices are
  Relatively low output power
  Relatively low wall plug efficiency
Advantages
  Instant on/off
  Selectable output wavelength(s)
  Different lamp geometries
Future: rapid improvements in power, efficiency, cost
From: Blatchley III, E.R. (2023) Photochemical Reactors: Theory, Methods and Applications of Ultraviolet Radiation, Wiley, Hoboken, NJ, ISBN: 978-1-119-87130-9.
Source: https://www.ushio.com/product/care222-filtered-far-uv-c-excimer-lamp-module/
From: Kim et al. (2022) Plasma Processes and Polymers, 19, 10, 2200075.

## Slide 8: Summary
Many opportunities for creativity, innovation with disinfection
Mixed disinfectants
  Multiple disinfection mechanisms
  Applications for simultaneous control of chemical contaminants
Stochastic analysis
  Application of contemporary simulation tools
  System optimization (reliability and cost)
Alternative sources of UV radiation
  LEDs
  Excimer lamps