## Slide 1
Course on Wastewater Disinfection
Microbial Indicators
Ernest R. Blatchley III
Lyles School of
Civil Engineering
Environmental and
Ecological Engineering

## Slide 2: Wastewater Microbiology
Viruses
Bacteria (vegetative cells, spores)
Protozoa (including resting stages)
Yeasts
Algae
Most are non-pathogenic
Some are pathogenic
Impractical/impossible to measure entire inventory
“Indicator” organisms are used as an index of microbial quality
Effluent concentration of indicator(s) of forms the basis for disinfection system design
Image from: Gutzeit, G & DA, Lorch & Weber, A & Engels, M & Neis, Uwe. (2005). “Bioflocculent algal-bacterial biomass improves low-cost wastewater treatment.” Water Science and Technology, 52. 9-18. 10.2166/wst.2005.0415.

## Slide 3: Characteristics of Ideal Indicators
Common to (undisinfected) wastewater samples
Non-pathogenic to humans
Simple, inexpensive, rapid to quantify using culture-based methods
Presence (absence) correlates strongly with presence (absence) of pathogens
At least as resistant to disinfectants as pathogens
A measure of the risk of exposure to microbial pathogens
Image from: Forster, B. and Pinedo, C.A. (2016) Bacterial Examination of Waters: Membrane Filtration Protocol, American Society for Microbiology, 15 pp.

## Slide 4: Common Bacterial Indicators
Coliform bacteria
  Total coliforms
  Fecal coliforms
  E. coli
Enterococcus
  For discharge to marine or brackish water
Indicator should be consistent with intended use of discharged water
Quantification by culture-based methods
  Membrane filtration
  Fermentation tubes (MPN)
Image from: https://doh.wa.gov/community-and-environment/drinking-water/contaminants/coliform
Image from: https://www.epa.gov/national-aquatic-resource-surveys/indicators-enterococci

## Slide 5
Non-Bacterial Indicators: Bacteriophage
Abundant and more persistent than bacteria
Indicators of viral contamination
Culture-based infectivity assays are safe, relatively simple (plaque assay)
Tend to be more resistant to disinfectants than bacteria
F-specific coliphages
Somatic coliphages
Structurally similar to human pathogenic viruses
Responses to disinfectants similar to human viruses
  Often slightly conservative relative to human pathogens
  Human Norovirus (HNV)
Image from: https://newscenter.lbl.gov/wp-content/uploads/2020/12/Phage-colored.jpg

## Slide 6
Summary
Broad spectrum of microorganisms in wastewater
Indicators are used as an index of microbial water quality
Common bacterial indicators
  Coliforms
  Enterococcus
Bacteriophage as an alternative to bacterial indicators
Effluent concentration of viable/infective indicator(s) often forms the basis for disinfection system design