## Slide 1
Course on Wastewater Disinfection
Disinfection with Halogens, Mechanisms and Kinetics
Ernest R. Blatchley III

## Slide 2
Mechanisms of Disinfection: Chlorine
Chemical damage to critical biomolecules, structures
  Proteins, nucleic acids, enzymes
  Membranes, pili
Microbial/viral inactivation
  Bacteria: colony formation
  Viruses: infection of host cell
  Protozoa: infection of host cell
  Algae: cell reproduction
Chemical damage and viability are not identical, but related
Extent of inactivation depends on disinfectant dose:
Image from: Nescerecka et al. (2015) “Behavior and stability of
adenosine triphosphate (ATP) during chlorine disinfection,”
Water Research, 101, 490-497.
= dose rate (disinfectant concentration)
= time
= period of exposure

## Slide 3
Disinfection Process Behavior
Dose (distribution) required to meet a treatment objective depends on:
Treatment objective (e.g., discharge to environment, wastewater reuse [irrigation], augmentation of potable water supply, etc.)
Target pathogens
Disinfectant (water chemistry, pH, etc.)
Hydrodynamics, transport behavior
Peripheral reactions
  Disinfectant “demand”
  DBP formation

## Slide 4
Disinfection Kinetics
Harriette Chick (1908)
Assumed disinfection kinetics could be described using logic applied to elementary, bimolecular reactions
= microorganism
= disinfectant
= inactivated microorganism
Herbert Watson (1908)
Re-examined Chick’s data, proposed a slight modification
= coefficient of specific lethality
= disinfectant concentration
= time
=empirical constant
Chick-Watson (pseudo-first-order) model is often used to describe disinfection kinetics

## Slide 5
Chick-Watson Kinetics
If are constants, then by separation of variables:
Extent of inactivation is governed by the disinfectant dose, or more formally:
0
0

## Slide 6
Ct Concept
Has its origin in Chick-Watson
Used for design and regulation of disinfection systems
  Focuses exclusively on intrinsic kinetics
  Ignores deviations from 1st-order behavior
  Ignores the effects of transport behavior and mixing
“Ct Tables” have been developed for many combinations of microbial target and disinfectant (largely focused on drinking water disinfection)
Table from: Disinfection Profiling and Benchmarking Guidance Manual,
USEPA, Office of Water, Cincinnati, OH, EPA 815-R-99-013.

## Slide 7
Summary
Chlorine is a broad-spectrum antimicrobial agent that causes microbial inactivation via several mechanisms
  Effective for inactivation of vegetative bacteria, viruses
  Limited effectiveness against bacterial spores, protozoan parasites
Disinfection kinetics represent an important component of disinfection system design
Chick-Watson model, based on 1st-order kinetics, represents the fundamental model of disinfection kinetics
Chick-Watson model represents the foundation of the “Ct Concept”