## Slide 1
Course on Wastewater Disinfection
Disinfection with UV Radiation, Laws of Photochemistry
Ernest R. Blatchley III

## Slide 2
Electromagnetic Spectrum
Electromagnetic radiation: energy that propagates through space
  Wave characteristics: energy is inversely related to wavelength
  Particle characteristics: energy is available in discrete units (photon or quantum)
  “Wave-particle duality”
Visible light:
Ultraviolet radiation:
  UV-A:
  UV-B:
  UV-C:
  VUV:
Image from http://www.albatrossuv.com/UV-Spectral-Output.php

## Slide 3
Laws of Photochemistry
First law of photochemistry (Grotthus-Draper Law): radiation (photons) must be absorbed by a molecule (atom or ion) to bring about a photochemical change.
Second law of photochemistry (Stark-Einstein Law, aka photochemical equivalence law): for each photon absorbed by a chemical system, only one molecule is activated for a photochemical (or photophysical) process.
  Photons (quanta) interact with at most one molecule
  Avogadro’s number of atoms/molecules/ions  1 mole
  Avogadro’s number of photons  1 einstein
  Molecules and photons are “equivalent” participants in photochemical reactions
Third law of photochemistry (Bunsen-Roscoe Law, aka law of reciprocity): the extent of a photochemical reaction will be governed by the dose (fluence) of radiation absorbed by the target, independent of the time required to deliver that dose.

## Slide 4
Implications of the Laws of Photochemistry
A photochemical reaction may take place iff:
  Radiation (photons) of an appropriate wavelength is (are) available
  Radiation (photons) is (are) absorbed by the target molecule
What is required for radiation to be “appropriate”?
  Photon energy meets or exceeds the energy of chemical bonds that will be broken, or formed
  Photons must be absorbed by target molecule
= photon energy [=]
= Planck constant =
= frequency of radiation [=] Hz or s-1
= speed of light in vacuum =
= wavelength of radiation [=] nm
= energy per einstein at wavelength  [=]
= Avogadro’s number =

## Slide 5
Photon Energy vs. Bond Energy
Photon energy must meet or exceed bond energy for a photochemical reaction to take place
  Minimum condition for a photochemical reaction to occur
  Photon must also be absorbed by target molecule
Most photochemical reactions require radiation from the UV part of the spectrum
Some photochemical reactions are initiated by visible light (e.g., photosynthesis, vision, film photography)
Image from: Blatchley III, E.R. (2023) Photochemical Reactors:
Theory, Methods, and Applications of Ultraviolet Radiation,
Wiley, Hoboken, NJ.

## Slide 6
Summary
First and Second Laws of Photochemistry define minimum conditions for a photochemical reaction to occur
  Photons must be absorbed by target
  Photons must have energy that meets or exceeds bond energy
Most photochemical reactions of interest are initiated by UV radiation
Third law of photochemistry indicates that the extent of a (pure) photochemical reaction is governed by the dose of radiation delivered to the target
  Dose is the master variable
  Time required to deliver dose does not affect reaction extent